## Slide 1: King Saud University College of Engineering IE – 462: “Industrial Information Systems” Fall – 2018 (1st Sem. 1439-40H)
Chapter 4:
Structured Analysis and Functional
Architecture Design – p1 – IDEF0 - ii
Prepared by: Ahmed M. El-Sherbeeny, PhD

## Slide 2: Lesson Overview
Modeling IIS – (p1)
Integrated Computer-Aided Manufacturing Definition 0 (IDEF0) – (p1)
Data Flow Diagram (DFD) – (p2)

## Slide 3: Functional Modeling Integrated Computer-Aided Manufacturing Definition 0 (IDEF0) – cont’d

## Slide 4
Top-level view of the enterprise: Node A0
An Integrated IDEF0 Model of an Entire Manufacturing Enterprise
USDA: US Dept. of Agriculture
FDA: Food & Drug Administration
Notes: Q: what is the Saudi equivalent of USDA and FDA? A: Saudi Food and Drug Authority; Saudi Office of Agricultural Affairs

## Slide 5
  A0 — Operate a Food Manufacturing Enterprise
  A1 — Manage Sales and Order Process
  A2 — Plan for Manufacture
  A3 — Manufacture Product
  A4 — Control Finished Goods
Decomposition of Node A0

## Slide 6
Decomposition of Node A0
Notes: Notice how node A3 has been highlighted (in order to emphasize that it will be the focus of the next decomposition)

## Slide 7
  A0 — Operate a Food Manufacturing Enterprise
  A1 — Manage Sales and Order Process
  A2 — Plan for Manufacture
  A3 — Manufacture Product
  A31 — Control Incoming Materials
  A32 — Control Stored Material
  A33 — Control Production Processes
  A4 — Control Finished Goods
Decomposition of Node A3
Notes: Node A3 was taken here as a sample (i.e. could be done also on A1, A2, A4)

## Slide 8
Decomposition of Node A3
Notes: Notice here how node A31 is highlighted

## Slide 9
Concept of tunneling
e.g. output of activity A31, labeled “Material Returned to Vendors”
Note the tunnel on the arrowhead of the arc
A tunnel arrow can represent:
an external arrow that did not appear in the parent diagram (i.e. it has a hidden source) or,
an arrow that goes to another activity but does not appear explicitly on the destination activity (i.e. a hidden destination)
Tunneling is used when it is not convenient to show all I’s, O’s, controls, or mechanisms at every level of the hierarchy
Decomposition of Node A3
Notes: Q: which type of tunnel arrowhead is shown here? (hidden source as it did not appear in the parent diagram (Decomposition of node A0)

## Slide 10
Concept of bundling
e.g. node A2 provides a control for activity node A3 called “production schedule and recipe”
Production schedule: daily schedule for production of a particular product
Recipe includes:
  Steps in the production process
  Materials/ingredients used at each step to make the product, and
  Critical operating parameters of the production line (e.g. temperatures, time settings for cooking and sterilization)
Decomposition of Node A3
Notes: Q: can you mention another example of bundling in the previous diagrams? USDA and FDA requirements

## Slide 11
Production schedule and recipe documents:
  retort processing information
      “retort”: chamber of superheated water for sterilizing packaged food products
  cook sheet
      formula that must be used for each product; includes ingredients and equipment settings
  day production schedule
      which production lines will be used to produce each of the products to be made that day, and order of production (for multiple products)
  material move schedule
      tells forklift truck operator which lots of ingredients to transfer from storage to production
Decomposition of Node A3

## Slide 12
Indication of DB on control documents
  DB: database
  This informs reader that this is information that is derived from some data source (e.g. electronic)
  Note, this notation is not part of the IDEF0 methodology (only added here for convenience)
Decomposition of Node A3

## Slide 13
A0 — Operate a Food Manufacturing Enterprise
A1 — Manage Sales and Order Process
A2 — Plan for Manufacture
A3 — Manufacture Product
A31 — Control Incoming Materials
A311 — Confirm Validity of Shipment
A312 — Inspect condition of materials
A313 — Receive Materials
A32 — Control Stored Material
A33 — Control Production Processes
A4 — Control Finished Goods
Decomposition of Node A31

## Slide 14
Elemental nodes
  Elemental level is the most detailed level of analysis of functions
  We will focus on node A31, Control Incoming Material
  Elemental nodes
    should be prepared with those individuals within the enterprise who are actors in the process
    should give clear conceptual understanding of the processes that are taking place and
    should give information requirements at each stage of the process
    elemental nodes are described in detail in next slides
Decomposition of Node A31

## Slide 15
Decomposition of Node A31

## Slide 16
  Node A311: Confirm validity of shipment
    Try to trace the story/narrative here on the decomposition chart
    First, the shipment arrives
    The receiving clerk (note the mechanism arc) compares,
      paperwork that comes with the shipment (bill of laden) with the
      enterprise’s purchase order (PO)
    If the material in the 2 inputs (BOL and PO) are matching  shipment is accepted
      otherwise, the shipment is refused (return to vendor)
    This procedure is defined as the “material receiving procedure” (by the enterprise management)
Decomposition of Node A31
Notes: Laden: حمولة/شحنة

## Slide 17
  Node A312: Inspect condition of material
    Receiving clerk notifies quality assurance (QA) that material has arrived
     QA personnel examine condition of truck contents (using shipment inspection criteria):
      e.g. broken containers can result in a partial/total rejection of the shipment
    Note, this is not an inspection of the quality of individual materials
      such testing is performed in quality control (QC) lab after the material is stored in the warehouse and before it is used in production
    When quality assurance clears the shipment for acceptance, the receiving clerk is notified
Decomposition of Node A31

## Slide 18
  Node A313: Receive materials
    Record of shipments: on a form called a receiving report
Decomposition of Node A31

## Slide 19
  Node A313: Receive materials (contd.)
    Upon accepting shipment, the receiving clerk:
      shipment is unloaded and made available for storage
      assigns lot numbers to accepted material
      lot numbers are assigned as sequential numbers and obtained by the clerk from a data source (DB)
      clerk also assigns material to storage location based on material location requirements/location availability
      forklift truck operator is informed of the location to which the material should be moved (indicated by the output arrow “Request to Store Raw Materials”)
Decomposition of Node A31
Notes: Note, data requirements for the execution of these functions will be addressed in the next chapter

## Slide 20: Sources
Design of Industrial Information Systems. Thomas Boucher, and Ali Yalcin. Academic Press. First Ed. 2006. Chapter 4.
Some useful videos:
  AI0Win Tutorial - Manage a Coffee Shop (https://youtu.be/kHDNlFclsiY)
  Rework IDEF0 Process Mapping (Free Simulation) https://youtu.be/sqlNNt4m8QA