## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 7
Cloud Computing and Remote Access
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Network+ Guide to Networks 7th Edition
Chapter 7
Cloud Computing and Remote Access

## Slide 2: Objectives
Identify the features and benefits of cloud computing
Explain methods for remotely connecting to a network
Discuss VPNs (virtual private networks) and the protocols they rely on
Understand methods of encryption, such as IPsec, SSL/TLS, SFTP, and SSH, that can secure data in storage and in transit
Notes: Objectives
Identify the features and benefits of cloud computing
Explain methods for remotely connecting to a network
Discuss VPNs (virtual private networks) and the protocols they rely on
Understand methods of encryption, such as IPsec, SSL/TLS, SFTP, and SSH, that can secure data in storage and in transit

## Slide 3: Objectives
Describe how user authentication protocols such as RADIUS, TACACS+, EAP, and Kerberos function
Recognize symptoms of connectivity and security problems commonly encountered with remote connections
Notes: Objectives
Describe how user authentication protocols such as RADIUS, TACACS+, EAP, and Kerberos function
Recognize symptoms of connectivity and security problems commonly encountered with remote connections

## Slide 4: Cloud Computing
Internet is frequently pictured as a cloud
Cloud computing
  Flexible provision of data storage, applications, and services to multiple clients over a network
Cloud computing distinguishing features
  On-demand service
  Elastic services and storage
  Support for multiple platforms
  Resource pooling and consolidation
  Metered service
Notes: Cloud Computing
Internet is frequently pictured as a cloud
Cloud computing
  Flexible provision of data storage, applications, and services to multiple clients over a network
Cloud computing distinguishing features
  On-demand service
  Elastic services and storage
  Support for multiple platforms
  Resource pooling and consolidation
  Metered service

## Slide 5: Cloud Computing
Notes: Cloud Computing

## Slide 6: Cloud Computing
Can provide virtual desktops
  Operating environments hosted virtually
Developers can load any kind of software on the servers and test it form afar
  Cloud services provider can make sure the development servers are secure and regularly backed up
Most cloud service providers use virtualization software to supply multiple platforms to multiple users
Notes: Cloud Computing
Can provide virtual desktops
  Operating environments hosted virtually
Developers can load any kind of software on the servers and test it form afar
  Cloud services provider can make sure the development servers are secure and regularly backed up
Most cloud service providers use virtualization software to supply multiple platforms to multiple users

## Slide 7: Cloud Computing Categories
Cloud computing service models are categorized by the types of services provided:
  IaaS (Infrastructure as a Service)
    Hardware services and network infrastructure devices
  PaaS (Platform as a Service)
    OS, runtime libraries or modules the OS provides to applications, and the hardware on which the OS runs
  SaaS (Software as a Service)
    Applications
  XaaS (Anything as a Service)
    Any combination of functions
Notes: Cloud Computing Categories
Cloud computing service models are categorized by the types of services provided:
  IaaS (Infrastructure as a Service)
    Hardware services and network infrastructure devices
  PaaS (Platform as a Service)
    OS, runtime libraries or modules the OS provides to applications, and the hardware on which the OS runs
  SaaS (Software as a Service)
    Applications
  XaaS (Anything as a Service)
    Any combination of functions

## Slide 8: Deployment Models
Public cloud
  Service provided over public transmission lines
Private cloud
  Service established on an organization’s own servers in its own data center
Community cloud
  Service shared between multiple organizations
Hybrid cloud
  Combination of the other service models into a single deployment
Notes: Deployment Models
Public cloud
  Service provided over public transmission lines
Private cloud
  Service established on an organization’s own servers in its own data center
Community cloud
  Service shared between multiple organizations
Hybrid cloud
  Combination of the other service models into a single deployment

## Slide 9: Remote Access
Remote access
  Service that allows a client to connect with and log on to a server, LAN, or WAN in a different geographical location
Types of remote access:
  Point-to-point over a dedicated line
  Virtual private network (VPN)
  Remote terminal emulation, also called remote virtual computing
Notes: Remote Access
Remote access
  Service that allows a client to connect with and log on to a server, LAN, or WAN in a different geographical location
Types of remote access:
  Point-to-point over a dedicated line
  Virtual private network (VPN)
  Remote terminal emulation, also called remote virtual computing

## Slide 10: Remote Access
Remote access server (RAS)
  Accepts remote connections and grants access to network resources
Two types of remote access servers:
  Dedicated devices
    Example: Cisco’s AS5800
  Software running on a server
    Example: DirectAccess
Notes: Remote Access
Remote access server (RAS)
  Accepts remote connections and grants access to network resources
Two types of remote access servers:
  Dedicated devices
    Example: Cisco’s AS5800
  Software running on a server
    Example: DirectAccess

## Slide 11: Remote Access
Notes: Remote Access

## Slide 12: Remote Access
Notes: Remote Access

## Slide 13: Point-to-Point Remote Access Protocols
SLIP (Serial Line Internet Protocol)
  Earlier and less sophisticated than PPP
  Can only carry IP packets
  Works strictly on serial connections
PPP (Point-to-Point Protocol)
  Can negotiate and establish a connection between two computers
  Can authenticate a client to a remote system
  Can support several types of Network layer protocols
  Can encrypt the transmissions, although PPP encryption is considered weak by today’s standards
Notes: Point-to-Point Remote Access Protocols
SLIP (Serial Line Internet Protocol)
  Earlier and less sophisticated than PPP
  Can only carry IP packets
  Works strictly on serial connections
PPP (Point-to-Point Protocol)
  Can negotiate and establish a connection between two computers
  Can authenticate a client to a remote system
  Can support several types of Network layer protocols
  Can encrypt the transmissions, although PPP encryption is considered weak by today’s standards

## Slide 14: VPNs (Virtual Private Networks)
VPNs
  Virtual networks logically defined for secure communication over public transmission systems
To ensure VPNs can carry all types of data securely
  Special VPN protocols encapsulate higher-layer protocols in a process known as tunneling
VPNs can be classified according to two models:
  Site-to-site VPN
  Client-to-site VPN
    Also called host-to-site VPN or remote-access VPN
Notes: VPNs (Virtual Private Networks)
VPNs
  Virtual networks logically defined for secure communication over public transmission systems
To ensure VPNs can carry all types of data securely
  Special VPN protocols encapsulate higher-layer protocols in a process known as tunneling
VPNs can be classified according to two models:
  Site-to-site VPN
  Client-to-site VPN
    Also called host-to-site VPN or remote-access VPN

## Slide 15: VPNs (Virtual Private Networks)
Notes: VPNs (Virtual Private Networks)

## Slide 16: VPNs (Virtual Private Networks)
Notes: VPNs (Virtual Private Networks)

## Slide 17: VPNs (Virtual Private Networks)
VPN software embedded in the OS
  RRAS (Routing and Remote Access Service) Microsoft’s remote access server software and VPN solution
Third-party solutions
  OpenVIN is open source and is available on a variety of platforms
Implemented by routers or firewalls
  Most common implementation of VPNs on UNIX-based networks
Notes: VPNs (Virtual Private Networks)
VPN software embedded in the OS
  RRAS (Routing and Remote Access Service) Microsoft’s remote access server software and VPN solution
Third-party solutions
  OpenVIN is open source and is available on a variety of platforms
Implemented by routers or firewalls
  Most common implementation of VPNs on UNIX-based networks

## Slide 18: VPNs (Virtual Private Networks)
VPN concentrator
  Specialized device that authenticates VPN clients, establishes tunnels for VPN connections, and manages encryption for VPN transmissions
  Also known as an encryption device
Two primary encryption techniques used by VPNs:
  IPsec
  SSL
Notes: VPNs (Virtual Private Networks)
VPN concentrator
  Specialized device that authenticates VPN clients, establishes tunnels for VPN connections, and manages encryption for VPN transmissions
  Also known as an encryption device
Two primary encryption techniques used by VPNs:
  IPsec
  SSL

## Slide 19: VPNs (Virtual Private Networks)
Notes: VPNs (Virtual Private Networks)

## Slide 20: VPN Tunneling Protocols
VPN tunneling protocols operate at the Data Link layer
  Encapsulate the VPN frame into a Network layer packet
Two VPN tunneling protocols:
  PPTP and L2TP
Notes: VPN Tunneling Protocols
VPN tunneling protocols operate at the Data Link layer
  Encapsulate the VPN frame into a Network layer packet
Two VPN tunneling protocols:
  PPTP and L2TP

## Slide 21: VPN Tunneling Protocols
PPTP (Point-to-Point Tunneling Protocol)
  A Layer 2 protocol that encapsulates PPP data frames so they can traverse the Internet masked as an IP transmission
  Uses TCP segments at the Transport layer
GRE (Generic Routing Encapsulation)
  Used to transmit PPP data frames through the tunnel
  Encapsulates PPP frames to make them take on the temporary identity of IP packets
PPTP is no longer considered secure and L2TP is now recommended
Notes: VPN Tunneling Protocols
PPTP (Point-to-Point Tunneling Protocol)
  A Layer 2 protocol that encapsulates PPP data frames so they can traverse the Internet masked as an IP transmission
  Uses TCP segments at the Transport layer
GRE (Generic Routing Encapsulation)
  Used to transmit PPP data frames through the tunnel
  Encapsulates PPP frames to make them take on the temporary identity of IP packets
PPTP is no longer considered secure and L2TP is now recommended

## Slide 22: VPN Tunneling Protocols
L2TP (Layer 2 Tunneling Protocol)
  Encapsulates PPP data in a similar manner to PPTP
  Can connect a VPN that uses a mix of equipment types
    It is a standard accepted and used by multiple vendors
  Can connect two routers, a router and a RAS, or a client and a RAS
Notes: VPN Tunneling Protocols
L2TP (Layer 2 Tunneling Protocol)
  Encapsulates PPP data in a similar manner to PPTP
  Can connect a VPN that uses a mix of equipment types
    It is a standard accepted and used by multiple vendors
  Can connect two routers, a router and a RAS, or a client and a RAS

## Slide 23: Terminal Emulation or Remote Virtual Computing
Remote virtual computing (terminal emulation)
  Allows a user on one computer to control another computer across a network connection
Examples of command-line software:
  Telnet and SSH
Examples of GUI-based software:
  Remote Desktop for Windows
  join.me
  VNC
  Team Viewer
Notes: Terminal Emulation or Remote Virtual Computing
Remote virtual computing (terminal emulation)
  Allows a user on one computer to control another computer across a network connection
Examples of command-line software:
  Telnet and SSH
Examples of GUI-based software:
  Remote Desktop for Windows
  join.me
  VNC
  Team Viewer

## Slide 24: Encryption Techniques, Protocols, and Utilities
Encryption
  Use of mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher
  Used to keep information private
  Provides the following assurances:
    Confidentiality
    Integrity
    Availability
Notes: Encryption Techniques, Protocols, and Utilities
Encryption
  Use of mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher
  Used to keep information private
  Provides the following assurances:
    Confidentiality
    Integrity
    Availability

## Slide 25: Key Encryption
Key
  Random string of characters
  Woven into original data’s bits
  Generates unique data block
Ciphertext
  Scrambled data block
Brute force attack
  Attempt to discover key
  Trying numerous possible character combinations
Notes: Key Encryption
Key
  Random string of characters
  Woven into original data’s bits
  Generates unique data block
Ciphertext
  Scrambled data block
Brute force attack
  Attempt to discover key
  Trying numerous possible character combinations

## Slide 26: Key Encryption
Private key encryption
  Data encrypted using single key
    Known only by sender and receiver
  Symmetric encryption
    Same key used during both encryption and decryption
Notes: Key Encryption
Private key encryption
  Data encrypted using single key
    Known only by sender and receiver
  Symmetric encryption
    Same key used during both encryption and decryption

## Slide 27: Key Encryption
Notes: Key Encryption

## Slide 28: Key Encryption
Public key encryption
  Data encrypted using two keys
  Private key: user knows
  Public key: anyone may request
Public key server
  Publicly accessible host
  Freely provides users’ public keys
Key pair
  Combination of public key and private key
Asymmetric encryption
  Requires two different keys
Notes: Key Encryption
Public key encryption
  Data encrypted using two keys
  Private key: user knows
  Public key: anyone may request
Public key server
  Publicly accessible host
  Freely provides users’ public keys
Key pair
  Combination of public key and private key
Asymmetric encryption
  Requires two different keys

## Slide 29: Key Encryption
Figure 7-11 Public key encryption begins with the recipient
Notes: Key Encryption

## Slide 30: Key Encryption
Digital certificate
  Holds identification information
  Includes public key
CA (certificate authority)
  Issues, maintains digital certificates
  Example: Verisign
PKI (public key infrastructure)
  Use of certificate authorities to associate public keys with certain users
Notes: Key Encryption
Digital certificate
  Holds identification information
  Includes public key
CA (certificate authority)
  Issues, maintains digital certificates
  Example: Verisign
PKI (public key infrastructure)
  Use of certificate authorities to associate public keys with certain users

## Slide 31: Key Encryption
Notes: Key Encryption

## Slide 32: Key Encryption
Figure 7-13 When the CA that issues a digital certificate is trusted and verified, the Web server’s public key can be trusted
Notes: Key Encryption

## Slide 33: IPsec (Internet Protocol Security)
IPsec
  Encryption protocol that defines rules for encryption, authentication, and key management for TCP/IP transmissions
IPsec creates secure connections in five steps:
  IPsec initiation
  Key management
  Security negotiations
  Data transfer
  Termination
Notes: IPsec (Internet Protocol Security)
IPsec
  Encryption protocol that defines rules for encryption, authentication, and key management for TCP/IP transmissions
IPsec creates secure connections in five steps:
  IPsec initiation
  Key management
  Security negotiations
  Data transfer
  Termination

## Slide 34: SSL (Secure Sockets Layer) and TLS (Transport Layer Security)
Both are methods of encrypting TCP/IP transmissions
  Including Web pages and data entered into Web forms
Both protocols work side by side and are widely known as SSL/TLS or TLS/SSL
SSL session
  Association between client and server
    Defined by agreement
    Specific set of encryption techniques
  Created by SSL handshake protocol
Notes: SSL (Secure Sockets Layer) and TLS (Transport Layer Security)
Both are methods of encrypting TCP/IP transmissions
  Including Web pages and data entered into Web forms
Both protocols work side by side and are widely known as SSL/TLS or TLS/SSL
SSL session
  Association between client and server
    Defined by agreement
    Specific set of encryption techniques
  Created by SSL handshake protocol

## Slide 35: SSL (Secure Sockets Layer) and TLS (Transport Layer Security)
Handshake protocol
  Allows client and server to authenticate
  Similar to a TCP three-way handshake
TTLS (Tunneled Transport Layer Security)
  Provides authentication like SSL/TLS, but does not require a certificate for each user
  Authenticates the server end of the connection by certificate
  Users are authenticated by password only
Notes: SSL (Secure Sockets Layer) and TLS (Transport Layer Security)
Handshake protocol
  Allows client and server to authenticate
  Similar to a TCP three-way handshake
TTLS (Tunneled Transport Layer Security)
  Provides authentication like SSL/TLS, but does not require a certificate for each user
  Authenticates the server end of the connection by certificate
  Users are authenticated by password only

## Slide 36: SSL VPN
SSL VPN
  A VPN configured to support SSL transmissions to and from services running on its protected network
  Typically created and supported by software running on a VPN concentrator
  Access by the user almost exclusively through a Web browser
  For the most secure VPNs, a user must install a personal digital certificate along with SSL VPN software, called a SSL VPN client
Notes: SSL VPN
SSL VPN
  A VPN configured to support SSL transmissions to and from services running on its protected network
  Typically created and supported by software running on a VPN concentrator
  Access by the user almost exclusively through a Web browser
  For the most secure VPNs, a user must install a personal digital certificate along with SSL VPN software, called a SSL VPN client

## Slide 37: SSH (Secure Shell)
SSH is a collection of protocols that provides for secure authentication and encryption
Guards against a number of security threats
  Unauthorized access to a host
  IP spoofing
  Interception of data in transit
  DNS spoofing
Encryption algorithm (depends on version)
  DES, Triple DES, RSA, Kerberos, others
Notes: SSH (Secure Shell)
SSH is a collection of protocols that provides for secure authentication and encryption
Guards against a number of security threats
  Unauthorized access to a host
  IP spoofing
  Interception of data in transit
  DNS spoofing
Encryption algorithm (depends on version)
  DES, Triple DES, RSA, Kerberos, others

## Slide 38: SSH (Secure Shell)
Developed by SSH Communications Security
  Version requires license fee
Open source versions available: OpenSSH
Secure connection requires SSH running on both machines
Requires public and private key generation
Configuration options
  Use one of several encryption types
  Require client password
  Perform port forwarding
Notes: SSH (Secure Shell)
Developed by SSH Communications Security
  Version requires license fee
Open source versions available: OpenSSH
Secure connection requires SSH running on both machines
Requires public and private key generation
Configuration options
  Use one of several encryption types
  Require client password
  Perform port forwarding

## Slide 39: SFTP (Secure File Transfer Protocol)
SFTP
  Secure version of FTP
  Uses SSH for encryption
  Sometimes called FTP over SSH or SSH FTP
  Can be configured to listen on any port
    Normally uses SSH’s port 22
Notes: SFTP (Secure File Transfer Protocol)
SFTP
  Secure version of FTP
  Uses SSH for encryption
  Sometimes called FTP over SSH or SSH FTP
  Can be configured to listen on any port
    Normally uses SSH’s port 22

## Slide 40: Hashes: MD5 and SHA
Hashed data
  Data that has been transformed through a particular algorithm that generally reduces the amount of space needed for the data
  Can only be retrieved by comparing it with known data
    Which receives the same hash function and then produces the same hash output
Notes: Hashes: MD5 and SHA
Hashed data
  Data that has been transformed through a particular algorithm that generally reduces the amount of space needed for the data
  Can only be retrieved by comparing it with known data
    Which receives the same hash function and then produces the same hash output

## Slide 41: Hashes: MD5 and SHA
MD5 (Message Digest 5) Hash
  Uses 128-bit hash values to replace actual data with values computed according to the hash algorithm
  Primary weakness of MD5 is a propensity for collisions
  Still in use, however, it is usually only enabled alongside the more secure SHA hash
Notes: Hashes: MD5 and SHA
MD5 (Message Digest 5) Hash
  Uses 128-bit hash values to replace actual data with values computed according to the hash algorithm
  Primary weakness of MD5 is a propensity for collisions
  Still in use, however, it is usually only enabled alongside the more secure SHA hash

## Slide 42: Hashes: MD5 and SHA
SHA (Secure Hash Algorithm)
  Advantage over MD5 is its resistance to collisions
  SHA-2 supports a variety of hash sizes
    Most popular are SHA-256 (256-bit hash) and SHA-512 (512-bit hash)
  SHA-3 is the most recent iteration of SHA
  Both are often implemented together for increased security
Notes: Hashes: MD5 and SHA
SHA (Secure Hash Algorithm)
  Advantage over MD5 is its resistance to collisions
  SHA-2 supports a variety of hash sizes
    Most popular are SHA-256 (256-bit hash) and SHA-512 (512-bit hash)
  SHA-3 is the most recent iteration of SHA
  Both are often implemented together for increased security

## Slide 43: Authentication Protocols
Authentication
  Process of verifying user’s credentials to grant user access to secured resources
Authentication protocols
  Rules computers follow to accomplish authentication
Several authentication protocol types
  Vary by encryption scheme:
    And steps taken to verify credentials
Notes: Authentication Protocols
Authentication
  Process of verifying user’s credentials to grant user access to secured resources
Authentication protocols
  Rules computers follow to accomplish authentication
Several authentication protocol types
  Vary by encryption scheme:
    And steps taken to verify credentials

## Slide 44: RADIUS and TACACS+
Environments that support many simultaneous connections should use a centralized service
  Often used to manage resource access
AAA (authentication, authorization, and accounting)
  Category of protocols that provide service
  Authenticate a client’s identity
  Authorize a user for certain privileges on a system
  Keep an account of the client’s system or network usage
Notes: RADIUS and TACACS+
Environments that support many simultaneous connections should use a centralized service
  Often used to manage resource access
AAA (authentication, authorization, and accounting)
  Category of protocols that provide service
  Authenticate a client’s identity
  Authorize a user for certain privileges on a system
  Keep an account of the client’s system or network usage

## Slide 45: RADIUS and TACACS+
RADIUS (Remote Authentication Dial-In User Service)
  Defined by the IETF
  Transported over UDP
  Can operate as application on remote access server
    Or on dedicated RADIUS server
  Highly scalable
  May be used to authenticate wireless connections
  Can work in conjunction with other network servers
Notes: RADIUS and TACACS+
RADIUS (Remote Authentication Dial-In User Service)
  Defined by the IETF
  Transported over UDP
  Can operate as application on remote access server
    Or on dedicated RADIUS server
  Highly scalable
  May be used to authenticate wireless connections
  Can work in conjunction with other network servers

## Slide 46: RADIUS and TACACS+
Notes: RADIUS and TACACS+

## Slide 47: RADIUS and TACACS+
TACACS+ (Terminal Access Controller Access Control System Plus)
  Offers option of separating access, authentication, and auditing capabilities
  Differences from RADIUS
    Relies on TCP at the Network layer
    Proprietary protocol developed by Cisco Systems, Inc.
    Typically installed on a router
    Encrypts all information transmitted for AAA
Notes: RADIUS and TACACS+
TACACS+ (Terminal Access Controller Access Control System Plus)
  Offers option of separating access, authentication, and auditing capabilities
  Differences from RADIUS
    Relies on TCP at the Network layer
    Proprietary protocol developed by Cisco Systems, Inc.
    Typically installed on a router
    Encrypts all information transmitted for AAA

## Slide 48: PAP (Password Authentication Protocol)
PPP does not secure connections
  Requires authentication protocols
PAP authentication protocol
  Operates over PPP
  Uses two-step authentication process
  Simple
  Not secure
    Sends client’s credentials in clear text
Notes: PAP (Password Authentication Protocol)
PPP does not secure connections
  Requires authentication protocols
PAP authentication protocol
  Operates over PPP
  Uses two-step authentication process
  Simple
  Not secure
    Sends client’s credentials in clear text

## Slide 49: CHAP and MS-CHAP
CHAP (Challenge Handshake Authentication Protocol)
  Operates over PPP
  Encrypts user names, passwords
  Uses three-way handshake
    Three steps to complete authentication process
Benefit over PAP
  Password never transmitted alone
  Password never transmitted in clear text
Notes: CHAP and MS-CHAP
CHAP (Challenge Handshake Authentication Protocol)
  Operates over PPP
  Encrypts user names, passwords
  Uses three-way handshake
    Three steps to complete authentication process
Benefit over PAP
  Password never transmitted alone
  Password never transmitted in clear text

## Slide 50: CHAP and MS-CHAP
Notes: CHAP and MS-CHAP

## Slide 51: CHAP and MS-CHAP
MS-CHAP (Microsoft Challenge Authentication Protocol)
  Used on Windows-based computers
CHAP, MS-CHAP vulnerability
  Eavesdropping could capture character string encrypted with password, then decrypt
MS-CHAPv2 uses stronger encryption, does not use the same encryption strings, and requires mutual authentication
  Both computers verify the credentials of the other
Notes: CHAP and MS-CHAP
MS-CHAP (Microsoft Challenge Authentication Protocol)
  Used on Windows-based computers
CHAP, MS-CHAP vulnerability
  Eavesdropping could capture character string encrypted with password, then decrypt
MS-CHAPv2 uses stronger encryption, does not use the same encryption strings, and requires mutual authentication
  Both computers verify the credentials of the other

## Slide 52: EAP (Extensible Authentication Protocol)
Another authentication protocol
  Operates over PPP
Works with other encryption and authentication schemes
  Verifies client, server credentials
Requires authenticator to initiate authentication process
  Ask connected computer to verify itself
EAP’s advantages: flexibility, adaptability
Notes: EAP (Extensible Authentication Protocol)
Another authentication protocol
  Operates over PPP
Works with other encryption and authentication schemes
  Verifies client, server credentials
Requires authenticator to initiate authentication process
  Ask connected computer to verify itself
EAP’s advantages: flexibility, adaptability

## Slide 53: 802.1x (EAPoL)
Codified by IEEE
  Specifies use of one of many authentication methods plus EAP
  Grant access to and dynamically generate and update authentication keys for transmissions to a particular port
Primarily used with wireless networks
Originally designed for wired LAN
  EAPoL (EAP over LAN)
Only defines process for authentication
Commonly used with RADIUS authentication
Notes: 802.1x (EAPoL)
Codified by IEEE
  Specifies use of one of many authentication methods plus EAP
  Grant access to and dynamically generate and update authentication keys for transmissions to a particular port
Primarily used with wireless networks
Originally designed for wired LAN
  EAPoL (EAP over LAN)
Only defines process for authentication
Commonly used with RADIUS authentication

## Slide 54: TKIP (Temporary Key Integrity Protocol) and AES (Advanced Encryption System)
TKIP
  Encryption key generation and management scheme
  WPA2 does continue to offer TKIP to provide compatibility with older wireless devices
AES
  Provides faster and more secure encryption than TKIP for wireless transmissions
  Uses a more sophisticated family of ciphers
Notes: TKIP (Temporary Key Integrity Protocol) and AES (Advanced Encryption System)
TKIP
  Encryption key generation and management scheme
  WPA2 does continue to offer TKIP to provide compatibility with older wireless devices
AES
  Provides faster and more secure encryption than TKIP for wireless transmissions
  Uses a more sophisticated family of ciphers

## Slide 55: Kerberos
Cross-platform authentication protocol
Uses key encryption
  Verifies client identity
  Securely exchanges information after client logs on
Private key encryption service
Provides significant security advantages over simple NOS authentication
Notes: Kerberos
Cross-platform authentication protocol
Uses key encryption
  Verifies client identity
  Securely exchanges information after client logs on
Private key encryption service
Provides significant security advantages over simple NOS authentication

## Slide 56: Kerberos
Terms
  KDC (Key Distribution Center)
  AS (authentication service)
  Ticket
  Principal
TGS (Ticket-Granting Service)
  An application running separate from the AS that also runs on the KDC
  Alleviates the need for the client to request a new ticket from the TGS each time it wants to use a different service on the network
Notes: Kerberos
Terms
  KDC (Key Distribution Center)
  AS (authentication service)
  Ticket
  Principal
TGS (Ticket-Granting Service)
  An application running separate from the AS that also runs on the KDC
  Alleviates the need for the client to request a new ticket from the TGS each time it wants to use a different service on the network

## Slide 57: Kerberos
Notes: Kerberos

## Slide 58: SSO (Single Sign-On)
SSO
  Form of authentication in which a client signs on one time to access multiple systems or resources
  Primary advantage is convenience
  Disadvantage is that once authentication is cleared, the user has access to numerous resources
Two-factor authentication
  User must provide something and know something
Multifactor authentication (MFA)
  Process that requires two or more pieces of information
Notes: SSO (Single Sign-On)
SSO
  Form of authentication in which a client signs on one time to access multiple systems or resources
  Primary advantage is convenience
  Disadvantage is that once authentication is cleared, the user has access to numerous resources
Two-factor authentication
  User must provide something and know something
Multifactor authentication (MFA)
  Process that requires two or more pieces of information

## Slide 59: SSO (Single Sign-On)
Three categories of authentication factors:
  Knowledge - something you know, ex: password
  Possession - something you have, ex: ATM card
  Inherence - something you are, ex: your fingerprint
MFA requires at least one authentication method from at least two different categories
Notes: SSO (Single Sign-On)
Three categories of authentication factors:
  Knowledge - something you know, ex: password
  Possession - something you have, ex: ATM card
  Inherence - something you are, ex: your fingerprint
MFA requires at least one authentication method from at least two different categories

## Slide 60: Troubleshooting Cloud Computing and Remote Access
Choosing a secure password
  Easiest and least expensive ways to guard against unauthorized access
Network administrators should:
  Choose difficult passwords
  Keep passwords confidential
  Change them frequently
See page 366 for tips on making and keeping passwords secure
Notes: Troubleshooting Cloud Computing and Remote Access
Choosing a secure password
  Easiest and least expensive ways to guard against unauthorized access
Network administrators should:
  Choose difficult passwords
  Keep passwords confidential
  Change them frequently
See page 360 for tips on making and keeping passwords secure

## Slide 61: Misconfigurations
Common issues to look out for:
  Mistyped username or password
  Incompatible encryption or authentication settings
  Improperly activated or inactivated user account
  Incorrectly assigned port
  Improperly configured firewall
  Network connection failure
  Failed handshake
Check configurations on the server handling AAA services
Notes: Misconfigurations
Common issues to look out for:
  Mistyped username or password
  Incompatible encryption or authentication settings
  Improperly activated or inactivated user account
  Incorrectly assigned port
  Improperly configured firewall
  Network connection failure
  Failed handshake
Check configurations on the server handling AAA services

## Slide 62: Misconfigurations
Make sure server’s date and time are correct
User roles must be properly defined
  User accounts must be properly activated
Check server logs for issues about configuration or individual client access
Use network connection troubleshooting tools to help narrow down the location of a connection problem
  Such as ping and tracert
Notes: Misconfigurations
Make sure server’s date and time are correct
User roles must be properly defined
  User accounts must be properly activated
Check server logs for issues about configuration or individual client access
Use network connection troubleshooting tools to help narrow down the location of a connection problem
  Such as ping and tracert

## Slide 63: Summary
Cloud computing refers to flexible provision of data storage, applications, or services to multiple clients over a network
Cloud services may be managed and delivered by any of a variety of deployment models
A remote client can access files, applications, and other shared resources, such as printers
SLIP is an earlier PPP protocol that does not support encryption, can carry only IP packets, and works strictly on serial connections
Notes: Summary
Cloud computing refers to flexible provision of data storage, applications, or services to multiple clients over a network
Cloud services may be managed and delivered by any of a variety of deployment models
A remote client can access files, applications, and other shared resources, such as printers
SLIP is an earlier PPP protocol that does not support encryption, can carry only IP packets, and works strictly on serial connections

## Slide 64: Summary
A VPN tunneling protocol operates at the Data Link layer to encapsulate the VPN frame into a Network layer packet
GRE encapsulates PPP frames to make them take on the temporary identity of IP packets at Layer 3
Remote virtual computing, also called terminal emulation, allows a user on one computer to control another computer across a network connection
Encryption is the use of a mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher
Notes: Summary
A VPN tunneling protocol operates at the Data Link layer to encapsulate the VPN frame into a Network layer packet
GRE encapsulates PPP frames to make them take on the temporary identity of IP packets at Layer 3
Remote virtual computing, also called terminal emulation, allows a user on one computer to control another computer across a network connection
Encryption is the use of a mathematical code, called a cipher, to scramble data into a format that can be read only by reversing the cipher

## Slide 65: Summary
Private key encryption is also known as symmetric encryption because the same key is used during encryption and decryption of data
In public key encryption, a user’s public key can be obtained from a third-party source, such as a public key server
IPsec is an encryption protocol that works at the Network layer and adds security information to the header of IP packets
Notes: Summary
Private key encryption is also known as symmetric encryption because the same key is used during encryption and decryption of data
In public key encryption, a user’s public key can be obtained from a third-party source, such as a public key server
IPsec is an encryption protocol that works at the Network layer and adds security information to the header of IP packets

## Slide 66: Summary
Authentication protocols vary according to which encryption schemes they rely on
  RADIUS, MS-CHAPv2, EAP, AES, Kerberos are all examples of authentication protocols
Choosing a secure password is one of the easiest and least expensive ways to guard against unauthorized access
When troubleshooting problems with remote connections, be sure to check configurations on the server handling AAA services
Notes: Summary
Authentication protocols vary according to which encryption schemes they rely on
  RADIUS, MS-CHAPv2, EAP, AES, Kerberos are all examples of authentication protocols
Choosing a secure password is one of the easiest and least expensive ways to guard against unauthorized access
When troubleshooting problems with remote connections, be sure to check configurations on the server handling AAA services