## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 10
Network Segmentation and Virtualization
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Network+ Guide to Networks 7th Edition
Chapter 10
Network Segmentation and Virtualization

## Slide 2: Objectives
Describe methods of network design unique to TCP/IP networks, including subnetting, CIDR, and supernetting
Explain virtualization and identify characteristics of virtual network components
Describe techniques for incorporating virtual components in VLANs
Notes: Objectives
Describe methods of network design unique to TCP/IP networks, including subnetting, CIDR, and supernetting
Explain virtualization and identify characteristics of virtual network components
Describe techniques for incorporating virtual components in VLANs

## Slide 3: Objectives
Explain the advanced features of a switch and understand popular switching techniques, including VLAN management
Identify methods of combining VM and VLAN technologies
Notes: Objectives
Explain the advanced features of a switch and understand popular switching techniques, including VLAN management
Identify methods of combining VM and VLAN technologies

## Slide 4: Segmentation and Subnetting
Segmentation
  Dividing a network into multiple smaller networks
  Traffic on one network is separated from another network’s traffic
  Each network is its own broadcast domain
Accomplish the following:
  Enhance security
  Improve performance
  Simplify troubleshooting
Notes: Segmentation and Subnetting
Segmentation
  Dividing a network into multiple smaller networks
  Traffic on one network is separated from another network’s traffic
  Each network is its own broadcast domain
Accomplish the following:
  Enhance security
  Improve performance
  Simplify troubleshooting

## Slide 5: How a Computer Uses a Subnet Mask
IPv4 address is divided into two parts:
  Network ID and host ID
Subnet mask is used so devices can determine which part of an IP address is network ID and which part is the host ID
  Number of 1s in the subnet mask determines the number of bits in the IP address belong to the network ID
Notes: How a Computer Uses a Subnet Mask
IPv4 address is divided into two parts:
  Network ID and host ID
Subnet mask is used so devices can determine which part of an IP address is network ID and which part is the host ID
  Number of 1s in the subnet mask determines the number of bits in the IP address belong to the network ID

## Slide 6: How a Computer Uses a Subnet Mask
Notes: How a Computer Uses a Subnet Mask

## Slide 7: CIDR (Classless Interdomain Routing)
CIDR
  Provides additional ways of arranging network and host information in an IP address
  Takes the network ID or a host’s IP address and follows it with a forward slash (/), followed by the number of bits used for the network ID
192.168.89.127/24
  24 represents the number of 1s in the subnet mask and the number of bits in the network ID
  Known as a CIDR block
Notes: CIDR (Classless Interdomain Routing)
CIDR
  Provides additional ways of arranging network and host information in an IP address
  Takes the network ID or a host’s IP address and follows it with a forward slash (/), followed by the number of bits used for the network ID
192.168.89.127/24
  24 represents the number of 1s in the subnet mask and the number of bits in the network ID
  Known as a CIDR block

## Slide 8: Why Subnets?
Example: A business has grown from 20-30 computers to having a few hundred computers on three floors
  There is only a single LAN or broadcast domain
  One router serves as the default gateway for the entire network
To better manage network traffic, segment the network so that each floor contains one LAN, or broadcast domain
Notes: Why Subnets?
Example: A business has grown from 20-30 computers to having a few hundred computers on three floors
  There is only a single LAN or broadcast domain
  One router serves as the default gateway for the entire network
To better manage network traffic, segment the network so that each floor contains one LAN, or broadcast domain

## Slide 9: Why Subnets?
Notes: Why Subnets?

## Slide 10: Why Subnets?
Notes: Why Subnets?

## Slide 11: Subnet Mask Tables
Class A, Class B, and Class C networks
  Can be subnetted
    Each class has different number of host information bits usable for subnet information
    Varies depending on network class and the way subnetting is used
LAN subnetting
  LAN’s devices interpret device subnetting information
  External routers
    Need network portion of device IP address
Notes: Subnet Mask Tables
Class A, Class B, and Class C networks
  Can be subnetted
    Each class has different number of host information bits usable for subnet information
    Varies depending on network class and the way subnetting is used
LAN subnetting
  LAN’s devices interpret device subnetting information
  External routers
    Need network portion of device IP address

## Slide 12: Subnet Mask Tables
Notes: Subnet Mask Tables

## Slide 13: Subnet Mask Tables
Notes: Subnet Mask Tables

## Slide 14: Subnet Mask Tables
Notes: Subnet Mask Tables

## Slide 15: Subnet Mask Tables
Notes: Subnet Mask Tables

## Slide 16: Supernetting
Supernetting
  Combine contiguous networks that all use the same CIDR block into one supernet
  Also called classless routing or IP address segmentation
Supernetting is helpful for two reasons:
  Reduce the number of routing table entries by combining several entries
  Allow a company to create a single network made up of more than one Class C license
Notes: Supernetting
Supernetting
  Combine contiguous networks that all use the same CIDR block into one supernet
  Also called classless routing or IP address segmentation
Supernetting is helpful for two reasons:
  Reduce the number of routing table entries by combining several entries
  Allow a company to create a single network made up of more than one Class C license

## Slide 17: Supernetting
Supernet is defined by a supernet mask
  Moves the network prefix to the left
Figure 10-6 Subnet mask and supernet mask for a Class C network
Notes: Supernetting
Supernet is defined by a supernet mask
  Moves the network prefix to the left

## Slide 18: Supernetting
Notes: Supernetting

## Slide 19: Subnetting in IPv6
Each ISP can offer customers an entire IPv6 subnet
Subnetting in IPv6
  Simpler than IPv4
  Classes not used
  Subnet masks not used
First four blocks (64 bits) normally identify the network
  Serve as the network prefix or routing prefix
Interfaces that share a network prefix belong to the same subnet
Notes: Subnetting in IPv6
Each ISP can offer customers an entire IPv6 subnet
Subnetting in IPv6
  Simpler than IPv4
  Classes not used
  Subnet masks not used
First four blocks (64 bits) normally identify the network
  Serve as the network prefix or routing prefix
Interfaces that share a network prefix belong to the same subnet

## Slide 20: Subnetting in IPv6
Sometimes the slash notation is called the prefix mask
Route prefixes vary in length
  The slash notation is necessary when defining them
  Example: 2608:FE10::/32
    Includes all subnets whose prefixes begin with 2608:FE10
Notes: Subnetting in IPv6
Sometimes the slash notation is called the prefix mask
Route prefixes vary in length
  The slash notation is necessary when defining them
  Example: 2608:FE10::/32
    Includes all subnets whose prefixes begin with 2608:FE10

## Slide 21: Subnetting in IPv6
Notes: Subnetting in IPv6

## Slide 22: Virtualization
Emulation of a computer, operating system environment, or application:
  On a physical system
Virtual machines (VMs)
  Virtual workstations
  Virtual servers
  Can be configured to use different types of:
    CPU
    Storage drive
    NIC
Notes: Virtualization
Emulation of a computer, operating system environment, or application:
  On a physical system
Virtual machines (VMs)
  Virtual workstations
  Virtual servers
  Can be configured to use different types of:
    CPU
    Storage drive
    NIC

## Slide 23: Virtualization
To users, a VM appears no different from a physical computer:
  Running the same software
Host
  Physical computer
Guest
  Each virtual machine
Hypervisor
  Software that allows you to define and manage virtual machines (also known as a virtual machine manager)
Notes: Virtualization
To users, a VM appears no different from a physical computer:
  Running the same software
Host
  Physical computer
Guest
  Each virtual machine
Hypervisor
  Software that allows you to define and manage virtual machines (also known as a virtual machine manager)

## Slide 24: Virtualization
Figure 10-11 Elements of virtualization
Notes: Virtualization

## Slide 25: Virtualization
Advantages of virtualization
  Efficient use of resources
  Cost and energy savings
  Fault and threat isolation
  Simple backups, recovery, and replication
Disadvantages
  Compromised performance
  Increased complexity
  Increased licensing costs
  Single point of failure
Notes: Virtualization
Advantages of virtualization
  Efficient use of resources
  Cost and energy savings
  Fault and threat isolation
  Simple backups, recovery, and replication
Disadvantages
  Compromised performance
  Increased complexity
  Increased licensing costs
  Single point of failure

## Slide 26: Virtualization
VMware
  Makes the most widely implemented virtualization software
  Provides several which are designed for managing virtual workstations on a single host
Other examples that provide similar functionality but differ in features, interfaces, and ease of use:
  Microsoft’s Hyper-V
  KVM (Kernel-based Virtual Machine)
  Oracle’s VirtualBox
  Citrix’s XenAPP
Notes: Virtualization
VMware
  Makes the most widely implemented virtualization software
  Provides several which are designed for managing virtual workstations on a single host
Other examples that provide similar functionality but differ in features, interfaces, and ease of use:
  Microsoft’s Hyper-V
  KVM (Kernel-based Virtual Machine)
  Oracle’s VirtualBox
  Citrix’s XenAPP

## Slide 27: Virtual Network Components
Virtual network
  Can be created to consist solely of virtual machines on a physical server
Most networks combine physical and virtual elements
Notes: Virtual Network Components
Virtual network
  Can be created to consist solely of virtual machines on a physical server
Most networks combine physical and virtual elements

## Slide 28: Virtual Machines and Network Adapters
Virtualization program
  Assigns VM’s software and hardware characteristics
  Often an easy to use, step-by-step wizard
Network connection
  Requires virtual adapter (vNIC)
  Each VM can have several vNICs
  Upon creation, each vNIC is automatically assigned a MAC address
    Also, by default, every VMs vNIC is connected to a port on a virtual switch
Notes: Virtual Machines and Network Adapters
Virtualization program
  Assigns VM’s software and hardware characteristics
  Often an easy to use, step-by-step wizard
Network connection
  Requires virtual adapter (vNIC)
  Each VM can have several vNICs
  Upon creation, each vNIC is automatically assigned a MAC address
    Also, by default, every VMs vNIC is connected to a port on a virtual switch

## Slide 29: Virtual Machines and Network Adapters
Notes: Virtual Machines and Network Adapters

## Slide 30: Virtual Machines and Network Adapters
Notes: Virtual Machines and Network Adapters

## Slide 31: Virtual Switches and Bridges
When first VM’s vNIC is selected
  Hypervisor creates a connection between that VM and the host
  This connection might be called a bridge or switch
Virtual switch
  Logically defined device
  Operates at Data Link layer
  Passes frames between nodes
The hypervisor controls the virtual switches
VMs can go through a virtual switch to reach network
Notes: Virtual Switches and Bridges
When first VM’s vNIC is selected
  Hypervisor creates a connection between that VM and the host
  This connection might be called a bridge or switch
Virtual switch
  Logically defined device
  Operates at Data Link layer
  Passes frames between nodes
The hypervisor controls the virtual switches
VMs can go through a virtual switch to reach network

## Slide 32: Virtual Switches and Bridges
Notes: Virtual Switches and Bridges

## Slide 33: Virtual Switches and Bridges
Notes: Virtual Switches and Bridges

## Slide 34: Network Connection Types
Must identify networking mode the vNIC will use
Frequently-used network connection types
  Bridged
  NAT
  Host-only
Bridged Mode
  vNIC accesses physical network using host machine’s NIC
  Obtains own IP address, default gateway, and netmask from DHCP server on physical LAN
Notes: Network Connection Types
Must identify networking mode the vNIC will use
Frequently-used network connection types
  Bridged
  NAT
  Host-only
Bridged Mode
  vNIC accesses physical network using host machine’s NIC
  Obtains own IP address, default gateway, and netmask from DHCP server on physical LAN

## Slide 35: Network Connection Types
Notes: Network Connection Types

## Slide 36: Network Connection Types
Notes: Network Connection Types

## Slide 37: Network Connection Types
NAT Mode
  vNIC relies on host to act as NAT device
  Obtains IP addressing information from host
  Virtualization software acts as a DHCP server
  Appropriate for VMs that do not need to be accessed at a known address by other network nodes
Host-only Mode
  VMs on one host can exchange data with each other and the host
  Cannot communicate with nodes beyond the host
  Never receive or transmit data with host’s physical NIC
Notes: Network Connection Types
NAT Mode
  vNIC relies on host to act as NAT device
  Obtains IP addressing information from host
  Virtualization software acts as a DHCP server
  Appropriate for VMs that do not need to be accessed at a known address by other network nodes
Host-only Mode
  VMs on one host can exchange data with each other and the host
  Cannot communicate with nodes beyond the host
  Never receive or transmit data with host’s physical NIC

## Slide 38: Network Connection Types
Notes: Network Connection Types

## Slide 39: Network Connection Types
Notes: Network Connection Types

## Slide 40: Network Connection Types
Notes: Network Connection Types

## Slide 41: Virtual Appliances and Virtual Network Services
Alternative to test servers for new software
Virtual appliance includes:
  Image of operating system, software, hardware specifications, and application configuration
Most commonly virtual servers
Popular functions
  Firewall
  Network management
  E-mail solutions
  Remote access
Notes: Virtual Appliances and Virtual Network Services
Alternative to test servers for new software
Virtual appliance includes:
  Image of operating system, software, hardware specifications, and application configuration
Most commonly virtual servers
Popular functions
  Firewall
  Network management
  E-mail solutions
  Remote access

## Slide 42: VRRP (Virtual Router Redundancy Protocol) and HSRP (Hot Standby Routing Protocol)
VRRP
  Cisco’s proprietary version is HSRP
  Used to assign a virtual IP address to a group of routers
Virtual IP address
  Can be shared by the entire group
  Messages routed to the virtual IP address are handled by the master router
  Routers involved are all physical routers acting together as a single virtual router or a group of virtual routers
Notes: VRRP (Virtual Router Redundancy Protocol) and HSRP (Hot Standby Routing Protocol)
VRRP
  Cisco’s proprietary version is HSRP
  Used to assign a virtual IP address to a group of routers
Virtual IP address
  Can be shared by the entire group
  Messages routed to the virtual IP address are handled by the master router
  Routers involved are all physical routers acting together as a single virtual router or a group of virtual routers

## Slide 43: SDN (Software Defined Networking)
SDN
  The virtualization of network services
    A network controller manages these services instead of services being directly managed by hardware devices
  Network controller integrates all of the network’s virtual and physical devices into one cohesive system
  Protocols handle the process of making decisions (called the control plane)
  Physical devices make actual contact with data transmissions as they traverse the network (called the data plane)
Notes: SDN (Software Defined Networking)
SDN
  The virtualization of network services
    A network controller manages these services instead of services being directly managed by hardware devices
  Network controller integrates all of the network’s virtual and physical devices into one cohesive system
  Protocols handle the process of making decisions (called the control plane)
  Physical devices make actual contact with data transmissions as they traverse the network (called the data plane)

## Slide 44: SDN (Software Defined Networking)
Notes: SDN (Software Defined Networking)

## Slide 45: VLANs and Trunking
VLAN (virtual local area network)
  Groups ports on a switch so that some of the local traffic on the switch is forced to go through a router
To create a VLAN
  You need a programmable physical switch whose ports can be partitioned into groups
Notes: VLANs and Trunking
VLAN (virtual local area network)
  Groups ports on a switch so that some of the local traffic on the switch is forced to go through a router
To create a VLAN
  You need a programmable physical switch whose ports can be partitioned into groups

## Slide 46: VLANs and Trunking
802.1Q
  The IEEE standard that specifies how VLAN information appears in frames and how switches interpret that information
Each VLAN is assigned its own subnet of IP addresses
  Each VLAN and subnet normally is a broadcast domain
A VLAN can include ports from more than one switch
Notes: VLANs and Trunking
802.1Q
  The IEEE standard that specifies how VLAN information appears in frames and how switches interpret that information
Each VLAN is assigned its own subnet of IP addresses
  Each VLAN and subnet normally is a broadcast domain
A VLAN can include ports from more than one switch

## Slide 47: VLANs and Trunking
Notes: VLANs and Trunking

## Slide 48: VLANs and Trunking
Reasons for using VLANs:
  Separating groups of users who need special security or network functions
  Isolating connections with heavy or unpredictable traffic patterns
  Identifying groups of devices whose data should be given priority handling
  Containing groups of devices that rely on legacy protocols incompatible with the majority of the network’s traffic
  Separating a large network into smaller subnets
Notes: VLANs and Trunking
Reasons for using VLANs:
  Separating groups of users who need special security or network functions
  Isolating connections with heavy or unpredictable traffic patterns
  Identifying groups of devices whose data should be given priority handling
  Containing groups of devices that rely on legacy protocols incompatible with the majority of the network’s traffic
  Separating a large network into smaller subnets

## Slide 49: VLANs and Trunking
Trunk
  A single physical connection between switches through which many logical VLANs can transmit and receive data
A port on a switch is configured as either an access port or a trunk port
  Access port - used for connecting a single node
  Trunk port - capable of managing traffic among multiple VLANs
Notes: VLANs and Trunking
Trunk
  A single physical connection between switches through which many logical VLANs can transmit and receive data
A port on a switch is configured as either an access port or a trunk port
  Access port - used for connecting a single node
  Trunk port - capable of managing traffic among multiple VLANs

## Slide 50: VLANs and Trunking
Notes: VLANs and Trunking

## Slide 51: VLANs and Trunking
To keep data belonging to each VLAN separate
  Each frame is identified with a VLAN identifier or tag
  Trunking protocols assign and interpret these tags
Cisco’s VTP (VLAN trunking protocol)
  The most popular protocol for exchanging VLAN information over trunks
  VTP allows changes to VLAN database on one switch, called the stack master, to be communicated to all other switches in the network
Notes: VLANs and Trunking
To keep data belonging to each VLAN separate
  Each frame is identified with a VLAN identifier or tag
  Trunking protocols assign and interpret these tags
Cisco’s VTP (VLAN trunking protocol)
  The most popular protocol for exchanging VLAN information over trunks
  VTP allows changes to VLAN database on one switch, called the stack master, to be communicated to all other switches in the network

## Slide 52: VLANs and Trunking
Potential problem in creating VLANs
  By grouping certain nodes, you are excluding another group
To allow different VLANs to exchange data
  You need to connect VLANs with a router or Layer 3 switch
VLAN hopping attack
  Occurs when an attacker generates transmissions that appear to belong to a protected VLAN
  Prevented by disabling auto trunking and moving native VLAN to an unused VLAN
Notes: VLANs and Trunking
Potential problem in creating VLANs
  By grouping certain nodes, you are excluding another group
To allow different VLANs to exchange data
  You need to connect VLANs with a router or Layer 3 switch
VLAN hopping attack
  Occurs when an attacker generates transmissions that appear to belong to a protected VLAN
  Prevented by disabling auto trunking and moving native VLAN to an unused VLAN

## Slide 53: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
IEEE standard 802.1D
Operates in Data Link layer
Prevents traffic loops
  Calculating paths avoiding potential loops
  Artificially blocking links completing loop
STP information is transmitted between switches
  Via BPDUs (Bridge Protocol Data Units)
BPDU guard
  Help to enforce STP path rules
BPDU filter can be used to disable STP on ports
Notes: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
IEEE standard 802.1D
Operates in Data Link layer
Prevents traffic loops
  Calculating paths avoiding potential loops
  Artificially blocking links completing loop
STP information is transmitted between switches
  Via BPDUs (Bridge Protocol Data Units)
BPDU guard
  Help to enforce STP path rules
BPDU filter can be used to disable STP on ports

## Slide 54: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
Three steps
  Select root bridge based on Bridge ID (BID)
  Examine possible paths between network bridge and root bridge
  Disables links not part of shortest path
Notes: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
Three steps
  Select root bridge based on Bridge ID (BID)
  Examine possible paths between network bridge and root bridge
  Disables links not part of shortest path

## Slide 55: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
Newer versions of STP can detect and correct for link failures in seconds
  RSTP (Rapid Spanning Tree Protocol)
  MSTP (Multiple Spanning Tree Protocol)
TRILL (Transparent Interconnection of Lots of Links)
  Designed to replace STP
  A multipath, link-state protocol
SPB (Shortest Path Bridging)
  A descendent of STP that operates at Layer 3
  Keeps all potential paths active while managing flow of data
Notes: STP (Spanning Tree Protocol) and SPB (Shortest Path Bridging)
Newer versions of STP can detect and correct for link failures in seconds
  RSTP (Rapid Spanning Tree Protocol)
  MSTP (Multiple Spanning Tree Protocol)
TRILL (Transparent Interconnection of Lots of Links)
  Designed to replace STP
  A multipath, link-state protocol
SPB (Shortest Path Bridging)
  A descendent of STP that operates at Layer 3
  Keeps all potential paths active while managing flow of data

## Slide 56: Switch Configurations
Unmanaged switch
  Provides plug-and-play simplicity with minimal configuration
    Has no IP address assigned to it
Managed switch
  Can be configured via a command-line interface and are usually assigned an IP address
  VLANS can only be implemented through managed switches
Notes: Switch Configurations
Unmanaged switch
  Provides plug-and-play simplicity with minimal configuration
    Has no IP address assigned to it
Managed switch
  Can be configured via a command-line interface and are usually assigned an IP address
  VLANS can only be implemented through managed switches

## Slide 57: Switch Configurations
Configuration options on a managed switch:
  Password security
  Console
    Management console
    Remote configuration is managed through a virtual terminal or virtual console
  AAA method
  Switch port security
  Speed and duplex
Notes: Switch Configurations
Configuration options on a managed switch:
  Password security
  Console
    Management console
    Remote configuration is managed through a virtual terminal or virtual console
  AAA method
  Switch port security
  Speed and duplex

## Slide 58: Wireless VLANs
Wireless controller (Wi-Fi controller or WLAN controller)
  Provides a central management console for all of the APs in the network
APs can also provide several options
  Thick AP is self-contained without relying on a higher-level management device
  Thin APs are simple devices that must be configured from the wireless controller’s console
Notes: Wireless VLANs
Wireless controller (Wi-Fi controller or WLAN controller)
  Provides a central management console for all of the APs in the network
APs can also provide several options
  Thick AP is self-contained without relying on a higher-level management device
  Thin APs are simple devices that must be configured from the wireless controller’s console

## Slide 59: Wireless VLANs
LWAPP (Lightweight Access Point Protocol)
  Direct all wireless frames to the controller by adding extra headers to the frames
  CAPWAP (Control and Provisioning of Wireless Access Points) is another example
Wireless controller can provide centralized authentication for wireless clients, load balancing, and channel management
VLAN pooling is accomplished by grouping multiple VLANs into a single VLAN group
Notes: Wireless VLANs
LWAPP (Lightweight Access Point Protocol)
  Direct all wireless frames to the controller by adding extra headers to the frames
  CAPWAP (Control and Provisioning of Wireless Access Points) is another example
Wireless controller can provide centralized authentication for wireless clients, load balancing, and channel management
VLAN pooling is accomplished by grouping multiple VLANs into a single VLAN group

## Slide 60: Troubleshooting VMs and VLANs
Virtual networks resemble physical networks in many ways
  Backups, troubleshooting, and software updates concerns are similar
To add VMs to a VLAN defined on a physical network
  Use the hypervisor to modify a virtual switch’s configuration
  VMs are not added to a preexisting VLAN on the physical switch that manages that VLAN
Notes: Troubleshooting VMs and VLANs
Virtual networks resemble physical networks in many ways
  Backups, troubleshooting, and software updates concerns are similar
To add VMs to a VLAN defined on a physical network
  Use the hypervisor to modify a virtual switch’s configuration
  VMs are not added to a preexisting VLAN on the physical switch that manages that VLAN

## Slide 61: Summary
Separating traffic by subnets or VLANs helps enhance security, improve network performance, and simplify troubleshooting
CIDR notation takes the network ID or a host’s IP address and follows it with a forward slash (/) followed by the number of bits used for network ID
To create a subnet, borrow bits that would represent host information in classful addressing
Supernetting allows you to combine contiguous networks that all use the same CIDR block into one supernet
Notes: Summary
Separating traffic by subnets or VLANs helps enhance security, improve network performance, and simplify troubleshooting
CIDR notation takes the network ID or a host’s IP address and follows it with a forward slash (/) followed by the number of bits used for network ID
To create a subnet, borrow bits that would represent host information in classful addressing
Supernetting allows you to combine contiguous networks that all use the same CIDR block into one supernet

## Slide 62: Summary
Subnetting in IPv6 is simpler than subnetting in IPv4
For a single computer, virtualization can emulate the hardware, OS, and/or applications
When you create a VM, use the virtualization program to assign the VM’s software and hardware characteristics
VMs can communicate with a virtual switch on the host computer to reach the physical network
A vNIC using bridged mode accesses a physical network using the host machine’s NIC
Notes: Summary
Subnetting in IPv6 is simpler than subnetting in IPv4
For a single computer, virtualization can emulate the hardware, OS, and/or applications
When you create a VM, use the virtualization program to assign the VM’s software and hardware characteristics
VMs can communicate with a virtual switch on the host computer to reach the physical network
A vNIC using bridged mode accesses a physical network using the host machine’s NIC

## Slide 63: Summary
A vNIC using NAT mode relies on the host machine to act as a NAT device
In host-only mode, VMs on one host can exchange data with each other and with their host, but cannot communicate with any nodes beyond the host
In software defined networking (SDN), services are delivered by applications that are managed by a network controller
Programmable switches create VLANs by partitioning their ports into groups
Notes: Summary
A vNIC using NAT mode relies on the host machine to act as a NAT device
In host-only mode, VMs on one host can exchange data with each other and with their host, but cannot communicate with any nodes beyond the host
In software defined networking (SDN), services are delivered by applications that are managed by a network controller
Programmable switches create VLANs by partitioning their ports into groups

## Slide 64: Summary
Switches and bridges use STP to help eliminate the possibility of broadcast storms and other loops
An unmanaged switch has minimal configuration and no IP address assigned to it
A large wireless network is often managed by a central wireless controller
Notes: Summary
Switches and bridges use STP to help eliminate the possibility of broadcast storms and other loops
An unmanaged switch has minimal configuration and no IP address assigned to it
A large wireless network is often managed by a central wireless controller