## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 11
Wide Area Networks
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Network+ Guide to Networks 7th Edition
Chapter 11
Wide Area Networks

## Slide 2: Objectives
Identify a variety of uses for WANs
Explain different WAN topologies, including their advantages and disadvantages
Compare the characteristics of WAN technologies, including their switching type, throughput, media, security, and reliability
Describe several WAN transmission and connection methods, including dial-up, ISDN, T-carriers, frame relay, DSL, broadband cable, broadband over power line, ATM, SONET, MPLS, and Metro Ethernet
Notes: Objectives
Identify a variety of uses for WANs
Explain different WAN topologies, including their advantages and disadvantages
Compare the characteristics of WAN technologies, including their switching type, throughput, media, security, and reliability
Describe several WAN transmission and connection methods, including dial-up, ISDN, T-carriers, frame relay, DSL, broadband cable, broadband over power line, ATM, SONET, MPLS, and Metro Ethernet

## Slide 3: Objectives
Describe wireless WAN technologies, including 802.16 (WiMAX), HSPA+, LTE, and satellite communications
Explore common problems with WAN connections and ways to prevent Internet connection problems
Notes: Objectives
Describe wireless WAN technologies, including 802.16 (WiMAX), HSPA+, LTE, and satellite communications
Explore common problems with WAN connections and ways to prevent Internet connection problems

## Slide 4: WAN Essentials
WAN
  Network traversing some distance, connecting LANs
  Transmission methods depend on business needs
WAN and LAN differences
  LANs connect nodes; WANs connect networks
  Layers 1 and 2 access methods, topologies, media
  LAN wiring: privately owned
  WAN wiring: public through NSPs (network service providers)
    Examples: AT&T, Verizon, Charter, and Comcast
Notes: WAN Essentials
WAN
  Network traversing some distance, connecting LANs
  Transmission methods depend on business needs
WAN and LAN differences
  LANs connect nodes; WANs connect networks
  Layers 1 and 2 access methods, topologies, media
  LAN wiring: privately owned
  WAN wiring: public through NSPs (network service providers)
    Examples: AT&T, Verizon, Charter, and Comcast

## Slide 5: WAN Essentials
WAN site
  Individual geographic locations connected by WAN
WAN link
  Connection between one WAN site and another site
Data Terminal Equipment (DTE)
  Customer’s endpoint device on the WAN
  Communicates on the LAN
Data Communications Equipment (DCE)
  Carrier’s endpoint device for the WAN
  Communicates on the WAN
Notes: WAN Essentials
WAN site
  Individual geographic locations connected by WAN
WAN link
  Connection between one WAN site and another site
Data Terminal Equipment (DTE)
  Customer’s endpoint device on the WAN
  Communicates on the LAN
Data Communications Equipment (DCE)
  Carrier’s endpoint device for the WAN
  Communicates on the WAN

## Slide 6: WAN Essentials
Notes: WAN Essentials

## Slide 7: WAN Essentials
Notes: WAN Essentials

## Slide 8: WAN Topologies
WAN topologies differ from LAN topologies
  Distance they must cover
  Larger number of users they serve
  Heavy traffic they often handle
Notes: WAN Topologies
WAN topologies differ from LAN topologies
  Distance they must cover
  Larger number of users they serve
  Heavy traffic they often handle

## Slide 9: Bus Topology
Bus topology WAN
  Each site connects serially to two sites maximum
  Each site depends on every other site to transmit and receive traffic
  Different locations connected to another through point-to-point links
Best use
  Organizations requiring small WAN, dedicated circuits
Drawback
  Not scalable
Notes: Bus Topology
Bus topology WAN
  Each site connects serially to two sites maximum
  Each site depends on every other site to transmit and receive traffic
  Different locations connected to another through point-to-point links
Best use
  Organizations requiring small WAN, dedicated circuits
Drawback
  Not scalable

## Slide 10: Bus Topology
Notes: Bus Topology

## Slide 11: Ring Topology
Ring topology WAN
  Each site connected to two other sites to form a ring pattern
  Connects locations rather than local nodes
  Relies on redundant rings
    Data rerouted upon site failure
  Expansion
    Difficult, expensive
Best use
  Connecting maximum five locations
Notes: Ring Topology
Ring topology WAN
  Each site connected to two other sites to form a ring pattern
  Connects locations rather than local nodes
  Relies on redundant rings
    Data rerouted upon site failure
  Expansion
    Difficult, expensive
Best use
  Connecting maximum five locations

## Slide 12: Ring Topology
Notes: Ring Topology

## Slide 13: Star Topology
Star topology WAN
  Single site acts as a central connection point
  Separate data routes between any two sites
Advantages
  Single connection failure affects one location
  Shorter data paths between any two sites
  Expansion: simple, less costly
Drawback
  Central site failure can bring down entire WAN
Notes: Star Topology
Star topology WAN
  Single site acts as a central connection point
  Separate data routes between any two sites
Advantages
  Single connection failure affects one location
  Shorter data paths between any two sites
  Expansion: simple, less costly
Drawback
  Central site failure can bring down entire WAN

## Slide 14: Star Topology
Notes: Star Topology

## Slide 15: Mesh Topology
Mesh topology WAN
  Incorporates many directly interconnected sites
  Data travels directly from origin to destination
  Routers can redirect data easily, quickly
Most fault-tolerant WAN type
Full-mesh WAN
  Every WAN site directly connected to every other site
  Drawback: cost
Partial-mesh WAN
  Less costly
Notes: Mesh Topology
Mesh topology WAN
  Incorporates many directly interconnected sites
  Data travels directly from origin to destination
  Routers can redirect data easily, quickly
Most fault-tolerant WAN type
Full-mesh WAN
  Every WAN site directly connected to every other site
  Drawback: cost
Partial-mesh WAN
  Less costly

## Slide 16: Mesh Topology
Notes: Mesh Topology

## Slide 17: Tiered Topology
Tiered topology WAN
  Sites connected in star or ring formations
    Interconnected at different levels
  Interconnection points are organized into layers
    Form hierarchical groupings
Flexibility
  Allows many variations, practicality
  Requires careful considerations
    Geography, usage patterns, growth potential
Notes: Tiered Topology
Tiered topology WAN
  Sites connected in star or ring formations
    Interconnected at different levels
  Interconnection points are organized into layers
    Form hierarchical groupings
Flexibility
  Allows many variations, practicality
  Requires careful considerations
    Geography, usage patterns, growth potential

## Slide 18: Tiered Topology
Notes: Tiered Topology

## Slide 19: PSTN (Public Switched Telephone Network)
PSTN (Public Switched Telephone Network)
  Network of lines, carrier equipment providing telephone service
  Also called POTS (plain old telephone service)
  Encompasses entire telephone system
  Originally: analog traffic
  Today: digital data, computer controlled switching
CO (central office)
  Where telephone company terminates lines
  Switches calls between different locations
Notes: PSTN (Public Switched Telephone Network)
PSTN (Public Switched Telephone Network)
  Network of lines, carrier equipment providing telephone service
  Also called POTS (plain old telephone service)
  Encompasses entire telephone system
  Originally: analog traffic
  Today: digital data, computer controlled switching
CO (central office)
  Where telephone company terminates lines
  Switches calls between different locations

## Slide 20: PSTN (Public Switched Telephone Network)
Local loop (last mile)
  Portion connecting residence, business to nearest CO
NIU (network interface unit)
  Termination point at customer’s demarcation point
FTTP (fiber to the premises)
  Use of a fiber-optic cable to connect a home or business
  Example of a digital local loop
Passive optical network (PON)
  Carrier uses fiber-optic cabling to connect with multiple endpoints
Notes: PSTN (Public Switched Telephone Network)
Local loop (last mile)
  Portion connecting residence, business to nearest CO
NIU (network interface unit)
  Termination point at customer’s demarcation point
FTTP (fiber to the premises)
  Use of a fiber-optic cable to connect a home or business
  Example of a digital local loop
Passive optical network (PON)
  Carrier uses fiber-optic cabling to connect with multiple endpoints

## Slide 21: PSTN (Public Switched Telephone Network)
Notes: PSTN (Public Switched Telephone Network)

## Slide 22: PSTN (Public Switched Telephone Network)
OLT (optical line terminal)
  Single endpoint at carrier’s central office in a PON
  Device with multiple optical ports (PON interfaces)
ONU (optical network unit)
  Distributes signals to multiple endpoints using fiber-optic cable
    Or via copper or coax cable
Notes: PSTN (Public Switched Telephone Network)
OLT (optical line terminal)
  Single endpoint at carrier’s central office in a PON
  Device with multiple optical ports (PON interfaces)
ONU (optical network unit)
  Distributes signals to multiple endpoints using fiber-optic cable
    Or via copper or coax cable

## Slide 23: T-Carriers
T-carrier technology includes:
  T1s, fractional T1s, and T3s
T-carrier standards (T-CXR standards)
  Specify a method of signaling
  A physical layer operation
Single channel divided into multiple channels
  Uses TDM (time division multiplexing) over two wire pairs
Medium
  Telephone wire, fiber-optic cable, wireless links
Notes: T-Carriers
T-carrier technology includes:
  T1s, fractional T1s, and T3s
T-carrier standards (T-CXR standards)
  Specify a method of signaling
  A physical layer operation
Single channel divided into multiple channels
  Uses TDM (time division multiplexing) over two wire pairs
Medium
  Telephone wire, fiber-optic cable, wireless links

## Slide 24: Types of T-Carriers
Many available
Notes: Types of T-Carriers
Many available

## Slide 25: Types of T-Carriers
T-carrier speed dependent on signal level
  Physical layer electrical signaling characteristics
  DS0 (digital signal, level 0)
    One data, voice channel
T1 use
  Connects branch offices, connects to carrier
  Connects telephone company COs, ISPs
T3 use
  Data-intensive businesses
Notes: Types of T-Carriers
T-carrier speed dependent on signal level
  Physical layer electrical signaling characteristics
  DS0 (digital signal, level 0)
    One data, voice channel
T1 use
  Connects branch offices, connects to carrier
  Connects telephone company COs, ISPs
T3 use
  Data-intensive businesses

## Slide 26: Types of T-Carriers
T3 provides 28 times more throughput (expensive)
  Multiple T1’s may accommodate needs
TI costs vary by region
Fractional T1 lease
  Use some T1 channels, charged accordingly
  Best suited to businesses that expect traffic to grow but cannot currently justify leasing a full T-1
Notes: Types of T-Carriers
T3 provides 28 times more throughput (expensive)
  Multiple T1’s may accommodate needs
TI costs vary by region
Fractional T1 lease
  Use some T1 channels, charged accordingly
  Best suited to businesses that expect traffic to grow but cannot currently justify leasing a full T-1

## Slide 27: T-Carrier Connectivity
T-carrier line requires connectivity hardware
  At customer site and switching facility
  Purchased or leased
  Cannot be used with other WAN transmission methods
T-carrier line requires different media
  Throughput dependent
Notes: T-Carrier Connectivity
T-carrier line requires connectivity hardware
  At customer site and switching facility
  Purchased or leased
  Cannot be used with other WAN transmission methods
T-carrier line requires different media
  Throughput dependent

## Slide 28: T-Carrier Connectivity
Wiring
  Plain telephone wire
    UTP or STP copper wiring
    STP preferred for clean connection
  Coaxial cable, microwave, fiber-optic cable
  T1s using STP require repeater every 6000 feet
  Multiple T1s or T3
    Fiber-optic cabling is preferred
Notes: T-Carrier Connectivity
Wiring
  Plain telephone wire
    UTP or STP copper wiring
    STP preferred for clean connection
  Coaxial cable, microwave, fiber-optic cable
  T1s using STP require repeater every 6000 feet
  Multiple T1s or T3
    Fiber-optic cabling is preferred

## Slide 29: T-Carrier Connectivity
When copper cabling is used to carry T-1 traffic
  It terminates in an RJ-48 connector
Notes: T-Carrier Connectivity
When copper cabling is used to carry T-1 traffic
  It terminates in an RJ-48 connector

## Slide 30: T-Carrier Connectivity
A T-1 crossover cable could be used to connect two connectivity devices
  Such as CSUs/DSUs or WAN interface cards (WICs)
Notes: T-Carrier Connectivity
A T-1 crossover cable could be used to connect two connectivity devices
  Such as CSUs/DSUs or WAN interface cards (WICs)

## Slide 31: T-Carrier Connectivity
At the customer’s demarc (demarcation point)
  RJ-48 connectors terminate in a smart jack
Notes: T-Carrier Connectivity
At the customer’s demarc (demarcation point)
  RJ-48 connectors terminate in a smart jack

## Slide 32: T-Carrier Connectivity
CSU/DSU (Channel Service Unit/Data Service Unit)
  Two separate devices
  Combined into single stand-alone device
    Or an interface card
  T1 line connection point
Notes: T-Carrier Connectivity
CSU/DSU (Channel Service Unit/Data Service Unit)
  Two separate devices
  Combined into single stand-alone device
    Or an interface card
  T1 line connection point

## Slide 33: T-Carrier Connectivity
Incoming T-carrier line
  Multiplexer separates combined channels
Outgoing T-carrier line
  Multiplexer combines multiple LAN signals
Notes: T-Carrier Connectivity
Incoming T-carrier line
  Multiplexer separates combined channels
Outgoing T-carrier line
  Multiplexer combines multiple LAN signals

## Slide 34: T-Carrier Connectivity
Terminal equipment
  The DTE is typically a router
    Accepts incoming CSU/DSU signals
    Translates Network layer protocols
    Directs data to destination
Notes: T-Carrier Connectivity
Terminal equipment
  The DTE is typically a router
    Accepts incoming CSU/DSU signals
    Translates Network layer protocols
    Directs data to destination

## Slide 35: T-Carrier Connectivity
Notes: T-Carrier Connectivity

## Slide 36: Frame Relay
Frame relay
  Group of Layer 2 protocols originally designed as a fast packet-switched network over ISDN
  Today is used as the Data Link protocol for various circuit interfaces and media
Data-link connection identifier (DLCI)
  Identifier routers read to determine which circuit to use for the frame
Frame relay is a connection-oriented protocol
Notes: Frame Relay
Frame relay
  Group of Layer 2 protocols originally designed as a fast packet-switched network over ISDN
  Today is used as the Data Link protocol for various circuit interfaces and media
Data-link connection identifier (DLCI)
  Identifier routers read to determine which circuit to use for the frame
Frame relay is a connection-oriented protocol

## Slide 37: Frame Relay
Supports two types of virtual circuits:
  SVC (switched virtual circuit)
    Connections established when parties need to transmit, then terminated after transmission is complete
  PVC (permanent virtual circuit)
    Connections established before data needs to be transmitted and are maintained after transmission
Advantage
  Pay for only the amount of bandwidth required
  Less expensive than other WAN technologies
Notes: Frame Relay
Supports two types of virtual circuits:
  SVC (switched virtual circuit)
    Connections established when parties need to transmit, then terminated after transmission is complete
  PVC (permanent virtual circuit)
    Connections established before data needs to be transmitted and are maintained after transmission
Advantage
  Pay for only the amount of bandwidth required
  Less expensive than other WAN technologies

## Slide 38: DSL (Digital Subscriber Line)
Operates over PSTN
Directly competes with T-1 and broadband cable
Requires repeaters for longer distances
  Best suited for WAN local loop
Supports multiple data, voice channels
  Over a single line
Uses advanced data modulation techniques
  Data signal alters carrier signal properties
  Amplitude or phase modulation
Notes: DSL (Digital Subscriber Line)
Operates over PSTN
Directly competes with T-1 and broadband cable
Requires repeaters for longer distances
  Best suited for WAN local loop
Supports multiple data, voice channels
  Over a single line
Uses advanced data modulation techniques
  Data signal alters carrier signal properties
  Amplitude or phase modulation

## Slide 39: Types of DSL
xDSL refers to all DSL varieties
  ADSL, G.Lite, HDSL, SDSL, VDSL, SHDSL
Symmetrical vs. Asymmetrical
  Downstream
    Data travels from carrier’s switching facility to customer
  Upstream
    Data travels from customer to carrier’s switching facility
Notes: Types of DSL
xDSL refers to all DSL varieties
  ADSL, G.Lite, HDSL, SDSL, VDSL, SHDSL
Symmetrical vs. Asymmetrical
  Downstream
    Data travels from carrier’s switching facility to customer
  Upstream
    Data travels from customer to carrier’s switching facility

## Slide 40: Types of DSL
Symmetrical vs. Asymmetrical (cont’d)
  Asymmetrical
    More throughput in one direction
    Downstream throughput higher than upstream throughput
    Best use: video conferencing, web surfing
  Symmetrical
    Equal capacity for upstream, downstream data
    Examples: HDSL, SDSL, SHDSL
    Best use: uploading, downloading significant data amounts
Notes: Types of DSL
Symmetrical vs. Asymmetrical (cont’d)
  Asymmetrical
    More throughput in one direction
    Downstream throughput higher than upstream throughput
    Best use: video conferencing, web surfing
  Symmetrical
    Equal capacity for upstream, downstream data
    Examples: HDSL, SDSL, SHDSL
    Best use: uploading, downloading significant data amounts

## Slide 41: Types of DSL
Modulation
  Some create multiple narrow channels in the higher frequency range
    A splitter must be installed at the carrier and at the customer’s premises to separate data from voice
  Some require the use of a filter to prevent high-frequency DSL signals from reaching the telephone
  Other types of DSL cannot use the same wire pair used for voice signals
    Use the extra pair of wires contained in the telephone cable
Notes: Types of DSL
Modulation
  Some create multiple narrow channels in the higher frequency range
    A splitter must be installed at the carrier and at the customer’s premises to separate data from voice
  Some require the use of a filter to prevent high-frequency DSL signals from reaching the telephone
  Other types of DSL cannot use the same wire pair used for voice signals
    Use the extra pair of wires contained in the telephone cable

## Slide 42: Types of DSL
Capacity and Maximum Line Length
  Varies in terms of capacity and maximum line length
  VDSL carries as much as 52 Mbps can extend only a maximum of 1000 feet
  Most popular form of DSL is ADSL
    Latest version is ADSL2+M
    Provides maximum throughput of 24 Mbps downstream and 3.3 Mbps upstream
Notes: Types of DSL
Capacity and Maximum Line Length
  Varies in terms of capacity and maximum line length
  VDSL carries as much as 52 Mbps can extend only a maximum of 1000 feet
  Most popular form of DSL is ADSL
    Latest version is ADSL2+M
    Provides maximum throughput of 24 Mbps downstream and 3.3 Mbps upstream

## Slide 43: DSL Connectivity
ADSL: common example on home computer
  Establish TCP connection
  Transmit through DSL modem
    Internal or external
    Splitter separates incoming voice, data signals
    May connect to switch or router
Notes: DSL Connectivity
ADSL: common example on home computer
  Establish TCP connection
  Transmit through DSL modem
    Internal or external
    Splitter separates incoming voice, data signals
    May connect to switch or router

## Slide 44: DSL Connectivity
ADSL (cont’d.)
  DSL modem forwards modulated signal to local loop
    Signal continues over four-pair UTP wire
    Distance less than 18,000 feet: signal combined with other modulated signals in telephone switch
  Carrier’s remote switching facility
    Splitter separates data signal from voice signals
    Request sent to DSLAM (DSL access multiplexer)
    Request issued from carrier’s network to Internet backbone
Notes: DSL Connectivity
ADSL (cont’d.)
  DSL modem forwards modulated signal to local loop
    Signal continues over four-pair UTP wire
    Distance less than 18,000 feet: signal combined with other modulated signals in telephone switch
  Carrier’s remote switching facility
    Splitter separates data signal from voice signals
    Request sent to DSLAM (DSL access multiplexer)
    Request issued from carrier’s network to Internet backbone

## Slide 45: DSL Connectivity
Notes: DSL Connectivity

## Slide 46: Broadband Cable
Cable companies connectivity option
Based on coaxial cable wiring used for TV signals
  Theoretical transmission speeds
    100 Mbps downstream; 20 Mbps upstream
  Real transmission
    10 Mbps downstream; 3 Mbps upstream
    Transmission limited ( throttled)
    Shared physical connections
Best uses
  Web surfing or network data download
Notes: Broadband Cable
Cable companies connectivity option
Based on coaxial cable wiring used for TV signals
  Theoretical transmission speeds
    100 Mbps downstream; 20 Mbps upstream
  Real transmission
    10 Mbps downstream; 3 Mbps upstream
    Transmission limited ( throttled)
    Shared physical connections
Best uses
  Web surfing or network data download

## Slide 47: Broadband Cable
Cable modem
  Modulates, demodulates transmission, reception signals via cable wiring
  Operates at Physical and Data Link layer
  May connect to connectivity device
Notes: Broadband Cable
Cable modem
  Modulates, demodulates transmission, reception signals via cable wiring
  Operates at Physical and Data Link layer
  May connect to connectivity device

## Slide 48: Broadband Cable
Infrastructure required
  HFC (hybrid fiber-coax)
    Expensive fiber-optic link supporting high frequencies
    Connects cable company’s offices to node
  Cable drop
    Connects node to customer’s business or residence
    Fiber-optic or coaxial cable
    Connects to head end
Provides dedicated connection
Many subscribers share same local line, throughput
Notes: Broadband Cable
Infrastructure required
  HFC (hybrid fiber-coax)
    Expensive fiber-optic link supporting high frequencies
    Connects cable company’s offices to node
  Cable drop
    Connects node to customer’s business or residence
    Fiber-optic or coaxial cable
    Connects to head end
Provides dedicated connection
Many subscribers share same local line, throughput

## Slide 49: ATM (Asynchronous Transfer Mode)
Functions at the Data Link layer
Asynchronous communications method
  Nodes do not conform to predetermined schemes
    Specifying data transmissions timing
  Each character transmitted
    Start and stop bits
Specifies Data Link layer framing techniques
Fixed packet size
  Packet (cell)
    48 data bytes plus 5-byte header
Notes: ATM (Asynchronous Transfer Mode)
Functions at the Data Link layer
Asynchronous communications method
  Nodes do not conform to predetermined schemes
    Specifying data transmissions timing
  Each character transmitted
    Start and stop bits
Specifies Data Link layer framing techniques
Fixed packet size
  Packet (cell)
    48 data bytes plus 5-byte header

## Slide 50: ATM (Asynchronous Transfer Mode)
Smaller packet size requires more overhead
  Decrease potential throughput
  Cell efficiency compensates for loss
ATM relies on virtual circuits
  ATM considered packet-switching technology
  Virtual circuits provide circuit switching advantage
  Reliable connection
Allows specific QoS (quality of service) guarantee
  Important for time-sensitive applications
Notes: ATM (Asynchronous Transfer Mode)
Smaller packet size requires more overhead
  Decrease potential throughput
  Cell efficiency compensates for loss
ATM relies on virtual circuits
  ATM considered packet-switching technology
  Virtual circuits provide circuit switching advantage
  Reliable connection
Allows specific QoS (quality of service) guarantee
  Important for time-sensitive applications

## Slide 51: ATM (Asynchronous Transfer Mode)
Notes: ATM (Asynchronous Transfer Mode)

## Slide 52: ATM (Asynchronous Transfer Mode)
Compatibility
  Other leading network technologies
  Cells support multiple higher-layer protocol
  LANE (LAN Emulation)
    Allows integration with Ethernet, token ring network
    Encapsulates incoming Ethernet or token ring frames
    Converts to ATM cells for transmission
Throughput: 25 Mbps to 622 Mbps
Cost: relatively expensive
Notes: ATM (Asynchronous Transfer Mode)
Compatibility
  Other leading network technologies
  Cells support multiple higher-layer protocol
  LANE (LAN Emulation)
    Allows integration with Ethernet, token ring network
    Encapsulates incoming Ethernet or token ring frames
    Converts to ATM cells for transmission
Throughput: 25 Mbps to 622 Mbps
Cost: relatively expensive

## Slide 53: SONET (Synchronous Optical Network)
Key strengths
  WAN technology interoperability
  Fast data transfer rates
  Simple link additions, removals
  High degree of fault tolerance (self-healing)
Synchronous
  Data transmitted and received by nodes must conform to timing scheme
Internationally, SONET is known as SDH (Synchronous Digital Hierarchy)
Notes: SONET (Synchronous Optical Network)
Key strengths
  WAN technology interoperability
  Fast data transfer rates
  Simple link additions, removals
  High degree of fault tolerance (self-healing)
Synchronous
  Data transmitted and received by nodes must conform to timing scheme
Internationally, SONET is known as SDH (Synchronous Digital Hierarchy)

## Slide 54: SONET (Synchronous Optical Network)
SONET ring
  Begins, ends at telecommunications carrier’s facility
  Connects organization’s multiple WAN sites in ring fashion
  Connect with multiple carrier facilities
    Additional fault tolerance
  Terminates at multiplexer
    Easy SONET ring connection additions, removals
Data rate of a particular SONET ring is indicated by its OC (Optical Carrier) level
Notes: SONET (Synchronous Optical Network)
SONET ring
  Begins, ends at telecommunications carrier’s facility
  Connects organization’s multiple WAN sites in ring fashion
  Connect with multiple carrier facilities
    Additional fault tolerance
  Terminates at multiplexer
    Easy SONET ring connection additions, removals
Data rate of a particular SONET ring is indicated by its OC (Optical Carrier) level

## Slide 55: SONET (Synchronous Optical Network)
Notes: SONET (Synchronous Optical Network)

## Slide 56: SONET (Synchronous Optical Network)
Notes: SONET (Synchronous Optical Network)

## Slide 57: MPLS (Multiprotocol Label Switching)
MPLS
  Extremely fast
  Can handle various types of payloads
  Often used by ISPs on their own networks for moving traffic from one customer site to another
  Becoming the solution of choice for many enterprises to connect their branch offices
Notes: MPLS (Multiprotocol Label Switching)
MPLS
  Extremely fast
  Can handle various types of payloads
  Often used by ISPs on their own networks for moving traffic from one customer site to another
  Becoming the solution of choice for many enterprises to connect their branch offices

## Slide 58: Metro Ethernet
Metro Ethernet Forum (MEF)
  An alliance of over 220 industry organizations worldwide
  Developing ways to send Ethernet traffic across MAN and WAN connections
Carrier-Ethernet Transport (CET)
  An Ethernet-based transport solution designed to overcome weaknesses of implementing Ethernet outside the LAN environment
Notes: Metro Ethernet
Metro Ethernet Forum (MEF)
  An alliance of over 220 industry organizations worldwide
  Developing ways to send Ethernet traffic across MAN and WAN connections
Carrier-Ethernet Transport (CET)
  An Ethernet-based transport solution designed to overcome weaknesses of implementing Ethernet outside the LAN environment

## Slide 59: Metro Ethernet
Notes: Metro Ethernet

## Slide 60: Metro Ethernet
Metro Ethernet advantages:
  Streamlined connections
  Cost efficiency
  Scalability
  Familiarity
  Hardware
Notes: Metro Ethernet
Metro Ethernet advantages:
  Streamlined connections
  Cost efficiency
  Scalability
  Familiarity
  Hardware

## Slide 61: Wireless WANs
Wireless broadband
  Specifically designed for:
    High-throughput; long-distance digital data exchange
On wireless WANs
  Downstream data transmission is typically faster than upstream transmission
    Downstream may also be called downlink
  Upstream (uplink) refers to the connection between a client’s transceiver and the carrier’s antenna
Notes: Wireless WANs
Wireless broadband
  Specifically designed for:
    High-throughput; long-distance digital data exchange
On wireless WANs
  Downstream data transmission is typically faster than upstream transmission
    Downstream may also be called downlink
  Upstream (uplink) refers to the connection between a client’s transceiver and the carrier’s antenna

## Slide 62: 802.16 (WiMAX)
WiMAX (Worldwide Interoperability for Microwave Access)
  Line-of-sight transmission between two antennas for use with fixed clients
  Use of frequencies in the 2-to-11 or 11-to-66 GHz range
    Licensed or nonlicensed frequencies
  Use of MIMO
  Ability to transmit and receive signals up to 30 miles
    With fixed antennas
  QoS provisions
Notes: 802.16 (WiMAX)
WiMAX (Worldwide Interoperability for Microwave Access)
  Line-of-sight transmission between two antennas for use with fixed clients
  Use of frequencies in the 2-to-11 or 11-to-66 GHz range
    Licensed or nonlicensed frequencies
  Use of MIMO
  Ability to transmit and receive signals up to 30 miles
    With fixed antennas
  QoS provisions

## Slide 63: 802.16 (WiMAX)
WiMAX
  Offers installation savings and benefits over other broadband services
  Well suited to rural customers
  Provides network access for mobile devices
  Can act as the backhaul link
    An intermediate connection between subscriber networks and a telecommunications carrier’s network
Notes: 802.16 (WiMAX)
WiMAX
  Offers installation savings and benefits over other broadband services
  Well suited to rural customers
  Provides network access for mobile devices
  Can act as the backhaul link
    An intermediate connection between subscriber networks and a telecommunications carrier’s network

## Slide 64: 802.16 (WiMAX)
Notes: 802.16 (WiMAX)

## Slide 65: 802.16 (WiMAX)
Newer version of WiMAX, known as WiMAX Release 2 (WiMAX 2)
  Based on the 802.16m standard
  Positioned to compete favorably with cellular data services
  Backward compatible with 802.16e equipment
Notes: 802.16 (WiMAX)
Newer version of WiMAX, known as WiMAX Release 2 (WiMAX 2)
  Based on the 802.16m standard
  Positioned to compete favorably with cellular data services
  Backward compatible with 802.16e equipment

## Slide 66: Cellular
Initially designed for analog phone service
  Today it can deliver data and voice
Cellular technology generations
  1G: analog
  2G: digital transmission up to 240Kbps
  3G: data rates up to 384Kbps
    Data communications use packet switching
  4G: all-IP, packet switched network for data and voice
    Specifies throughputs of 100 Mbps for fast-moving clients; 1 Gbps for slow-moving clients
Notes: Cellular
Initially designed for analog phone service
  Today it can deliver data and voice
Cellular technology generations
  1G: analog
  2G: digital transmission up to 240Kbps
  3G: data rates up to 384Kbps
    Data communications use packet switching
  4G: all-IP, packet switched network for data and voice
    Specifies throughputs of 100 Mbps for fast-moving clients; 1 Gbps for slow-moving clients

## Slide 67: Cellular
Use one of two competing voice technologies:
  GSM (Global System for Mobile Communications)
  CDMA (Code Division Multiple Access)
Network infrastructure
  Cells served by antenna and base station
  Controller assigns mobile clients frequencies
Cell size depends on:
  Network’s access method
  Region’s topology, population, and amount of cellular traffic
Notes: Cellular
Use one of two competing voice technologies:
  GSM (Global System for Mobile Communications)
  CDMA (Code Division Multiple Access)
Network infrastructure
  Cells served by antenna and base station
  Controller assigns mobile clients frequencies
Cell size depends on:
  Network’s access method
  Region’s topology, population, and amount of cellular traffic

## Slide 68: Cellular
MSC (Mobile switching center)
  Also called an MTSO
Each base station is connected to an MSC by a wireless link or fiber-optic cabling (see Figure 11-33)
Basic infrastructure
  HSPA+ (High Speed Packet Access Plus)
    3G technology
  LTE (Long Term Evolution)
    4G technology
Notes: Cellular
MSC (Mobile switching center)
  Also called an MTSO
Each base station is connected to an MSC by a wireless link or fiber-optic cabling (see Figure 11-33)
Basic infrastructure
  HSPA+ (High Speed Packet Access Plus)
    3G technology
  LTE (Long Term Evolution)
    4G technology

## Slide 69: Cellular
Figure 11-33 Cellular network
Notes: Cellular

## Slide 70: Satellite
Used to deliver:
  Digital television and radio signals
  Voice and video signals
  Cellular and paging signals
  Data services to mobile clients in remote locations
Satellite Orbits
  Geosynchronous Earth orbit (GEO)
    Satellites orbit at same rate Earth turns
    Most popular
Notes: Satellite
Used to deliver:
  Digital television and radio signals
  Voice and video signals
  Cellular and paging signals
  Data services to mobile clients in remote locations
Satellite Orbits
  Geosynchronous Earth orbit (GEO)
    Satellites orbit at same rate Earth turns
    Most popular

## Slide 71: Satellite
Satellite Orbits (cont’d)
  Downlink
    Satellite transponder transmits signal to Earth-based receiver
  Typical satellite
    24 to 32 transponders
    Unique downlink frequencies
  Frequencies, as well as satellite’s orbit location are assigned and regulated by the FCC
Notes: Satellite
Satellite Orbits (cont’d)
  Downlink
    Satellite transponder transmits signal to Earth-based receiver
  Typical satellite
    24 to 32 transponders
    Unique downlink frequencies
  Frequencies, as well as satellite’s orbit location are assigned and regulated by the FCC

## Slide 72: Satellite
Notes: Satellite

## Slide 73: Satellite
Satellite frequency bands
  L-band—1.5–2.7 GHz
  S-band—2.7–3.5 GHz
  C-band—3.4–6.7 GHz
  Ku-band (K-under band) —12–18 GHz
  K-band—18–27 GHz
  Ka-band (K-above band)—18–40 GHz
Within each band
  Frequencies used for uplink and downlink transmissions differ
Notes: Satellite
Satellite frequency bands
  L-band—1.5–2.7 GHz
  S-band—2.7–3.5 GHz
  C-band—3.4–6.7 GHz
  Ku-band (K-under band) —12–18 GHz
  K-band—18–27 GHz
  Ka-band (K-above band)—18–40 GHz
Within each band
  Frequencies used for uplink and downlink transmissions differ

## Slide 74: Satellite
Satellite Internet Services
  Subscriber uses small satellite dish antenna, receiver
  Exchanges signals with provider’s satellite network
  Typically asymmetrical
  Bandwidth shared among many subscribers
  Throughput controlled by service provider
  Slower, more latency than other wireless WAN options
  Client equipment is more expensive than that required by WiMAX, HSPA+, or LTE
Notes: Satellite
Satellite Internet Services
  Subscriber uses small satellite dish antenna, receiver
  Exchanges signals with provider’s satellite network
  Typically asymmetrical
  Bandwidth shared among many subscribers
  Throughput controlled by service provider
  Slower, more latency than other wireless WAN options
  Client equipment is more expensive than that required by WiMAX, HSPA+, or LTE

## Slide 75: Troubleshooting WAN Issues
There are steps to take when troubleshooting a problem with a WAN connection
  Before calling your ISP
Preventative measures can be implemented to avoid having the problem in the first place
Notes: Troubleshooting WAN Issues
There are steps to take when troubleshooting a problem with a WAN connection
  Before calling your ISP
Preventative measures can be implemented to avoid having the problem in the first place

## Slide 76: Company Policies
Consider incorporating the following into your company’s security policy:
  Fair access and utilization limits
  Throttling
  Blocking
Notes: Company Policies
Consider incorporating the following into your company’s security policy:
  Fair access and utilization limits
  Throttling
  Blocking

## Slide 77: Common ISP Problems
Need to know the difference between ISP’s equipment and equipment that belongs to the subscriber
  Equipment located at the customer’s premises, regardless of who owns it and who is responsible, is called customer premise equipment (CPE)
Equipment belonging to the ISP should only be serviced by the ISP’s technicians
  Even if located on the customer’s side of demarc
Notes: Common ISP Problems
Need to know the difference between ISP’s equipment and equipment that belongs to the subscriber
  Equipment located at the customer’s premises, regardless of who owns it and who is responsible, is called customer premise equipment (CPE)
Equipment belonging to the ISP should only be serviced by the ISP’s technicians
  Even if located on the customer’s side of demarc

## Slide 78: Common ISP Problems
Devices commonly found at or near the demarc:
  NIU
  Line drivers
  CSU/DSU
Common issues to look for:
  Interface error
  Routing loops
  Router misconfiguration
  DNS issues
  Interference
Notes: Common ISP Problems
Devices commonly found at or near the demarc:
  NIU
  Line drivers
  CSU/DSU
Common issues to look for:
  Interface error
  Routing loops
  Router misconfiguration
  DNS issues
  Interference

## Slide 79: Summary
Not all businesses need the same kind of WAN
A WAN in which each site is directly connected to no more than two other sites is known as a bus topology WAN
In a ring topology WAN, each site is connected to two other sites to form a ring patter
In a star topology WAN, a single site acts as the central connection point for several other points
A mesh topology WAN incorporates many directly interconnected sites
Notes: Summary
Not all businesses need the same kind of WAN
A WAN in which each site is directly connected to no more than two other sites is known as a bus topology WAN
In a ring topology WAN, each site is connected to two other sites to form a ring patter
In a star topology WAN, a single site acts as the central connection point for several other points
A mesh topology WAN incorporates many directly interconnected sites

## Slide 80: Summary
ISDN is a legacy technology that is now almost completely phased out
Multiplexing enables a single T-1 circuit to carry 24 channels, each capable of 64-Kbps throughput
The speed of a T-carrier depends on its signal level
For T-1s using STP, repeaters must regenerate the signal approximately every 6000 feet
Frame relay was originally designed as a fast packet-switched network over ISDN
DSL operates over the PSTN
Notes: Summary
ISDN is a legacy technology that is now almost completely phased out
Multiplexing enables a single T-1 circuit to carry 24 channels, each capable of 64-Kbps throughput
The speed of a T-carrier depends on its signal level
For T-1s using STP, repeaters must regenerate the signal approximately every 6000 feet
Frame relay was originally designed as a fast packet-switched network over ISDN
DSL operates over the PSTN

## Slide 81: Summary
Broadband cable is based on the coaxial cable used for TV signals
Signals transmitted via power lines are subject to much more noise than DSL or cable services
ATM specifies Data Link layer framing techniques
SONET is a high-bandwidth WAN signaling technique developed for fiber-optic cabling
MPLS is extremely fast and can carry various types of payloads
The 802.16 standards are known as WiMAX
Notes: Summary
Broadband cable is based on the coaxial cable used for TV signals
Signals transmitted via power lines are subject to much more noise than DSL or cable services
ATM specifies Data Link layer framing techniques
SONET is a high-bandwidth WAN signaling technique developed for fiber-optic cabling
MPLS is extremely fast and can carry various types of payloads
The 802.16 standards are known as WiMAX

## Slide 82: Summary
Geosynchronous earth orbit means that satellites orbit the Earth at the same rate as the Earth turns
Within each satellite band, frequencies used for uplink and downlink transmission differ to help ensure that signals traveling in one direction do not interfere with signals traveling in the other direction
Equipment located at the customer’s premises, regardless of who owns it, is called customer premise equipment (CPE)
Notes: Summary
Geosynchronous earth orbit means that satellites orbit the Earth at the same rate as the Earth turns
Within each satellite band, frequencies used for uplink and downlink transmission differ to help ensure that signals traveling in one direction do not interfere with signals traveling in the other direction
Equipment located at the customer’s premises, regardless of who owns it, is called customer premise equipment (CPE)