## Slide 1: STAT 441 (QC ) Methods and Philosophy of Quality Control
Dr. Abdulhakim Al-Babtain

## Slide 2: Operations as a Transformation Process
Feedback
INPUT
Material
Machines
Labor
Management
Capital
OUTPUT
Goods
Services
TRANSFORMATION
PROCESS

## Slide 3: Transformation Processes
Physical (manufacturing)
Locational (transportation/ warehouse)
Exchange (retail)
Physiological (health care)
Psychological (entertainment)
Informational (communications)

## Slide 4
Why Study Operation Management?
Related to all areas of any business
No business without Operations
Employs the most number of people
Largest investment in asset
Global nature of competition
Most costs incurred in operations
Technical core of any business

## Slide 5: An Integrated Value Chain
Manufacturer
Supplier
Customer
Flow of information (customer order)
Flow of product (order fulfillment)

## Slide 6: J.M. Juran
Quality from the bottom of the organization up,
Quality is “fitness for use”,
The Quality Trilogy
  Planning: create a processes capable of meeting quality goals
  Control: compare actual performance to standard and take action on the difference
  Improvement: find ways to better than the standard

## Slide 7: Deming PDCA Cycle
What change is needed?
What data are available?
Must a test be conducted?
Perform test.
Analyze data.
Carry out change.
Evaluate results.
Did improvement occur?
Make change permanent.
Try another change

## Slide 8: Process Capability and Statistical Quality Control
Process Variation
Process Control Procedures
  Variable data
  Attribute data
Acceptance Sampling
  Process Capability
  Operating Characteristic Curve
Notes: 2

## Slide 9: Basic Forms of Variation
Assignable variation is caused by factors that can be clearly identified and possibly managed.
Common variation is inherent in the production process.
Notes: 3

## Slide 10: Introduction to SPC
Statistical process control is a collection of tools that when used together can result in process stability and variability reduction

## Slide 11: Chance and Assignable Causes of Quality Variation
A process that is operating with only chance causes of variation present is said to be in statistical control.
A process that is operating in the presence of assignable causes is said to be out of control.
The eventual goal of SPC is reduction or elimination of variability in the process by identification of assignable causes.
Tampering can make the process variation 1.41 times worse than not doing anything!!!

## Slide 12: Statistical Basis of Control Chart
Basic Principles
A typical control chart has control limits set at values such that if the process is in control, nearly all points will lie between the upper control limit (UCL) and the lower control limit (LCL).

## Slide 13: Statistical Basis of Control Chart

## Slide 14: Statistical Basis of Control Chart
Out-of-Control Situations
If at least one point plots beyond the control limits, the process is out of control
If the points behave in a systematic or nonrandom manner, then the process could be out of control.

## Slide 15: Statistical Basis of Control Chart
Relationship between hypothesis testing and control charts
We have a process that we assume the true process mean is  = 74 and the process standard deviation is  = 0.01. Samples of size 5 are taken giving a standard deviation of the sample average, , as
Control limits can be set at 3 standard deviations from the mean.
This results in “3-Sigma Control Limits”
UCL = 74 + 3(0.0045) = 74.0135
CL= 74
LCL = 74 - 3(0.0045) = 73.9865

## Slide 16: Statistical Basis of the Control Chart
H0:  = 74
H1:   74

## Slide 17: Statistical Basis of the Control Chart
Important uses of the control chart
Most processes do not operate in a state of statistical control.
Consequently, the routine and attentive use of control charts will identify assignable causes. If these causes can be eliminated from the process, variability will be reduced and the process will be improved.
The control chart only detects assignable causes. Management, operator, and engineering action will be necessary to eliminate the assignable causes.
Out-of-control action plans (OCAPs) are an important aspect of successful control chart usage.
Refer to the process improvement cycle.

## Slide 18: Statistical Basis of the Control Chart
Types the control chart
Variables Control Charts
  These charts are applied to data that follow a continuous distribution (measurement data).
  X-bar chart, R chart, S chart, …
Attributes Control Charts
  These charts are applied to data that follow a discrete distribution.
  p chart, c chart, u chart, …

## Slide 19: Statistical Basis of the Control Chart

## Slide 20: Choice of Control Limits
General model of a control chart
where L = distance of the control limit from the center line
= mean of the sample statistic, w.
= standard deviation of the statistic, w.

## Slide 21: Choice of Control Limits
“99.7% of the Data”
If approximately 99.7% of the data lies within 3 of the mean (i.e., 99.7% of the data should lie within the control limits), then 1 - 0.997 = 0.003 or 0.3% of the data can fall outside 3 (or 0.3% of the data lies outside the control limits). (Actually, we should use the more exact value 0.0027).
0.0027 is the probability of a Type I error or a false alarm in this situation.

## Slide 22: Choice of Control Limits
Three-Sigma Limits
The use of 3-sigma limits generally gives good results in practice.
If the distribution of the quality characteristic is reasonably well approximated by the normal distribution, then the use of 3-sigma limits is applicable.
These limits are often referred to as action limits.

## Slide 23: Choice of Control Limits
Warning Limits on Control Charts
Warning limits (if used) are typically set at 2 standard deviations from the mean.
If one or more points fall between the warning limits and the control limits, or close to the warning limits the process may not be operating properly.
Good thing: warning limits often increase the sensitivity of the control chart.
Bad thing: warning limits could result in an increased risk of false alarms.

## Slide 24: Sample Size and Sampling Frequency
In designing a control chart, both the sample size to be selected and the frequency of selection must be specified.
Larger samples make it easier to detect small shifts in the process.
Current practice tends to favor smaller, more frequent samples.

## Slide 25: Rational Subgroups
Subgroups or samples should be selected so that if assignable causes are present, the chance for differences between subgroups will be maximized, while the chance for differences due to these assignable causes within a subgroup will be minimized.

## Slide 26: Rational Subgroups
Selection of Rational Subgroups
Select consecutive units of production.
  Provides a “snapshot” of the process.
  Effective at detecting process shifts.
Select a random sample over the entire sampling interval.
  Can be effective at detecting if the mean has wandered out-of-control and then back in-control.

## Slide 27: Analysis of Patterns on Control Charts
Nonrandom patterns can indicate out-of-control conditions
Patterns such as cycles, trends, are often of considerable diagnostic value
Look for “runs” - this is a sequence of observations of the same type (all above the center line, or all below the center line)
Runs of say 8 observations or more could indicate
an out-of-control situation.
  Run up: a series of observations are increasing
  Run down: a series of observations are decreasing

## Slide 28: Control Charts for and R
Control Limits for the chart (P. 251)
A2 and A3 is found in Appendix VI for various values of n (P-702).

## Slide 29: Control Charts for and R
Control Limits for the R chart
and
Control Limits for the S chart
and
Since is unbiased estimate for σ.
D3, D4 , B3 and B4 are found in Appendix VI for various values of n (P-702).

## Slide 30: X-bar & R Charts: Example

## Slide 31: X-bar & R Charts: Example

## Slide 33
The Control Chart for Attributes
The cost of collecting data for attributes is less than that for the variables
There are various types of control charts for attributes:
  The p chart for the fraction rejected
  The np chart for the total number rejected
  The c chart for the number of defects
  The u chart for the number of defects per unit

## Slide 34: p Chart
Type of attributes control chart
  Nominally scaled categorical data
    e.g., good-bad
Shows % of nonconforming items
Example: Count # defective chairs & divide by total chairs inspected; Plot
  Chair is either defective or not defective
Notes: 24

## Slide 35: p Chart Control Limits
# Defective Items in Sample i
Size of sample i
z = 2 for 95.5% limits; z = 3 for 99.7% limits
Notes: 25

## Slide 42: c Chart
Type of attributes control chart
  Discrete quantitative data
Shows number of nonconformities (defects) in a unit
  Unit may be chair, steel sheet, car etc.
  Size of unit must be constant
Example: Count # defects (scratches, chips etc.) in each chair of a sample of 100 chairs; Plot
Notes: 26

## Slide 43: c Chart Control Limits
# Defects in Unit i
# Units Sampled
Use 3 for 99.7% limits
Notes: 27

## Slide 46: U Chart P. 314

## Slide 47
https://www.youtube.com/watch?v=p-gvwkHePaU

## Slide 48
HW, X R bar Charts

## Slide 49
The Basic Seven (B7)
The magnificent seven
Tools of Quality
Histogram or stem-and-leaf plot
Check sheet
Pareto chart
Cause-and-effect diagram
Defect concentration diagram
Scatter diagram
Control chart
"As much as 95% of quality related problems in the factory can be solved with seven fundamental quantitative tools.“
- Kaoru Ishikawa
https://asq.org/quality-resources/seven-basic-quality-tools

## Slide 50
Histogram or stem-and-leaf plot

## Slide 51
2. Check sheet

## Slide 52
3. Pareto chart
A Pareto Chart is a graph that indicates the frequency of defects, as well as their cumulative impact. Pareto Charts are useful to find the defects to prioritize in order to observe the greatest overall improvement.
Pareto Analysis
Very similar to Histograms
Use of the 80/20 rule
Use of percentages to show importance

## Slide 53
The Pareto diagram serves as a visual representation of the vital few against the trivial many.

## Slide 54
4. Fishbone Diagrams
Cause-and-Effect Diagram
How to Construct,
Define the problem or effect to be analysed.
Form the team to perform the analysis. Often the team will uncover potential
causes through brainstorming.
Draw the effect box and the centre line.
Specify the major potential cause categories and join them as boxes connected to the center line.
Identify the possible causes and classify them into the categories in step 4. Create new categories, if necessary.
Rank order the causes to identify those that seem most likely to impact the problem.
Take corrective action.
Notes: -

## Slide 56
5. Defect concentration diagram

## Slide 57
6. Scatter diagram
The scatter diagram graphs pairs of numerical data, with one variable on each axis, to look for a relationship between them. If the variables are correlated, the points will fall along a line or curve.

## Slide 58: Basic Forms of Statistical Sampling for Quality Control
Sampling to accept or reject the immediate lot of product at hand (Acceptance Sampling).
Sampling to determine if the process is within acceptable limits (Statistical Process Control)
Notes: 3

## Slide 59: Acceptance Sampling
Purposes
  Determine quality level
  Ensure quality is within predetermined level
Advantages
  Economy
  Less handling damage
  Fewer inspectors
  Upgrading of the inspection job
  Applicability to destructive testing
  Entire lot rejection (motivation for improvement)
Notes: 4

## Slide 60: Acceptance Sampling
Disadvantages
  Risks of accepting “bad” lots and rejecting “good” lots
  Added planning and documentation
  Sample provides less information than 100-percent inspection
Notes: 5

## Slide 61: Acceptance Sampling by Variables
Caution in the Use of Variables Sampling
The distribution of the quality characteristic must be known in order to use variables sampling
The usual assumption is that the parameter of interest follows the normal distribution. This is a critical assumption.
If the normality assumption is not satisfied, then estimates of the fraction defective based on the sample mean and standard deviation will not be the same as if the parameter were normally distributed.

## Slide 62: Acceptance Sampling by Variables
Caution in the Use of Variables Sampling
It is possible to use variables sampling plans when the parameter of interest does not have a normal distribution.
If the form of the distribution is known, it is possible to devise a procedure for applying a variables sampling plan.

## Slide 63
Design of Lot-by Lot Sampling Plans
Specify the plan (n,c) given N: for a lot size N, determine the sample size n, and the acceptance number c. (Reject lot if number of defects > c.) Specify course of action if lot is rejected.
N
n
Number
Conforming
Accept or
Reject Lot

## Slide 64: Types of Sampling Plans
There are variables sampling plans and attribute sampling plans (this chapter concentrates on attributes)
  Single sampling plan
  Double-sampling plan
  Multiple-sampling plan
  Sequential-sampling

## Slide 65: Acceptance Sampling: Single Sampling Plan
A simple goal
Determine (1) how many units, n, to sample from a lot, and (2) the maximum number of defective items, c, that can be found in the sample before the lot is rejected.
Notes: 7

## Slide 66: A Single Sample Plan
Lot of N items
Random sample of size n pulled
Sample inspected (d= number of defectives)
d > c
Replace the defectives and accept the lot
Reject the lot and take corrective action
no
yes
N = lot size
n = sample size
c = acceptance number
d = observed number of defectives

## Slide 67: Types of Error
Type I error - rejecting the null hypothesis when it is true.
Pr(Type I error) = . Sometimes called the producer’s risk.
Type II error - not rejecting the null hypothesis when it is false.
Pr(Type II error) = . Sometimes called the consumer’s risk.

## Slide 68: Risk
Acceptable Quality Level (AQL)
the maximum percentage of nonconforming items in a batch that can be considered acceptable.
α (Producer’s risk)
  The probability of rejecting a good lot.
Lot Tolerance Percent Defective (LTPD)
percentage of nonconforming items in a lot for which the consumer wishes the probability of acceptance is a specified low value. Also know as “unacceptable quality level.”
 (Consumer’s risk)
  The probability of accepting a bad lot.
Notes: 8

## Slide 69
Example: Lots of size N = 1000 fuses are inspected using an (50,3) sampling acceptance plan. Usually, the defect rate is 3% but occasionally there is a bad batch that has a 6% defect rate.
What is the producer’s risk of this sampling plan?
What is the consumer’s risk of this sampling plan?
What if the plan was changed to (50,2)? What would the relative change be between the consumer’s and producer’s risk?

## Slide 70: The OC Curve
The operating-characteristic (OC) curve measures the performance of an acceptance-sampling plan.
The OC curve plots the probability of accepting the lot versus the lot fraction defective.
The OC curve shows the probability that a lot submitted with a certain fraction defective will be either accepted or rejected.

## Slide 71: Operating Characteristic Curve
n = 99
c = 4
AQL
LTPD
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
1
2
3
4
5
6
7
8
9
10
11
12
Percent defective
Probability of acceptance
 =.10
(consumer’s risk)
a = .05 (producer’s risk)
Notes: 9

## Slide 72: Example: Acceptance Sampling Problem
Zypercom, a manufacturer of video interfaces, purchases printed wiring boards from an outside vender, Procard. Procard has set an acceptable quality level of 1% and accepts a 5% risk of rejecting lots at or below this level. Zypercom considers lots with 3% defectives to be unacceptable and will assume a 10% risk of accepting a defective lot.
Develop a sampling plan for Zypercom and determine a rule to be followed by the receiving inspection personnel.
Notes: 10

## Slide 73: Example: Step 1. What is given and what is not?
In this problem, AQL is given to be 0.01 and LTDP is given to be 0.03. We are also given an alpha of 0.05 and a beta of 0.10.
What you need to determine your sampling plan is “c” and “n.”
Notes: 11

## Slide 74: Example: Step 2. Determine “c”
First divide LTPD by AQL.
Then find the value for “c” by selecting the value in the TN7.10 “n(AQL)”column that is equal to or just greater than the ratio above.
Exhibit TN 7.10
c
LTPD/AQL
n AQL
c
LTPD/AQL
n AQL
0
44.890
0.052
5
3.549
2.613
1
10.946
0.355
6
3.206
3.286
2
6.509
0.818
7
2.957
3.981
3
4.890
1.366
8
2.768
4.695
4
4.057
1.970
9
2.618
5.426
So, c = 6.
Notes: 11

## Slide 75: Example: Step 3. Determine Sample Size
c = 6, from Table
n (AQL) = 3.286, from Table
AQL = .01, given in problem
Sampling Plan:
Take a random sample of 329 units from a lot.
Reject the lot if more than 6 units are defective.
Now given the information below, compute the sample size in units to generate your sampling plan.
n(AQL/AQL) = 3.286/.01 = 328.6, or 329
(always round up)
Notes: 13

## Slide 76
Average Outgoing Quality
Outline
Average Outgoing Quality (AOQ)
Average Outgoing Quality Limit (AOQL)

## Slide 77
Average Outgoing Quality
After a sample is inspected, the items which are found defective, may be
  Case 1: returned to the producer or
  Case 2: repaired or replaced by the producer.
We assume Case (2).
If a lot is rejected, it may be subjected to a 100% inspection. Such action is referred to as screening inspection, or detailing. This is sometimes described as an acceptance/rectification scheme.

## Slide 78
Average Outgoing Quality
If a lot is rejected, there may again be two assumptions regarding the defective items. The defective items may be
  Case 1: returned to the producer or
  Case 2: repaired or replaced by the producer.
We assume Case 2.
So, if a lot is rejected, it will contain no defective item at all, after screening inspection. The consumer will get N good items. However, if a lot is accepted, it may contain some defective items because many of the (N-n items in a single sampling plan) items not inspected may be defective.

## Slide 79
Average Outgoing Quality
Thus, if there is an average of 2% defective items, the accepted lots will contain little less than 2% defective items and rejected lots will contain no defective item at all. On average, the consumer will receive less than 2% defective items.
Given a proportion of defective, p the Average Outgoing Quality (AOQ) is the proportion of defectives items in the outgoing lots. More precise definition is given in the next slide.

## Slide 80: Average Outgoing Quality

## Slide 81
Average Outgoing Quality
Case 1 is not discussed in class

## Slide 82
Average Outgoing Quality

## Slide 83
Average Outgoing Quality
Given a proportion of defective, we can compute the Average Outgoing Quality (AOQ)
As p increases from 0.0, the AOQ values increases up to a limit called Average Outgoing Quality Limit (AOQL), after which the AOQ values descend continuously to 0.0. This is shown in the next slide.

## Slide 84
AOQ Curve
0.015
0.010
0.005
0.01
0.02
0.03
0.04
0.05
0.06
0.07
0.08
0.09
0.10
AOQL
Average
Outgoing
Quality
(Incoming) Percent Defective
AQL
LTPD

## Slide 85
Example: Suppose that Noise King is using rectified inspection for its single sampling plan. Calculate the average outgoing quality limit for a plan with n=110, c=3, and N=1000. (Assume that the defective items are replaced)

## Slide 86
Take small initial sample
If # defectives < lower limit, accept;
If # defectives > upper limit, reject;
If # defectives between limits, take second sample.
Accept or reject lot based on 2 samples
Less inspection than in single-sampling
Double Sampling Plans

## Slide 88
Process Capability
Whether a process is capable of meeting specification refers to the variability of the product in relation to the specification limits.
Frequency
Mean
Specification
Limits set at:
Frequency
Frequency
High
Capability
Medium
Capability
Low
Capability

## Slide 89: The Quality Improvement Model
Use SPC to Maintain Current Process
Collect & Interpret Data
Select Measures
Define Process
Is Process Capable ?
Improve Process Capability
Is Process Stable ?
Investigate & Fix Special Causes
No
Yes
No
Yes
Is Process Capable?
Purpose: Determine the adequacy of the process with respect to customer /management needs.
Notes: This module covers this step

## Slide 90: Capable Process
A stable process that meets customer requirements.
8
22
24
2
4
6
10
12
14
16
18
20
26
28
30
32
Run Order
UCL
CL
LCL
Control Chart
Lower Spec
Upper Spec
Target
Histogram
Capability assessments for unstable processes, may not be indicative of how the process is actually performing.
Notes: Capable process produce everything within customer specifications
Stability is a crucial prerequisite for capability

## Slide 91: Assessing Process Capability
Counting Measures
  The average percent defectives.
  The average number of defects.
Instrument Measures
  Comparing both the center of the process and the process variation
Notes: Counting Measures - Process average IS your capability
Instrument Measures - Look at the center and the variability of the process

## Slide 92: Capability Assessment for Counting Measures “Order Entry Process”
Is this process adequate as is?
Should it be improved?
Week
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Total
# Errors
15
22
18
10
13
9
27
12
24
22
8
8
26
16
20
10
16
9
15
20
320
0
5
10
15
20
25
30
35
5
10
15
20
Avg=16.0
LCL=4.0
UCL=28.0
Week
Number
of Errors
Control Chart
Notes: Process is stable - confirmed by control chart
“Is this process adequate as is?”
“What are management’s expectations for this process?”
Not all processes need to be improved right now. Others may need to be worked on first, then return to this one.
Customer focus is important, even if the customer doesn’t provide input easily. They may just say, “no errors is what I want.”

## Slide 93: Measures of Process Capability
C
p
=
Specification Range
True Process Range
=
USL - LSL
6sc
C
pk
=
Distance from process average
to closest specification limit
1
2
True Process Range
=
min (USL -
x
,
x
- LSL)
3sc
Problem: We are assuming the process has a target that is in the center of the specification range, and that the process is in fact centered on that target.
Note: a negative result is possible if the process average is outside specifications
Benefits:
• Optimal values are attained by running exactly
between specs.
• Can (must) be used for 1-sided specifications
C
p
< 1.0
®
Process is not capable of meeting specs
C
p
= 1.0
®
Process is marginally capable
C
p
> 1.0
®
Process is capable of meeting specs
C
pk
< 1.0
®
Process is not capable of meeting specs
C
pk
= 1.0
®
Process is marginally capable
C
pk
> 1.0
®
Process is capable of meeting specs
Warning: Capability assessments for unstable processes, may not be indicative of how the process is actually performing.

## Slide 94: Process Capability
How much material is out of spec?
  In the short term?
  In the long term?
USL
LSL

## Slide 95: Process Capability Ratios
Voice of The Customer
Voice of The Process
USL
LSL
https://www.youtube.com/watch?v=H6St9mCKWuA

## Slide 97: Process Capability - The Strategy
Centering –The Process Is On Target
Spread – Reduce The Variation
LSL
USL
Defects
Defects

## Slide 98: Process Capability Ratios
2 Key Metrics for Measuring Capability
C
Min(
X
-
LSL
3
USL
-
X
3
pk

,
)

## Slide 99: Process Capability Ratios - Concept
Total Tolerance
C
Process Spread
p


## Slide 100: CP & CPK Measure Short-term Capability
A Short-term Capability study covers a relatively short period of time (days, weeks) generally consisting of 30 to 50 data points. The actual number depends on the subject under study.
Is The Process
In Control ?
Is It Producing
Defects ?

## Slide 101: Long Term Performance
A long-term capability study covers a relatively long period of time (weeks, months) generally consisting of 100-200 data points. Again, the actual amount depends on the subject under study.
Is The Process
In Control ?
Is It Producing
Defects ?
Short term
Capability

## Slide 102: A Further Look at Capability
Compare the estimates of the process deviations from the short-term and long-term data
What is the difference between the short-term and the long-term data?
What implication does this have in doing capability studies?
Descriptive Statistics
Variable N Mean StdDev
short term 30 30.6 2.23
long term 180 33.8 4.44

## Slide 103: Measures of Process Performance
P
p
=
Specification Range
True Process Range
=
USL - LSL
6ss
P
pk
=
Distance from process average
to closest specification limit
1
2
True Process Range
=
min (USL -
x
,
x
- LSL)
3ss
Benefits:
• Optimal values are attained by running exactly
between specs.
• Can (must) be used for 1-sided specifications
P
p
< 1.0
®
Process Performance is not meeting specs
P
p
= 1.0
®
Process Performance is marginally meeting specs
P
p
> 1.0
®
Process Performance is meeting specs
Ppk
< 1.0
®
Process Performance is not meeting specs
Ppk
= 1.0
®
Process Performance is marginally meeting specs
Ppk
> 1.0
®
Process Performance is meeting specs
Note: a negative result is possible if the process average is outside specifications
Problem: We are assuming the process has a target that is in the center of the specification range, and that the process is in fact centered on that target.

## Slide 104: Performance vs. Capability
These data show that the process, if well controlled can perform much better than it currently is
Days Sales Outstanding for 55 Days
DSO

## Slide 105: Capability vs. Performance
Days Sales Outstanding for 55 Days
DSO
Process Performance: Total Variation including shifts and drifts
(Pp & Ppk)
Capability: Only random or short term variability
(Cp & Cpk)

## Slide 106: Process Performance Ratios
The P-family of indices are computationally the same as the C-family of ‘capability’ indices, but use the observed long-term standard deviation.
P
Min(
X
-
LSL
USL
-
X
pk

,
)
3ss
3ss
P
p
=
USL - LSL
6ss

## Slide 107: WARNING!!!
Statistical Assumptions Made In Capability Studies
Data Comes From a Stable Process
If not, work towards getting the process in control