## Slide 1: Chapter 12
Concrete Construction Part 2

## Slide 2: 12-2 CONCRETE CONSTRUCTION PRACTICES
Concrete construction involves:
  concrete batching,
  mixing,
  transporting,
  placing,
  consolidating,
  finishing, and
  curing.

## Slide 3: 12-2 CONCRETE CONSTRUCTION PRACTICES
Transporting and Handling
Placing and Consolidating
Finishing and Curing
Hot-Weather Concreting
Cold-Weather Concreting

## Slide 4: Transporting and Handling
A number of different items of equipment are available for moving concrete from the mixer to its final position.
  wheelbarrows,
  buggies,
  chutes,
  conveyors,
  pumps,
  buckets, and
  trucks.
care must be taken to avoid segregation when handling plastic concrete.

## Slide 5: FIGURE 12-15: Concrete pump and truck mixer. (Courtesy of Challenge-Cook Bros., Inc.)

## Slide 6: Transporting and Handling
Concrete conveyors: move concrete either horizontally or vertically.
Chutes are widely used for:
  moving concrete from the mixer to haul units, and
  placing concrete into forms.

## Slide 7: Transporting and Handling
Truck mixers are equipped with integral retracting chutes
It used for discharging concrete directly into forms within the radius of the chute.
When chuting concrete,
  the slope of the chute must be high enough to keep the chute clean
  but not high enough to produce segregation of the concrete.

## Slide 8: Placing and Consolidating
Placing: the movement of plastic concrete into its final position (usually within forms).
  Before placing concrete, the underlying surface and the interior of all concrete forms must be properly prepared.

## Slide 9: Placing and Consolidating
Consolidation: is the process of removing air voids in concrete as it is placed by using.
  Concrete vibrators
    hand rodding or spading may be employed.
  Immersion-type electric,
  pneumatic, or
  hydraulic concrete vibrators are widely used.

## Slide 10: Finishing and Curing
Finishing: is the process of bringing the surface of concrete to its final position and imparting the desired surface texture.
Finishing operations include:
  Screeding: is the process of striking off the concrete in order to bring the concrete surface to the required grade
  https://www.youtube.com/watch?v=LSyTBM5nfMU
  Floating: When the concrete has hardened enough, the concrete is floated with a wood or metal float,
  https://www.youtube.com/watch?v=aRFdoVcJAPc
  Troweling: with a steel trowel follows floating when a smooth dense surface is desired, and
  https://www.youtube.com/watch?v=N1C-Zi-5qzE
  brooming: the concrete may be broomed by drawing a stiff broom across the surface.

## Slide 11: FIGURE 12-16: Roller finisher being used on large slab pour. (Courtesy of CMI Corp.)

## Slide 12: Hot-Weather Concreting
The rate of hardening of concrete is greatly accelerated when concrete temperature is appreciably higher than the optimum temperature of 50 to 60°F (10 to 15.5°C).
90 degrees Fahrenheit (32°C) is considered a reasonable upper limit for concreting operations.

## Slide 13: Cold-Weather Concreting
The problems of cold-weather concreting are essentially opposite to those of hot-weather concreting.
Concrete must not be allowed to freeze during the first 24 h after placing (to avoid permanent damage and loss of strength).
  Keep Minimum 50°F (l0°C) for at least 3 days after placing.
  Use Type III (high early strength) cement or
  Use an accelerator to reduce concrete setting time during low temperatures

## Slide 14: 12-3 CONCRETE FORMWORK
General Requirements for Formwork
Typical Formwork
Minimizing Cost of Formwork
Construction Practices
Formwork Safety

## Slide 15: General Requirements for Formwork
The principal requirements for concrete formwork are that it be:
  safe,
  produce the desired shape and surface texture, and
  be economical.
Procedures for designing formwork that will be safe under the loads imposed by:
  plastic concrete,
  workers and other live loads, and
  external forces (such as wind loads)

## Slide 16: FIGURE 12-18: Typical wall form.

## Slide 17: FIGURE 12-20: Typical column form. (U.S. Department of the Army)

## Slide 18: FIGURE 12-21: Form for elevated slab. (Courtesy of American Concrete Institute)

## Slide 19: FIGURE 12-22: Beam and slab form. (Courtesy of American Concrete Institute)

## Slide 20: FIGURE 12-23: One-way slab form. (Courtesy of American Concrete Institute)

## Slide 21: FIGURE 12-24: Two-way slab form. (Courtesy of American Concrete Institute)

## Slide 22: FIGURE 12-25: Wood form for stairway. (U.s. Department of the Army)

## Slide 23: Minimizing Cost of Formwork
repetitive use of forms can lower formwork cost.
Multiple-use forms may be either:
  standard commercial types or
  custom-made by the contractor.
    use assembly-line techniques whenever possible.
Flying forms (Figure 12-26): are often economical in repetitive types of concrete construction.
use of slip forms and tilt-up construction techniques (Where appropriate)

## Slide 24: FIGURE 12-26: Repositioning flying form. (Courtesy of Lorain Division, Koehring Co.)

## Slide 25: Formwork Safety
Provide adequate foundations for all formwork.
Provide adequate bracing of forms.
Control the rate and location of concrete placement so that design loads are not exceeded.
Ensure that forms and supports are not removed before the concrete has developed the required strength.
When placing prefabricated form sections in windy weather, care must be taken to avoid injury due to swinging of the form caused by wind forces.
Clean the site from the nails.