## Slide 1
EIGRP
(Enhanced Interior Gateway Routing Protocol)

## Slide 2: What is EIGRP ?
EIGRP (Enhanced Interior Gateway Routing Protocol) is a network protocol that lets routers exchange information more efficiently than with earlier network protocols.
EIGRP evolved from IGRP (Interior Gateway Routing Protocol) and routers using either EIGRP and IGRP can interoperate because the metric (criteria used for selecting a route) used with one protocol can be translated into the metrics of the other protocol. EIGRP can be used not only for Internet Protocol (IP) networks but also for AppleTalk and Novell NetWare networks.

## Slide 3: EIGRP Metrics
EIGRP scales IGRP’s metrics by a factor of 256
  IGRP metric = 24 bits; EIGRP metric = 32 bits
  Bandwidth and Delay are equally weighted
  Reliability, Load, and MTU are off by default
  Hop count limited to 224 (IGRP’s limit is 255)
To remember of metric EIGRP components:
  Big = Bandwidth
  Dogs = Delay
  Really = Reliability
  Like = Load
  Me = MTU

## Slide 4: EIGRP for IP
No updates. Route updates sent only when a change occurs
Hello messages sent to neighbors every 5 seconds (60 seconds in most WANs)
Enhanced IGRP
EIGRP
EIGRP

## Slide 5: Configuring EIGRP for IP
172.16.10.0
10.110.1.0
AS=10
192.168.0.0
A
C
B
Enable EIGRP
Assign networks
If you use the same AS number for EIGRP as IGRP, EIGRP will automatically redistribute IGRP into EIGRP
Router(config)#router eigrp 10 Router(config-router)#network 10.0.0.0 Router(config-router)#network 172.16.0.0

## Slide 6: EIGRP Metrics (4)
The table in the figure shows the default delay values for various interfaces.
Notice that the default value is 20,000 microseconds for Serial interfaces and 100 microseconds for FastEthernet interfaces.

## Slide 7: Comparing between EIGRP & IGRP
IGRP | EIGRP
Classful Routing Protocol | Classless Routing Protocol VLSM, CIDR
bandwidth = (10,000,000/bandwidth kbps) delay = delay/10 24 bit metric for bandwidth and delay | bandwidth = (10,000,000/bandwidth kbps) * 256 delay = (delay/10) * 256 32 bit metric for bandwidth and delay
Maximum Hop Count = 255 | Maximum Hop Count = 224
No differentiation between internal and external routes. | Outside routes (redistributed) are tagged as external routes.
Automatic redistribution between IGRP and EIGRP as long as “AS” numbers are the same. | 

## Slide 8: Displaying Interface Values
R1> show interface fa0/0
Ethernet0 is up, line protocol is up
Hardware is Lance, address is 0010.7b3a.cf84 (bia 0010.7b3a.cf84)
MTU 1500 bytes, BW 100000 Kbit, DLY 100 usec,
rely 255/255, load 1/255
<output omitted>
R3> show interface s0/0
Serial0/0 is up, line protocol is up
Hardware is QUICC Serial
Description: Out to R1
Internet address is 192.168.64.5/30
MTU 1500 bytes, BW 1544 Kbit, DLY 20000 usec,
rely 255/255, load 246/255
<output omitted>

## Slide 9
S0/0 192.168.64.2/30
S0/0 192.168.64.1/30
S0/1 192.168.64.6/30
S0/0 192.168.64.5/30
Fa0/0 192.168.72.1/24
Fa0/0 192.168.1.1/24
Fa0/0 192.168.1.2/24
EIGRP AS 100
Bandwidth = (10,000,000/bandwidth kbps) * 256
R1
R2
R3
Bandwidth = 1,657,856
Bandwidth = 25,600
Delay = 512,000
Delay = 2,560
Determining the Bandwidth between R1 & R2
FastEthernet
= (10,000,000/100,000) * 256
= 25,600
T1
= (10,000,000/1544) * 256
= 1,657,856

## Slide 10
S0/0 192.168.64.2/30
S0/0 192.168.64.1/30
S0/1 192.168.64.6/30
S0/0 192.168.64.5/30
Fa0/0 192.168.72.1/24
Fa0/0 192.168.1.1/24
Fa0/0 192.168.1.2/24
EIGRP AS 100
Delay = (delay/10) * 256
R1
R2
R3
Bandwidth = 1,657,856
Bandwidth = 25,600
Delay = 512,000
Delay = 2,560
Determining the Delay between R1 & R2
FastEthernet
= (100/10) * 256
= 2,560
T1
= (20,000/10) * 256
= 512,000

## Slide 11
S0/0 192.168.64.2/30
S0/0 192.168.64.1/30
S0/1 192.168.64.6/30
S0/0 192.168.64.5/30
Fa0/0 192.168.72.1/24
Fa0/0 192.168.1.1/24
Fa0/0 192.168.1.2/24
EIGRP AS 100
What is the cost (metric) for 192.168.72.0/24 from R2?
R1
R2
R3
Bandwidth = 1,657,856
Bandwidth = 25,600
Slowest!
Delay = 512,000
Delay = 2,560
1,657,856512,000 2,560 --------------2,172,416
Cost: Slowest bandwidth
+ sum of delays
The cost!
bandwidth = (10,000,000/bandwidth kbps) * 256
delay = (delay/10) * 256
Determining the cost between R1 & R2

## Slide 12: The Routing Table
Administrative Distance / Metric
R3#show ip route
D 192.168.72.0/24 [90/2172416]
via 192.168.64.6, 00:28:26, Serial0

## Slide 13
Thank you for listing