## Slide 1
Enhanced Interior Gateway Routing Protocol
EIGRP

## Slide 2: INTRODUACTION
* EIGRP is enhanced version of IGRP.
* EIGRP classifies route entries into one of three categories: interior routes, system routes, and exterior routes.
2

## Slide 3
Interior route: is a path to a subnet of the network address of the data link on which the update is being broadcast.
System route : is a path to a network address, which has been summarized by a network boundary router.
Exterior route : is a path to a network that has been flagged as a default network.
3

## Slide 4: EIGRP Overview
- Fast convergence : ”routing table store in each router”
- AD = 90
-Eigrp is classless … Supports VLSM
Router send update only when there is change
- Use Diffusing update algorithm (DUAL).
- Successor & Feasible Successor.
4

## Slide 5: EIGRP TABLES
*Neighbor table : Keep information of Neighbors.
*Topology table : Successor and Feasible successor.
*Routing table : EIGRP places best routers form its topology table into the common routing table.
5

## Slide 6: EIGRP MESSAGES
Hello : Identifies neighbors and serves as a keep alive mechanism.
Update : Reliably send route information.
Query : Reliably requests specific route information.
Reply : Reliably responds to a query.
ACK : Acknowledgment.
6

## Slide 7: NEIGHBOR DISCOVERY AND ROUTE EXCHANGE
Step 1 : Router A sends out a hello (5-15,60-180)sec.
Step 2 : Router B sends back a hello and an update,
the update contains routing table.
Step 3 : Router A acknowledges the update.
Step 4 : Router A sends its update.
Step 5 : Router b acknowledges.
7

## Slide 8: BASIC EIGRP CONFIGURATION :
Router1(config)# router eigrp AS
Router1(config-router)# network network-ID
Router1(config-router)# no auto-summary
8

## Slide 9: EIGRP ROUTING
9

## Slide 10: EIGRP CONFIGURATION :
10

## Slide 11: EIGRP CONFIGURATION :
11