ASTiD

Advisory System for Tired Drivers

INSTALLATION, SET UP CONFIGURATION & USER GUIDE

Table of Contents

1	Installation Guide

2	ASTiD Set up Configuration

2.1 		Setting the language

2.2 		Setting the time and date

3	ASTiD overview

3.1		Background to research

3.2		What ASTiD monitors

4	ASTiD User Guide

  - Selecting sleep input

  - Setting snooze function

  - Power save mode

5	Service and Warranty

  - Return & replacement

  - Warranty

  - Contact details

6	Safety Warning

2	ASTID Set up & Configuration

When you turn on the ignition ASTiD will run through a self-test procedure. The traffic light unit will illuminate each LED in sequence and on the main unit the following words will be seen once the test is completed.

On first installation, ASTiD has a real time clock that needs to be set to local time zones. You will be prompted to reset the time and date. The clock can also be reset in normal mode by holding the left hand SELECT button down

2.1	Setting the language

The driver will need to select his or her preferred language. Press and hold down the SELECT button for 5 seconds. The screen will now change to the ‘Set Time’ display.

Release and then press and hold down the SELECT button for a further 5 seconds until the screen changes to the ’LANGUAGE’ menu.

Now press the SET button  to scroll through the available language codes

Now press SELECT to confirm and configure ASTiD to your selected language. You then need to press the SELECT button 3 times to get back to the main screen.

2.2	Setting the time and date

From the main screen press the SET button until the right hour is shown. Then, press the left hand SELECT button to set the hour. The cursor will now be on the minutes. Again, press the SET button to set the correct minutes.

A final press of the SELECT button will set the correct time. The display then automatically goes to the set date display

As the date may not have been set, press the SET button until the right day is shown. Then, press the SELECT button to set the day.

The cursor will now be on the month. Again, press the SET button to set the correct month. The cursor will now be on the year. Again, press the SET button to set the correct year.

A final press of the SELECT button will set the correct date.

The clock and date will only need to be re set if the Battery Back up runs flat or when clocks are changed for daylight saving.

## ASTiD is now installed and ready for driver use

# Text boxes

Rear View

Front View

To external display

The front RJ data port is only used for downloading information into the ASTiD MIS programme (not supplied).

To PC for download

EEPROM  OK

Set time    09: 15

LANGUAGE  GB

FR

Set time    09: 15

Date     17-03-09