## Slide 1
Unit 11
Datapath Design
College of Computer and Information Sciences
Department of Computer Science
CSC 220: Computer Organization

## Slide 2
Unit 11: Datapath Design
Overview
  Register file
  Function Unit
    ALU
    Combinational Shifter
  Basic Datapaths Design
  General Datapath Representation
  Accessing RAM
  The Control Word
Chapter-8
M. Morris Mano, Charles R. Kime and Tom Martin, Logic and Computer Design Fundamentals, Global (5th) Edition, Pearson Education Limited, 2016. ISBN: 9781292096124

## Slide 3: Datapath Design
A limited set of registers serve as fast temporary storage.
ALU & Shifter perform various operations on the data stored in the registers
A larger, but slower, random-access memory is also available.
The datapath completes a single microoperation each clock cycle.
For given microoperation, we need to specify;
    Source registers
    Destination register
    Operation to perform
ALU + Shifter
Registers

## Slide 4: Register file
Modern processors contain a number of registers grouped together in a register file.
Much like words stored in a RAM, individual registers are identified by an address.
Here is a block symbol for a
2k x n register file.
  There are 2k registers, so register addresses are k bits long.
  Each register holds an n-bit word, so the data inputs and outputs are n bits wide.
n
n
n
k
k
k
D data
Write
D address
A address
B address
A data
B data
Register File
D
WR
DA
AA
A
B
BA

## Slide 5: Accessing the register file
You can read two registers at once by supplying the AA and BA inputs. The data appears on the A and B outputs.
You can write to a register by using the DA and D inputs, and setting WR = 1.
These are registers so there must be a clock signal, even though we usually don’t show it in diagrams.
  We can read from the register file at any time.
  Data is written only on the positive edge of the clock.
n
n
n
k
k
k
D data
Write
D address
A address
B address
A data
B data
Register File
D
WR
DA
AA
A
B
BA

## Slide 6: What’s inside the register file
Here’s a 4 x n register file. (We’ll assume a 2k x n = 4 x n register file for all our examples.)
n
n
n
decoder
n Mux (41)
n Mux (41)
DA0 & DA1
Select the register
to write in
AA0 & AA1
BA0 & BA1
Select the register
to read from
The n-bit 4-to-1 muxes select the two register file outputs A and B, based on the inputs AA and BA.

## Slide 7: The all-important ALU
The main job of a central processing unit is to “process,” or to perform computations....remember the ALU
We’ll use the following general block symbol for the ALU.
  A and B are two n-bit numeric inputs.
  FS is an m-bit function select code, which picks one of 2m functions.
  The n-bit result is called G.
  Several status bits provide more
  information about the output G:
    V = 1 in case of signed overflow.
    C is the carry out.
    N = 1 if the result is negative.
    Z = 1 if the result is 0.
A
B
ALU
G
Z
N
C
V
FS
n
n
n
m

## Slide 8: Combinational Shifter
Bidirectional shift register with parallel load
  Disadvantage: 3 clock pulses required
Combinational Shifter
  Transfer from a source to destination register
  One clock cycle
Operations: Transfer, Shift Left, Shift Right
Filling of vacant positions
  Here, will provide input lines or zero fill
  Many options depending on instruction set

## Slide 9: 4-Bit Basic Left/Right Shifter
Serial Inputs:
  IR for right shift
  IL for left shift
Serial Outputs
  R for right shift (Same as MSB input)
  L for left shift (Same as LSB input)
Shift Functions: (S1, S0) = 00 Pass B unchanged 01 Right shift 10 Left shift 11 Unused
B
3
I
R
I
L
S
Serial
output L
Serial
output R
2
B
2
B
1
B
0
H
0
H
1
H
2
H
3
S
M
U
X
0
1
2
S
M
U
X
0
1
2
S
M
U
X
0
1
2
S
M
U
X
0
1
2

## Slide 10: Function Unit Design
Function Unit = ALU + Shifter
The function select code FS is 4 bits long, but there are only 15 different functions here.
0
V
C
N
Z
Bus A
Bus B
Function unit
A
B
n
G select
4
Zero Detect
MF select
n
n
n
F
MUX F
H select
2
A
B
S
2:0
|| C
in
Arithmetic/logic
unit (ALU)
G
B
S
Shifter
H
I
L
I
R
0
0
1
A
B
Function Unit
F
Z
N
C
V
FS
n
n
n
m

## Slide 11: Definition of Function Unit Select (FS) Codes
Boolean
Equations:
MF = F3 F2
Gi = Fi
Hi = Fi
G
Select,
H
Select,
and
MF
in T
of
FS
Codes
FS(3:0)
MF
Select
G
Select(3:0)
H
Select(3:0)
Micr
ooperation
0000
0
0000
XX
0001
0
0001
XX
0010
0
0010
XX
0011
0
0011
XX
0100
0
0100
XX
0101
0
0101
XX
0110
0
0110
XX
0111
0
0111
XX
1000
0
1
X
00
XX
1001
0
1
X
01
XX
1010
0
1
X
10
XX
1011
0
1
X
11
XX
1100
1
XXXX
00
1101
1
XXXX
01
1110
1
XXXX
10
F A
¬
F A
1
+
¬
F A
B
¬
F A
B
1
¬
F A
B
¬
F A
B
1
¬
F A
1
-
¬
F
A
¬
F
A B
Ù
¬
F
A B
Ú
¬
F
A B
¬
F
A
¬
F
B
¬
F
sr
B
¬
F
sl
B
¬
+
+
+
+
+
+
Å

## Slide 12: Basic Datapaths Design
Guiding principles for basic datapaths:
  The set of registers
    A set of registers with common access resources called a register file
  Microoperation implementation
    One or more shared resources for implementing microoperations
    Buses - shared transfer paths
    Arithmetic-Logic Unit (ALU) - shared resource for implementing arithmetic and logic microoperations
    Shifter - shared resource for implementing shift microoperations

## Slide 13: Datapath Example
Four parallel-load registers (R0-R3)
Two mux-based register selectors
Register destination decoder
Mux B for external constant input
Buses A and B with external address and data outputs
ALU and Shifter with Mux F for output select
Mux D for external data input
Logic for generating status bits V, C, N, Z
MD select
0
1
MUX D
V
C
N
Z
n
n
n
n
n
n
n
n
n
n
n
2
2
n
n
A data
B data
Register file
1
0
MUX B
Address
Out
Data
Out
Bus A
Bus B
n
n
Function unit
A
B
n
G select
4
Zero Detect
MF select
n
n
n
F
MUX F
H select
2
n
A
B
S
2:0
|| C
in
Arithmetic/logic
unit (ALU)
G
B
S
Shifter
H
MUX
0
1
2
3
MUX
0
1
2
3
0
1
2
3
Decoder
Load
Load
Load
Load
(Load enable)
WR
D data
D address
2
Destination select
Constant in
MB select
A select
A address
B select
B address
R3
R2
R1
R0
Bus D
n
Data In
I
L
I
R
0
0
0
1

## Slide 14: Datapath Example: Performing a Microoperation
Microoperation: R0 ← R1 + R2
MD select
0
1
MUX D
V
C
N
Z
n
n
n
n
n
n
n
n
n
n
n
2
2
n
n
A data
B data
Register file
1
0
MUX B
Address
Out
Data
Out
Bus A
Bus B
n
n
Function unit
A
B
n
G select
4
Zero Detect
MF select
n
n
n
F
MUX F
H select
2
n
A
B
S
2:0
|| C
in
Arithmetic/logic
unit (ALU)
G
B
S
Shifter
H
MUX
0
1
2
3
MUX
0
1
2
3
0
1
2
3
Decoder
Load
Load
Load
Load
Load enable
Write
D data
D address
2
Destination select
Constant in
MB select
A select
A address
B select
B address
R3
R2
R1
R0
Bus D
n
Data In
I
L
I
R
0
0
0
1
Apply 01 to A select to place contents of R1 onto Bus A
Apply 10 to B select to place contents of R2 onto B data and apply 0 to MB select to place B data on Bus B
Apply 0010 to G select to perform addition G = Bus A + Bus B
Apply 0 to MF select and 0 to MD select to place the value of G onto BUS D
Apply 00 to Destination select to enable the Load input to R0
Apply 1 to Load Enable to force the Load input to R0 to 1 so that R0 is loaded on the clock pulse (not shown)
The overall microoperation requires 1 clock cycle

## Slide 15: General Datapath Representation
Here we move up one level in the hierarchy from that datapath
The registers, and the multiplexer, decoder, and enable hardware for accessing them become a register file
A register file is an array of fast registers
The ALU, shifter, Mux F and status hardware become a function unit
The remaining muxes and buses which handle data transfers are at the new level of the hierarchy
Address out
Data out
Constant in
MB select
Bus A
Bus B
FS
V
C
N
Z
MD select
n
D data
Write
D address
A address
B address
A data
B data
2
m
x
n
Register file
m
m
m
n
n
n
n
n
A
B
Function
unit
F
4
MUX B
1
0
MUX D
0
1
n
n
Data in

## Slide 16: Datapath Representation (continued)
In the register file:
  Multiplexer select inputs become A address and B address
  Decoder input becomes D address
  Multiplexer outputs become A data and B data
  Input data to the registers becomes D data
  Load enable becomes write
The register file now appears like a memory based on clocked flip-flops (the clock is not shown)
The function unit labeling is quite straightforward except for FS
Address out
Data out
Constant in
MB select
Bus A
Bus B
FS
V
C
N
Z
MD select
n
D data
Write
D address
A address
B address
A data
B data
2
m
x
n
Register file
m
m
m
n
n
n
n
n
A
B
Function
unit
F
4
MUX B
1
0
MUX D
0
1
n
n
Data in

## Slide 17: Accessing RAM
Here’s a way to connect RAM into our existing datapath.
Write to RAM: we must give an address and a data value.
These will come from the registers/Constant. We connect A data to the memory’s ADRS input, and B data to the memory’s DATA input.
Set MW = 1 to write to the RAM. (It’s called MW to distinguish it from the WR write signal on the register file.)
MW = 1
to write to the RAM
D0
Q D1
S
D data
Write
D address
A address
B address
A data
B data
Register File
WR
DA
AA
BA
RAM
ADRS
DATA
CS
WR
OUT
MW
+5V
A
B
F
Z
N
C
V
FS
FS
MD
S D1 D0
Q
Constant
MB

## Slide 18: Reading from RAM
To read from RAM, A data must supply the address.
Set MW = 0 for reading.
The incoming data will be sent to the register file for storage.
This means that the register file’s D data input could come from either the ALU output or the RAM.
A mux MD selects the source for the register file.
  When MD = 0, the ALU output can be stored in the register file.
  When MD = 1, the RAM output is sent to the register file instead.
D0
Q D1
S
D data
Write
D address
A address
B address
A data
B data
Register File
WR
DA
AA
BA
RAM
ADRS
DATA
CS
WR
OUT
MW
+5V
A
B
F
Z
N
C
V
FS
FS
MD
S D1 D0
Q
Constant
MB

## Slide 19: Notes about this setup
We now have a way to copy data between our register file and the RAM.
Notice that there’s no way for the Function Unit to directly access the memory—RAM contents must go through the register file first.
Here the size of the memory is limited by the size of the registers; with n-bit registers, we can only use a 2n x n RAM.
D0
Q D1
S
D data
Write
D address
A address
B address
A data
B data
Register File
WR
DA
AA
BA
RAM
ADRS
DATA
CS
WR
OUT
MW
+5V
A
B
F
Z
N
C
V
FS
FS
MD
S D1 D0
Q
Constant
MB

## Slide 20: Datapath (Summary)
The datapath completes a single microoperation each clock cycle.
For given microoperation, we need to specify;
    Source registers
    Destination register
    Operation to perform
For the datapath, we also need to specify;
    External or function data
    Data B from register or constant
    Whether the destination is updated

## Slide 21: The Control Word
The datapath has many control inputs
The signals driving these inputs can be defined and organized into a control word
To execute a microinstruction, we apply control word values for a clock cycle. For most microoperations, the positive edge of the clock cycle is needed to perform the register load
The datapath control word format and the field definitions are shown on the next slide

## Slide 22: The Control Word Fields
Fields
  DA – D Address (destination)
  AA – A Address
  BA – B Address (source for MUXB
  MB – Mux B (constant/source
  FS – Function Select
  MD – Mux D
  RW – Register Write
The connections to datapath are shown in the next slide
Control word
D
A
AA
BA
M
B
FS
M
D
R
W
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0

## Slide 23: Control Word Block Diagram
10
8
14
0
13
11
Bus D
Constant in
n
n
MUX B
1
0
D data
Write
D address
A address
B address
A data
B data
8
x
n
Register file
A
B
Function
unit
n
n
n
MUX D
0
1
n
n
Data in
Bus A
Bus B
R
W
12
AA
15
D
A
n
BA
9
Address out
Data out
V
C
N
Z
7
MD
1
MB
6
4
FS
5
3
2

## Slide 24: Encoding The Control Word

## Slide 25: Microoperations for the Datapath - Symbolic Representation

## Slide 26: Microoperations for the Datapath - Binary Representation
Results of simulation of the above on the next slide

## Slide 27: Datapath Simulation Results of simulation of the above
1
4
7
1
0
4
5
2
0
7
0
3
6
0
3
0
X
X
2
0
7
0
3
6
0
2
3
0
14
1
2
0
10
2
0
0
1
X
18
18
1
255
2
2
3
4
12
18
5
0
6
7
8
clock
DA
1
4
AA
2
BA
3
6
Constant_in
2
MB
Address_out
Data_out
FS
5
Status_bits
Data_in
MD
RW
reg0
0
reg1
reg2
reg3
reg4
reg5
reg6
reg7
7
8
5

## Slide 28: Stored Program Computer
Control words operate the datapath
Store control words in memory
  Sequence through them to perform a series of computational steps
This is what a computer does