## Slide 1: Water
Lecture 3

## Slide 2: Objectives
Chemical and physical properties of water.
Sources of water.
Water cycle.
Types and sources of water pollution.
Processing drinking water.
Environmental hazards from water pollution.

## Slide 3: Introduction
What is water?
Compound made up of 2 atoms of hydrogen and one atom of oxygen (H2O).
  Gas, liquid and solid state.
Essential for life on earth.
  Biochemical reactions.
  Water in oceans and lakes holds heat and helps to control earth’s temperature.
Humans may not survive more than three (3) days without water.
Dehydration
  2% – thirst.
  5% – fatigue, nausea, headache.
  10-15% – muscle spasms, delirium.
  > 15% – death.

## Slide 5: Introduction
Water facts
2/3 of earth’s surface covered by water
Only ~3% is fresh water
  ~ 30% of it is underground water.
  ~ 1% is in the atmosphere.
  ~0.3% is in rivers and lakes.
  The rest is in the form of ice.
Middlecamp CH et al.Chemistry in Context: Applying Chemistry to Society. 7th Edition. McGrawHill. 2012

## Slide 6: Sources of water
Surface water – fresh water from rivers, lakes, streams.
Ground water – sweet water in aquifers.
Sea water – salty water that needs desalination before use.
Ice caps and glaciers – frozen water.
Middlecamp CH et al.Chemistry in Context: Applying Chemistry to Society. 7th Edition. McGrawHill. 2012
In Saudi Arabia, supplies of fossil ground water in aquifers have been rapidly depleted.
Desalination of sea water to convert sea water into fresh drinkable water.

## Slide 7: Watershed
  Watershed: carries water "shed" from the land after rain falls and snow melts.
  Stream, lake, wetland, the ocean.
Supplies water for drinking, agriculture, manufacturing, recreation and the habitat to plants and animals.
http://water.epa.gov/type/watersheds/whatis.cfm What is a watershed?
http://www.nature.org/ourinitiatives/regions/northamerica/unitedstates/indiana/journeywithnature/watersheds-101.xml

## Slide 8: Uses of water
Domestic – drinking, cooking, cleaning.
Public use – parks, fire-fighting.
Agricultural – crop irrigation.
Recreational – lakes, rivers.
Industrial – energy, cooling, heating.
Environmental – habitat for fauna and flora.

## Slide 9: Water cycle
https://www.youtube.com/watch?v=9pqh6tlEOhs

## Slide 10: Factors affecting the water cycle
Natural factors
A particle of water make take from a few days to thousands of years to complete the water cycle.
Trapped water – underground or in glaciers.
  Needs to get back into the atmosphere.
Seasons.
  Winter and trees losing their leaves – very little transpiration.
Air temperature.
  Changes affect the rate of water evaporation, transpiration.
  Evaporation and transpiration increase with air temperature.

## Slide 11: Factors affecting the water cycle
Vegetation
  Environment determines the type of vegetation and the rate of transpiration.
    Desert plants transpire little to save water.
Amount of sunshine
  Sun provides the energy to naturally evaporate water.
    Desert areas have a lot of sunshine and high rates of evaporation.
Landscape (geography)
  Run-off and percolation change with soil type a geography of terrain.
  Precipitation (rain) is higher in hills and mountains than in lower areas.

## Slide 12: Factors affecting the water cycle
Humidity
  Amount of water vapor in the air.
  Evaporation decreases when the air has high humidity.

## Slide 13: Factors affecting the water cycle
Global climate changes
Affect the water cycle, environment and living organisms.
  Excess rain, storms and floods and water contamination and scarcity.
  Drought.
  Melting glaciers.
  Reduced precipitation in mountain tops, means no ice in winter, and no lakes or rivers in the summer.
  Change animal patterns of migration.
  Infectious diseases outbreaks.

## Slide 14: Water pollution
Presence of substances not normally found in water and that can be harmful to living organisms.
  Chemical, physical, radioactive, pathogenic substances.
Natural or man-made.
Degree of pollution has to do with the quantity of pollutant in the water.
Following the use of water, water needs disposal, recycling, and possibly reusing.
Wastewater treatment/disposal and public health.
Natural water cycles and water purification take a long time.

## Slide 15: Sources of water pollution
Natural and man-made
Point and Non-Point Sources

## Slide 16: Causes of water pollution
Industrial and agricultural waste
Radioactive waste
Oil pollution/spills
Solid waste (any garbage)
Sewage/waste water
Global warming

## Slide 17: Types of Water Pollution
Chemical pollution
Household
    Drugs, antibiotics dumped in sewage.
    Cleaning chemicals.
    Food waste.
Agriculture
    Pesticides, herbicides, fertilizers
    Radioactive materials from phosphate rock-made fertilizers.
The Encyclopedia of Earth. Water pollution. http://www.eoearth.org/view/article/156920/
Sources

## Slide 18: Types of Water Pollutants
Chemical pollution
Industrial
  Runoffs, oil spills.
  Heavy metals from mining.
  Chemicals from manufacturing.
  Radioactive materials from nuclear power plants.
Water and sewage treatment.
  Chlorinated organic molecules from sewage and water treatment.
Landfill (site of disposal waste).
The Encyclopedia of Earth. Water pollution. http://www.eoearth.org/view/article/156920/

## Slide 19: Types of Water Pollution
Acid Rain
Sulfur dioxide (SO2) and nitrogen oxides (NOx) react in the atmosphere with water, oxygen, and other chemicals to form a mild solution of sulfuric acid and nitric acid.
  Natural sources – volcanoes and decaying vegetation.
  Man-made sources – emissions from fossil fuel combustion.
It includes any form of precipitation with acids.
Acid rain increases acidity and aluminum content in lakes and streams in a watershed.
  Harm to biodiversity.
  Toxic to fish and other aquatic life.
http://www3.epa.gov/acidrain/effects/surface_water.html

## Slide 20: Types of Water Pollution
Physical pollution
Solid debris
  Vegetation, animal or human waste.
  Excessive sediment (dirt) load from farming, construction, gardening.
  Solid waste from human activity (plastic bags, bottles, construction).
Temperature changes
  Heat, steam from industrial activities (point source).
Three big pollutants. http://water.epa.gov/learn/resources/bigpollutants.cfm

## Slide 21: Types of Water Pollution
Nutrient pollution
Nitrogen, phosphorus.
Fertilizers from farms and gardens.
Animal waste.
Detergents.
The Encyclopedia of Earth. Water pollution. http://www.eoearth.org/view/article/156920/
Effect on the environment
  Death of aquatic life.
  Interfere with water treatment.

## Slide 22: Types of Water Pollution
Microbial pollution
Protozoa, bacteria, viruses, fungi.
  Untreated sewage, surface runoff.
  Landfill and dump runoff.
  Animal waste from farms.
Entamoeba histolytica – protozoa.
Salmonella, Shigella, E. coli, Vibrio cholerae – bacteria.
Usually associated with fecal contamination of water.
Three big pollutants. http://water.epa.gov/learn/resources/bigpollutants.cfm
Staph Aureus
Influenza virus
Hookworm
Fungi
Amoeba
Common waterborne pathogens

## Slide 23: Water Pollution and waterborne disease
Transmitted by contaminated water carrying the infective agent.
  Gastroenteritis – diarrhea, cramps, nausea, vomiting.
Life-threatening for the young, the elderly, pregnant women and the immunocompromised.
Amebiasis – caused by the parasite Entamoeba histolytica.
  Amoeba produces cysts that are carried in feces.
  intestinal infections.
Giardiasis and Cryptosporidiosis – caused by parasites in animal and human feces.
  Especially at risk are the immunocompromised.
    Diarrhea, cramps, headache.
  Chlorine destroys Giardia but not Cryptosporidium.
  Boiling water for >1minute will destroy these and other pathogens.

## Slide 24: Water Pollution and waterborne disease
Legionnaire’s disease
  Lung infections – pneumonia.
  High fever, cough, chest pain, abdominal pain and diarrhea.
  Contaminated aerosol particles from home water systems, cooling systems and stagnant water.
  Some protozoa (amoebas) serve as host for the bacteria.
Naegleria fowleri
  ‘Brain-eating’ amoeba.
  Normally harmless and found in warm freshwater lakes and in soil.
  Can infect the brain via the nasal passages, breaking down nerve cells.
  Tap water, saline solutions.

## Slide 25: Water consumption
Maximum contaminant level goal (MCLG) – ideal situation.
  Maximum level of a contaminant in drinking water at which no known or anticipated adverse effect on human health would occur.
  For known carcinogens the goal is zero, because any small amount is considered a risk.
Chemistry in Context: Applying Chemistry to Society. 7th Edition. Middlecamp C et al.. McGrawHill. 2012
Maximum contaminant level (MCL) – real situation.
  It is the legal limit for the concentration of a contaminant in drinking water.
  Set as close as possible to the MCLG considering the practicality of it.
  Most MCL are the same as MCLG, except for carcinogens.

## Slide 26: Water consumption
Making water safe to drink
Whether water is safe to drink or not depends on:
  What is in the water.
  How much of it is in the water.
  How much water someone drinks in a day.
Contaminants harmful to human health have legal limits according to their toxicity.
  Limits take into account the technology available for removal.
Some contaminants can affect liver, kidney function, or the nervous system.
Lead is particularly harmful to children, accumulate in bone and brain, affecting brain and neural development.
  Industrial waste.
  Lead pipes and lead-lined tanks in water coolers.

## Slide 27: Water consumption
Contaminants regulated in drinking water
Inorganic chemicals
  Heavy metals – copper, cadmium, chromium, mercury, lead.
  Non-metal ions – nitrate, fluoride, arsenic.
Organic chemicals
  Pesticides, solvents, and compounds for plastics manufacturing.
Radionuclides
  Alpha and beta particles, radium and uranium.
Biological agents
  Cryptosporidium, Giardia, Legionella, fecal coliforms (E. coli) and intestinal viruses.
Disinfectants
  Chloramines, chlorine, chlorine dioxide.
Disinfection byproducts
  Bromate, chlorite, haloacetic acids, trihalomethanes.
http://www.epa.gov/your-drinking-water/table-regulated-drinking-water-contaminants

## Slide 28: Contaminants in drinking water
Water disinfectants
  Chloramines
    Eye/nose irritation, stomach problems, anemia.
  Chlorine
    Eye/nose irritation, stomach problems.
  Chlorine dioxide
    Anemia, CNS problems in infants and children.
Water disinfection byproducts
  Bromate
    Increased cancer risk.
  Chlorite
    Anemia and CNS problems in infants and children.
  Haloacetic acids and Total triahalomethanes (TTHMs).
    Increased cancer risk.
    TTHMs – liver, kidney or CNS.
Drinking Water Contaminants. http://water.epa.gov/drink/contaminants/#List

## Slide 29: Secondary drinking water contaminants
Non-mandatory standards established only as guidelines to assist public water systems in managing their drinking water for taste, color, and odor.
  These contaminants are not considered a risk to health.
Problems related to secondary contaminants
  Aesthetic — taste, color or odor.
  Cosmetic — skin or teeth discoloration.
  Technical — damage to water equipment or reduced effectiveness of treatment.
Contaminant | Secondary MCL | Noticeable Effects above the Secondary MCL
Aluminum | 0.05 to 0.2 mg/L* | colored water
Chloride | 250 mg/L | salty taste
Color | 15 color units | visible tint
Copper | 1.0 mg/L | metallic taste; blue-green staining
Corrosivity | Non-corrosive | metallic taste; corroded pipes/ fixtures staining
Fluoride | 2.0 mg/L | tooth discoloration
Foaming agents | 0.5 mg/L | frothy, cloudy; bitter taste; odor
Iron | 0.3 mg/L | rusty color; sediment; metallic taste; reddish or orange staining
Manganese | 0.05 mg/L | black to brown color; black staining; bitter metallic taste
Odor | 3 TON (threshold odor number) | "rotten-egg", musty or chemical smell
pH | 6.5 - 8.5 | low pH: bitter metallic taste; corrosion high pH: slippery feel; soda taste; deposits
Silver | 0.1 mg/L | skin discoloration; graying of the white part of the eye
Sulfate | 250 mg/L | salty taste
Total Dissolved Solids (TDS) | 500 mg/L | hardness; deposits; colored water; staining; salty taste
Zinc | 5 mg/L | metallic taste

## Slide 30: Treating drinking water
1. Water purification
Screen-removal of debris.
  Plant material, garbage.
Coagulation and Flocculation.
  Addition of aluminum sulfate and calcium hydroxide to form a gel that collects suspended dirt particles.
Sedimentation.
  Particles settle at the bottom.
Filtration.
  Charcoal or gravel, and sand.
Disinfection
  Kill disease-causing microbes.
Additional steps
  Spraying the water in the air to remove volatile compounds.
  Adding fluoride.

## Slide 31: Treating drinking water
2. Disinfection
A. Chlorine
Kills microorganisms by direct contact.
Cannot kill bacteria or viruses inside dirt particles.
Dirt particles must be removed before chlorination.
Toxicity concerns
Chlorine-containing compounds that remain after disinfection.
  Gases that keep the water form getting contaminated during transport.
Chlorine can react with organic matter in drinking water forming toxic compounds.
  Trihalomethanes – chlorine, bromine.

## Slide 32: Treating drinking water
Disinfection
B. Ozone treatment
O3 can kill bacteria when used for water disinfection.
Advantages
Smaller amounts of O3 compared to chlorine are used.
More effective against viruses than chlorine.
Disadvantages
Expensive to treat small amounts of water.
Ozone decomposes quickly and water can get contaminated during transport.
Small amount of chlorine is added to ozonated water before leaving the treatment plant.

## Slide 33: Treating drinking water
Disinfection
C. Ultraviolet light
UV-C light that can breakdown nucleic acids and DNA in microorganisms like bacteria, viruses, molds, parasites.
Advantages
Fast, inexpensive, can be used in a small scale.
  Rural homes with unsafe well water.
Disadvantages
It does not destroy microbes hidden inside suspended particles.
Water can get contaminated after leaving the treatment plant.

## Slide 34: Water Desalination
Removal of the sodium and chloride ions from the water.
  Sea water has high salt content (3.5%).
Distillation – heating sea water, and condensing and collecting the vapor.
  Energy-consuming process (-).
  The heat purifies the water (+).
Reverse osmosis – membranes and pressure to separate the sodium and chlorine ions from the water.

## Slide 35: Prevention of water pollution and waste
Conserve water.
  Turn off the tap when running water is not necessary.
  Cut down water spent on household cleaning.
Mind the waste that goes down the drains.
Reduce use of household chemicals.
  Cleaning and personal use.
  Pesticides and fertilizers.

## Slide 36: Consequences of water pollution
Harm to living organisms - long-term and short-term exposure.
Industrial waste and heavy metals
  Toxic to immune system, reproductive system, liver, kidneys, developmental problems, cancer.
Acid rain
  Harm to aquatic life.
Microbial pollutants from sewage.
  Waterborne infectious diseases.
    Cholera and typhoid fever.
Suspended particles in freshwater affect the quality of drinking water for humans and the environment for aquatic life.
  Can reduce the amount of sunlight penetrating the water, disrupting the growth of photosynthetic plants and micro-organisms.

## Slide 37: References
Frumkin H. Environmental Health: From Global to Local. 2nd Ed. Jossey-BSS, Wiley Imprint. 2010.
Middlecamp CH et al. Chemistry in Context: Applying Chemistry to Society. 7th Edition. McGrawHill. 2012.
The Encyclopedia of Earth. Water pollution. http://www.eoearth.org
The water cycle. http://www.futuresparks.org.au/media/20852/pearson_science_7_sb_chapter_3_unit_3.3.pdf
USGS. Summary of the water cycle. http://water.usgs.gov/edu/watercyclesummary.html
Drinking Water Contaminants. http://water.epa.gov/drink/contaminants/#List
Water: drinking water. http://water.epa.gov/drink/
Penn State Extension. Lead in drinking water. http://extension.psu.edu/natural-resources/water/drinking-water/water-testing/pollutants/lead-in-drinking-water Based on Lead in Drinking Water, 1994, by Bryan Swistock and William Sharpe. Updated January 2016 by Amy Galford and Bryan Swistock.

## Slide 38: Reading (optional)
http://waterandme.tamu.edu/WaterPollution/waterpollution.pdf

## Slide 40
Thank you!