## Slide 1
Chapter 6
Petrochemicals
Dr. Seham ALTERARY
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 2
By the end of this chapter students will be able to:
Remember, understand, apply, Analyse, evaluate and create
Petrochemicals
Definition of petroleum
Fractional distillation of crude oil Major petrochemicals and uses
Comparison between Light and heavy Crude oil
The Organization of the Petroleum Exporting Countries (OPEC)
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 3
Petrochemicals
The Organization of the Petroleum Exporting
Countries (OPEC):
OPEC, Embargos, and Conservation:
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
The Organization of Oil Exporting Countries (OPEC) was founded by five countries Iran, Iraq, Kuwait, Saudi Arabia and Venezuela in 1960.
EC now includes 13 members: Algeria, Angola, Ecuador, Indonesia, Iran, Iraq, Kuwait, Libya, Nigeria, Qatar, Saudi Arabia, the United Arab Emirates, and Venezuela.
The organization-especially Saudi Arabia, which is the richest in reserves-strives to stabilize oil prices by acting as a “swing” producer, raising production when prices are high and cutting production when prices are low.

## Slide 4
Petrochemicals
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
شركة ينبع الوطنية للبتروكيماويات (ينساب) شركة مساهمة سعودية مؤسسة بموجب أنظمة المملكة العربية السعودية تحت سجل تجاري رقم 4700009432 صادر بتاريخ 12 محرم 1427هـ الموافق 11 فبراير 2006م.
إن أهداف شركة ينساب تتمثل في تصنيع المنتجات البتروكيماوية الآتية: إثيلين، إثيلين جلايكول، بولي إثيلين عالي الكثافة، بولي إثيلين منخفض الكثافة الخطي، بولي بروبلين، بيوتين 1، بيوتين 2، إم. تي. بي. إي ، بي.تي.أكس طبقا لعقد ينساب التأسيسي والأنظمة المتبعة في المملكة. بدأت الشركة في مزاولة نشاطها التجاري في 1 مارس 2010م.

## Slide 5
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
شركة كيان السعودية للبتروكيماويات هي شركة مساهمة سعودية , وأعلن عن تأسيس شركة كيان السعودية للبتروكيماويات كيان السعودية بموجب اتفاقية الشراكة التي وقعت بين الشركة السعودية للصناعات الأساسية سابك وشركة الكيان للبتروكيماويات كيان , وكان ذلك في الربع الأول من عام 2006 , وقضت اتفاقية الشراكة بتأسيس شركة مساهمة باسم شركة كيان السعودية للبتروكيماويات كيان السعودية ، يكون مقرها مدينة الجبيل الصناعية، برأس مال قدره خمس عشر مليار ريال سعودي، يوزع كما يلي : 45% طرح عام ، 35% للشركة السعودية للصناعات الأساسية سابك , 20% شركة الكيان للبتروكيماويات (كيان)
لإنتاج : أثيلين، بروبلين ، بولي بروبلين ،بولي أثيلين ، جلايكول الأثيلين ، ميثيل الأمين ،ثنائي ميثيل الفرماميد ،كلورايد الكولين ، ايثول الأمين ، الايثوكسليت،بيسفينول أ ، إضافة إلى البولي كربونيت . بولي اثلين علي الكثافه , بولي اثلين منخفض الكثافه

## Slide 6
Petrochemicals
What is petroleum?
Petroleum is a compound of two Latin words: petra (rock) + oleum (oil).
Petroleum also is called crude oil, crude, black gold.
Bitumen (tar) also known as asphalt is a solid or semisolid form of petroleum.
Biocrude comes from plants or municipal wastes.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 7
Petrochemicals
What is petroleum?
o There are hundreds of different crude oils with a wide range of physical
and chemical properties; properties vary with location, depth, and age
of the oil field.
i
o Crude oil is the base for lots of products. These include transportation fuels such as gasoline, diesel, and jet fuel. They also include fuel oils used for heating and electricity generation.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 8
Petrochemicals
Fractional Distillation
Is different from distillation in that it separates a mixture into a number of different parts, called fractions. A tall column is fitted above the mixture, with several condensers coming off at different heights. The column is hot at the bottom and cool at the top.
Substances with high boiling points condense at the (hot) bottom and substances with lower boiling points condense on the way to the (cold) top.
The crude oil is evaporated and its vapours condense at different temperatures in the fractionating column. Each fraction contains hydrocarbon molecules with a similar number of carbon atoms.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 9
Petrochemicals
Appearance:
Some crude oil is as clear as vegetable oil and other crudes are green, brown, or black.
Some flow like water, while others don’t flow at all unless they are heated.
Bitumen and tar are black and gooey.

## Slide 10
Petrochemicals
Petroleum is not a single substance.
Petroleum is a complex mixture of countless organic molecules derived from ancient microorganisms.
Most of the molecules are hydrocarbons.
Some contain sulfur, nitrogen, oxygen, or trace elements.
Raw crude oil contains inorganic matter, such as water, salt, inorganic sulfur, and dirt.
Chemical Composition:

## Slide 11
Petrochemicals
Saturated hydrocarbons can be acyclic paraffins (alkanes) or cyclic paraffins (naphthene's).
  Olefins are very rare in natural petroleum.
They are mainly products from thermal cracking in refineries.
  Hydrocarbon Ring Compounds (Naphthene's and Aromatics).
Molecular Composition:

## Slide 12
o Heteroatom compounds contain sulfur, nitrogen, oxygen, and trace elements.
Petrochemicals
Sulfur is found primarily as H2S, mercaptans, sulfides, disulfides, thiophenes, benzothiophenes, and polybenzothiophenes.
Nitrogen is present primarily pyrroles, pyridines, quinolines, indoles, and carbazoles.
  Amides and oxazoles contain both nitrogen and oxygen.
  Amines are not found in raw crudes.
Oxygen compounds include naphthenic acids, carboxylic acids, phenols, cresols, and furans.

## Slide 13
Petrochemicals
Light Crude oil
It has low density and flows freely at RT.
It has low viscosity, low specific gravity and high API gravity due to the presence of a high proportion of light hydrocarbon fractions.
It generally has a low wax content as
well.
It receives a higher price than heavy crude oil on commodity markets because it produces a higher percentage of gasoline and diesel fuel when converted into products by an oil refinery.
Heavy crude oil or extra heavy crude oil
It is any type of crude oil which does not flow easily.
Its density or specific gravity is
higher than that of light crude oil.
It has more negative impact on the
environment than counterpart since its
its light refinement
requires the use of more advanced techniques an the use of contaminants.
Comparison between Light and heavy Crude oil

## Slide 14
What is the API Gravity?
The American Petroleum Institute gravity, or API gravity, is a measure of how heavy or light a petroleum liquid is compared to water.
If API Gravity> 10  lighter than water, floats on water.
If API Gravity< 10  heavier than water, sinks.
It’s a measure of the relative density of a petroleum liquid and the density of water. It is used to compare the relative densities of petroleum liquids.
Petrochemicals

## Slide 15
Some Important definitions
Petrochemicals
A feedstock refers to any unprocessed material used to supply a manufacturing process.
Feedstocks are bottleneck assets because their availability determines the ability to make products.
Crude Oil:
Crude oil is a naturally occurring, unrefined petroleum product composed of hydrocarbon deposits
and other organic materials.
Refining
The process of separating crude oil into useful components including gasoline, diesel fuel, jet fuel, fuel oil, and other products.

## Slide 16
Cracking, as the name suggests, is a process in which large hydrocarbon molecules are broken down
into smaller and more useful ones, for example:
Petrochemicals
Steam cracking is a petrochemical process in which saturated hydrocarbons are broken down into smaller, often unsaturated, hydrocarbons. It is the principal industrial method for producing the lighter alkenes (or commonly olefins ), including ethene (or ethylene ) and propene (or propylene).
Cracking

## Slide 17
Petrochemicals
Petroleum Refining Processes
Crude Oil Preprocessing
Crude oil comes from the ground mixed with a variety of substances: gases, water, salt, and dirt.
These must be removed before the crude can be transported effectively and refined without undue fouling and corrosion.

## Slide 18
Petrochemicals
Activities related to the petroleum industry
Petroleum industries depend on a large number of activities that require specialized equipment and trained labour. These activities include the
following operations:
Oil detection
Drilling
Oil extraction
Oil treatment
Oil transportation
Refining
The most
important
characteristic of this industry is the industry based on oil refining to obtain petroleum products.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 19
Petrochemicals
An oil refinery or industrial process plant
where crude oil
petroleum refinery is an
is
transformed and refined into more useful products such as petroleum naphtha, gasoline, diesel fuel, asphalt base, heating oil , kerosene, liquefied petroleum gas, jet fuel and fuel oils. Petrochemicals feed stock like ethylene and propylene can also be produced directly by cracking crude oil without the need of using refined products of crude oil such as naphtha.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Oil refinery

## Slide 20
Petrochemicals
Petroleum products are materials derived from crude oil(petroleum) as it is processed in oil refineries. The majority of petroleum is converted to petroleum products, which includes several classes of fuels.
This includes:
Gases (Methane, Ethane, Propane, and Butane)
Light distillers (Petroleum ether, Gasoline and Naphtha)
Medium distillates (kerosene and diesel)
Heavy distillates (oils, lubricants, waxes, and asphalt)
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 21
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 22
The feedstock goes through a steam cracker, where numerous basic petrochemicals are produced.
These chemicals are either sold to other petrochemical companies or, to create more value, go through a process of polymerization in which they become thermoplastic resins.
Resins are sold to converters, that transform them into finished products ready to be sold
to the market.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 23
The list of some commercial petrochemicals the chemical products obtained from petroleum by refining.
Petrochemicals

## Slide 24
Petrochemicals

## Slide 25
Petrochemicals

## Slide 26
Petrochemicals

## Slide 27
Petrochemicals
The term modification
alkyd
of
is a the
original name
"alcid",
reflecting they
the fact that are derived
from alcohol and organic acids

## Slide 28: Chapter 6-Part II Petrochemicals
Dr. Seham ALTERARY
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 29
Petrochemicals
Out Lines
Refining process
Petroleum Composite
What is Naphtha?
What is Natural Gas?
  Petrochemicals
    Petrochemicals from Methane
    Petrochemicals from Ethane
    Petrochemicals from other petroleum cut

## Slide 30
Petrochemicals
1
Separation
2
Conversion
3
Treating
The Three Stages of Refining
Petrochemicals
Refining Process:

## Slide 31
Petrochemicals
1. Separation
In the first step, molecules are separated through atmospheric distillation (i.e. at normal atmospheric pressure), according to their molecular weight.
During the process, which known as refining the oil is heated at the bottom of a 60-meter distillation column at a temperature of 350 to 400°C, causing it to vaporize. The vapours rise inside the column while the heaviest molecules, or residuals, remain at the bottom, without vaporizing.

## Slide 32
Petrochemicals
1. Separation
Each tray collects a different petroleum cut (fraction), , also known as a petroleum cut, with highly viscous preservation (hydrocarbons) like asphalt (bitumen) at the bottom and gases at the top.
As the vapours rise, the molecules condense into liquids at different temperatures in the column. Only gases reach the top, where the temperature has dropped to 150°C. The liquids, which are become increasingly light the higher they are found in the column, are collected on trays located at different heights of the column.

## Slide 33
Petrochemicals
2.Conversion
There are still too many heavy hydrocarbon
molecules remaining after the
separation process. To meet demand for lighter products, the heavy molecules are “cracked” into two or more lighter ones.

## Slide 34
Petrochemicals
Cracking
Long hydrocarbon are less useful than shorter ones like petrol. We can 'crack' these longer chains into shorter ones. This is done using heat or a catalyst.
CRACKING
Crude oil contains many large molecules. If these are to be used as fuels or feedstock for
the chemical industry then they have to be cracked into smaller molecules.
When hydrocarbons burn they are reacting with oxygen in the air. In general, the smaller
the molecule the better it will mix and then react with the air.

## Slide 35
Petrochemicals
2.Conversion
The conversion process, which is carried out at 500°C, is also known as catalytic cracking because it uses a catalyst to speed up the chemical reaction. This process converts 75% of the heavy products into gas, gasoline and diesel. The yield can be increased further by adding hydrogen , a process called hydrocracking.
The more complex the operation, the more it costs and the more energy it uses. The refining industry’s ongoing objective is to find a balance between yield and the cost of conversion.
Note That:

## Slide 36
Petrochemicals
Crude oil naturally contains contaminants such as sulfur, nitrogen, and heavy metals, which are undesirable in motor fuels. The treating process, primarily hydrotreating, removes these chemicals by binding them with hydrogen, absorbing them in separate columns, or adding acids to remove them.
Treating involves removing or significantly reducing molecules that are corrosive or cause air pollution, especially sulfur. European Union sulfur emission standards are very stringent. Since January 1, 2009, gasoline and diesel sold in Europe cannot contain more than 10 parts per million (ppm) , or 10 milligrams per kilogram, of sulfur.
The purpose of these measures is to improve air quality and optimize the effectiveness of catalytic
converters used to treat exhaust gas.
3. Treating

## Slide 37
Petrochemicals
Type of Product |  | No of Carbons | BpTemp. in Celsius | Usage
Natural Gas | Methane, Ethane Propane, Butane | 1,2 3,4 | -162 , -89 -42, 0 | As Fuel & in Petrochemicals industries
Light distillers | Petroleum ether Gasoline Naphtha | 5,6 5-10 6-12 | 36-60 35-175 65-200 | Solvents and Detergents vehicle fuel Solvents, motors fuel and Petrochemicals industries
Medium distillers | -Kerosene(paraffin) -Diesel fuel | 18-10 25-12 | 325-125 360-210 | Fuel for jet engines, tillage machines and for Residential boilers Fuel for diesel engines and houses.
Heavy distillers | Lubricating oils Wax Asphalt or bitumen Chem 342, | 50-23 20-40 More than By Dr. Seham ALTERARY. 1st | 370-700 350-560 Above 700 Semester 1443-2021 | Heavy mineral oils, ship fuel, and lubricating oils Paraffin wax and Vaseline Asphalt roads and waterproofing materials
Petroleum Composite

## Slide 38
Petrochemicals
What is Naphtha?
Petroleum naphtha is an intermediate hydrocarbon liquid stream derived from the refining of crude oil.

## Slide 39
Petrochemicals
What is Natural Gas?
Natural gas is made up of a mixture of four naturally occurring gases, all of which have different molecular structures. This mixture consists primarily of methane, which makes up 70-90% of natural gas along with ethane, butane and propane.

## Slide 40
Petrochemicals

## Slide 41
Petrochemicals
Petrochemicals from other petroleum cut
Petrochemicals from Ethane
Petrochemicals from Methane
Synthesis Gas CO/H2
Methanol
Ammonia
Ethyl hexanol
Acetylene
Carbon black
Polyethylene
PolyvinylChloride
Polystyrene
Polyvinylacetate
Ethanol
Acetaldehyde
Ethylene Oxide
Acrylic Acid
Propylene
Butane
Naphtha
Toluene
Benzene
Xylene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 42
Petrochemicals
Petrochemicals from Methane

## Slide 43
Petrochemicals
Synthesis Gas (CO/H2)
Used in the Production of
Methane
Acetylene
Chloromethane
Carbon Black
Methanol
CH3OH
Ammonia
NH3
2-Ethyl hexanol

## Slide 44
Petrochemicals
It is used for production of methanol or ammonia. It is also used for production of synthetic
fuels, both diesel (Fischer–Tropsch process) and gasoline
Syngas
Syngas, also known as synthesis gas, synthetic gas or producer gas, can be produced from a variety of different materials that contain carbon.

## Slide 45
Petrochemicals
Syngas can be formed by the following methods
1.By steam Reforming
CH4
O2
CO
H2 +
Heat
Heat
mix
Cu+(NH3)4
High Pressure
Cu+(NH3)4CO
atm P 40-50oC
CO
2.By Auto-thermal Cracking

## Slide 46
Petrochemicals
Syngas can be used to synthesize Methanol
2
2H +
CO
320-380oC / 250-350 atm
ZnO - Cr O
2 3
3
CH OH
2
2H +
CO
240-260oC / 50-100 atm
CuO - ZnO - Al O
2 3
3
CH OH
Methanol Properties:
Methanol is a colourless liquid that boils at 64.96 °C (148.93 °F) and solidifies at −93.9 °C (−137 °F). It forms explosive mixtures with air and burns with a nonluminous flame. It is completely miscible in water.
Methanol
CH3OH

## Slide 47
Petrochemicals
Importance of Methanol :
It is used as a fuel for cars and homes.
It is used as fuel in ovens, steam boilers, and in gas turbines
It is used as Solvents
Its use as an important source in the production of many chemicals required for different industries:
  50% for the formaldehyde industry
  20% for the manufacture of dimethyl terephthalate (required for the production of polyester fibers) and for the manufacture of methacrylate (necessary for the manufacture of plastics).
  30% for the manufacture of many other products such as vinegar acid and methyl chloride (used in the manufacture of silicon rubber).

## Slide 48
Petrochemicals
from Methane
Methanol
Synthesis Gas CO/H2

Formaldehyde
Acetal resin
Phenol formaldehyde resin
urea formaldehyde resin
melamine formaldehyde resin
1,4-Butandiol
Hexamethylene tetramine (HMT)
Pentaerythritol
Vinyl Acetate
Petrochemicals

## Slide 49
Synthesis of Formaldehyde from Methanol
By vapour-phase oxidation of Methanol :
Petrochemicals
CH2O | Formaldehyde
Density | 815 kg/m³
Molecular Weight/ Molar Mass | 30.031 g/mol
Boiling Point | -19 °C
Melting Point | -92.0 oC
Chemical Formula | HCHO
Formaldehyde Properties
1/ O
2 2
+
300-400oC / P
Fe2O3 / MoO3
3
CH OH
HCHO

## Slide 50
Petrochemicals
Importance of Formaldehyde
It is used in large amounts in a variety of chemical manufacturing processes:
1,4-Butanedion
6-Hexamethylene tetramine (TMT)
Pentaerythriol
Resins:
phenol formaldehyde resin Urea formaldehyde resin Melamine formaldehyde resin

## Slide 51
Petrochemicals
+ 2 HCHO
CuC2 / Bis (SiO2)2 / heat / P
H2 / Ni
HOH2C C C CH2OH
Butynediol
HOCH2CH2CH2CH2OH
1,4-Butanediol
HC CH
It is prepared by reacting formaldehyde with acetylene in the presence of a
catalyst (copper acetyl and bismuth in a SiO2 or magnesium silicate).
Its importance is highlighted in the manufacture of synthetic fibres (polyesters, elastomers and polyurethane).
It is used in the preparation of the solvent known as THC
I. Derivatives From Formaldehyde
1,4-Butandiol

## Slide 52
It is prepared by reacting ammonia with formaldehyde by 6/4 by passing ammonia inside formalin at 20-30 ◦C with stirring and evaporating the solution to get rid of water to produce the compound in the form of solid colourless crystals.
Petrochemicals
Hexamethylene tetramine (HMT)
It is used as a fungicide and the production of some pharmaceutical compounds.
I. Derivatives From Formaldehyde

## Slide 53
Petrochemicals
I. Derivatives From Formaldehyde
1,3-Pentaerythritol
It is prepared by reacting formaldehyde with acetaldehyde in aqueous
calcium hydroxide or sodium hydroxide solution at 15-45◦C.
Pentaerythritol is a building block for the synthesis and production of explosives, plastics,
alkyd paints, appliances, cosmetics , and many other commercial products.

## Slide 54
Petrochemicals
I. Derivatives From Formaldehyde
Alkyd Resins
Example
Modified Alkyd
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 55
Petrochemicals
II. Derivatives From Acetic Acid
Synthesis of Acetic acid from Methanol
It is prepared by reacting methanol with carbon monoxide (in the presence of cobalt
iodide with a traces of water as a catalyst.
3
CH OH
+ CO
3
CH COOH
CoI2
250 C / 30-40 atm

## Slide 56
50% for the production of vinyl acetate monomer.
Production of cellulose acetate (necessary for the production of synthetic fibres).
Acetic anhydride production (required for the production of aspirin).
Production of methyl acetate, isopropyl acetate, butyl acetate, acetanilide, acetyl
chloride, and acetamide.
Used as a solvent.
Petrochemicals
II. Derivatives From Acetic Acid
Importance of Acetic acid in industry& laboratories

## Slide 57
II. Derivatives From Acetic Acid
II.1 Production of Vinyl acetate
3
CH COOH
Zn(OAc)2 / Charcoal 170-260oC
Vinyl acetate
HC CH +
2
H
Petrochemicals
It is produced by the reaction of acetic acid with acetylene in the gas phase.
O
H C C O C
CH
3
3
+ 2NaCl + Pd + CH COOH
2CH3COONa
PdCl2 CH3COOH
Vinyl acetate
H2C CH2 +
2
H C
H
Or by converting acetic acid into sodium acetate that interacts with ethylene in the vinegar acid solution in the presence of palladium.
O
C O C CH3

## Slide 58
Petrochemicals
II. Derivatives From Acetic Acid
Vinyl acetate is used to produce Poly (vinyl acetate) by emulsion
polymerization, which is characterized by the following:
Colourless transparent material.
It swells in water and does not resist acids and alkalis.
It is used as an adhesive between the two layers of glass, because of its strong ability to stick to the surfaces of glass and various metals, such as the front glass of cars
It is used in the manufacture of water based paints (Latex).
Used in varnishes (surface polishing material) and paint
It is used in resin concrete.
Used in the preparation of poly (vinyl alcohol) with alcohol decomposition using
methanol with sodium methoxide.
CH3
Poly(vinyl acetate)
Poly(vinyl alcohol)
OH
H2 H H2
C C
O n
C O
H
C C
n
CH3ONa
3
CH OH
Poly (vinyl alcohol) is used in the manufacture of textile glues and adhesives.

## Slide 59
Petrochemicals
III. Derivatives From Chloromethane
Synthesis of Chloromethane from Methanol
Uses of chloromethane
It can be used for the production of dichloride, methyl chloride (chloroform) and tetrachloride. Which is used as a non-flammable -solvent - (except for chloromethane).
It is used in the production of Fluoroplastics [CF2-CF2]n

## Slide 60
Petrochemicals
polytetrafluoroethylene (PTFE).It is a plastic as well as having superb properties of heat resistance, smoothness (slipperiness), non-stick, chemical resistance, low friction and excellent electrical insulation (non-conductance).

## Slide 61
Petrochemicals
IV. Derivatives From methyl tertiary butyl ether
Synthesis of methyl tertiary butyl ether from Methanol
From the reaction of Methanol with isobutylene
Added to vehicles fuel to improve its quality instead of lead compounds.

## Slide 62
Petrochemicals
V. Derivatives From methyl amins
Synthesis of methyl amins from Methanol
Can be prepared f rom the reaction of Methanol with ammonia
Primary amines are accompanied by products of secondary and tertiary amines depending on reaction conditions and methanol : ammonia ratios.
It can be used as Intermediate substance for solvent synthesis such as; DMF & DMAc. As well as, pesticides, herbicides, pharmaceuticals and detergents

## Slide 63
Petrochemicals
VI. Derivatives From Esters
VII. Derivatives From Hydrogen cyanide
Methanol is used to produce a large number of compounds that are used in the production of plastics and synthetic fibres such as:
Methyl methacrylate
Dimethylterphthalate
Prepared from the reaction of methanol with Carbon Monoxide
It can be used to prepare chemicals for the manufacture of synthetic fibres such as; acrylonitrile and methyl methacrylate.

## Slide 64
Petrochemicals
Petrochemicals
from Methane
Methanol
Synthesis Gas CO/H2
Ammonia
Nitric acid
Compound fertilizers
Ammonium phosphate
Ammonium sulfate
Ammonium nitrate
Urea
Urea formaldehyde
Melamine
Melamine resin formaldehyde

## Slide 65
Petrochemicals
Ammonia
NH3
Ammonia is a gas that has a distinct smell and its
The Preparation of Ammonia:
boiling point −33.34 °C
N2
3H2
2NH3
Fe2O3
+
500oC/300 atm
The hydrogen can be generated from the Syngas (CO/H2) after the oxidation of CO into CO2 by using oxidation Catalyst, followed by DEA which is absorbent for Carbon dioxide .
The nitrogen is separated from the air by fractional distillation.
Ammonia
Urea

## Slide 66
Petrochemicals
1.Urea
Properties of Urea
Urea is a white crystalline material ; It’s melting point is 132.5 ◦C.
The highest nitrogen fertilizers concentrated with nitrogen 46.6%
75% of ammonia is used in the manufacture of various organic and inorganic fertilizers.
O
NH2 C NH2
Urea
Ammonia
NH3

## Slide 67
Petrochemicals
Synthesis of Urea
NH2 C NH2 + H2O 2NH3 CO2
Urea
+
The reaction of Urea with water releases ammonia and carbon dioxide
O
Selective precipitation of ammonium carbamate was achieved by reacting gaseous CO2 and NH3 . In the second step of the process the pure ammonium carbamate is used to produce urea with good yield (up to 54%)
Ammonia
NH3
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 68
Petrochemicals
Urea is used as a fertilizer - livestock feed - leather tanning
Production of Urea formaldehyde (UF) polymer or resin.
Ammonia
NH3
Usage of Urea
Two steps in formation of urea-formaldehyde resin
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 69
Petrochemicals
Ammonia
NH3
In Melamine production which is made up of (Urea+Ammonia).
Melamine formaldehyde resin
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 70
Petrochemicals
Ammonia
NH3
2.Ammonium nitrate
Used in the manufacture of fertilizers - explosives - herbicides and
insects
Other nitrates such as sodium nitrate are prepared by reacting ammonia with oxygen to give NO, CO2, then the resulting oxides interact with sodium carbonate.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 71
Petrochemicals
Ammonia
NH3
  Used in the fertilizer industry - to fight forest fires (fire extinguishers)
3.Ammonium Sulfate
Used in fertilizer industry - water treatment - to fight forest fires (fire ignition)
fire extinguishers
These fire extinguishers are pressurized with non-flammable gas. When there is a fire and we operate the extinguisher the dry chemical power, Ammonium phosphate, will form a thin layer of coating over the burning material thus cut off the oxygen smothering the fire.
Ammonium phosphate
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Ammonium Phosphate

## Slide 72
Petrochemicals
Ammonia
NH3
5.Compound Fertilizers
A fertilizer integrating 2 or 3 of the three nutrient elements in NPK
(Nitrogen, Phosphorus and Potassium) in the same compound. Ammonium polyphosphate fertilizers are NP compound fertilizers, potassium nitrate is a NK compound fertilizer, and potassium phosphate is a PK compound fertilizer.
6. Nitric Acid HNO3
75% of the production are used in fertilizers
In Production of cellulose nitrate with low viscosity resulted in fast-drying lacquer coatings, which were used extensively in automobile and furniture production.
explosives manufacturing
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 73
2-Ethyl hexanol
Petrochemicals
Hydroformyaltion is the general term applied to the reaction of an olefin with a mixture of CO and H2 (syngas) to
form aldehyde.
When substituted, terminal olefin is used both liner and branched aldehydes are formed.
The aldehyde is an important chemical intermediate. Some of the butyraldehyde is hydrogenated to n-butanol
which is used extensively as an industrial solvent. The major part of the n-butyraldehyde is converted to
2-ethylhexanol via aldol condensation and hydrogenation.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 74
2-Ethyl hexanol
Petrochemicals
Much of the 2-ethylhexanol is converted to phthalate esters which are used as plasticizers in polyvinyl chloride
PVC.
2
Dioctyl phthalate
Phthalic anhydride
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 75
Petrochemicals
It is produced industrially from methane by high temperature decomposition (pyrolysis)
Acetylene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Acetylene

## Slide 76
It is the starting material of many organic molecules
Acetylene
Petrochemicals

## Slide 77
Petrochemicals
Carbon Black
Pure black charcoal made in the form of dry powders.
Is a material produced by the incomplete combustion of heavy petroleum products such as Fluid catalytic
cracking FCC tar, coal tar , or ethylene cracking tar. Carbon black is a form of para-crystalline carbon that has a high surface-area-to-volume ratio, albeit lower than that of activated carbon. .
Carbon Black
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 78
Petrochemicals
Carbon Black
Carbon Black Usages:
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 79
Petrochemicals
Petrochemicals from Ethane and Other Distillates
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 80
Petrochemicals
Petrochemicals from other petroleum cut
Petrochemicals from Ethane
Petrochemicals from Methane
Synthesis Gas CO/H2
Methanol
Ammonia
Ethyl hexanol
Acetylene
Carbon black
Polyethylene
PolyvinylChloride
Polystyrene
Polyvinylacetate
Ethanol
Acetaldehyde
Ethylene Oxide
Acrylic Acid
Propylene
Butane
Naphtha
Toluene
Benzene
Xylene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 81
Petrochemicals
Petrochemicals from Ethane
Polyethylene
PolyvinylChloride
Polystyrene Polyvinylacetate Ethanol
Acetaldehyde Ethylene Oxide
Acrylic Acid
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 82
Ethane
CH3-CH3
Ethylene
CH2=CH2
Polyethylene
LDPE, HDPE
Ethylene oxide
Ethylene Chloride
Ethylene Benzene
Ethylene Glycol
Polyethylene Glycol
Polyvinyl Chloride PVC
Styrene
Polystyrene
Petrochemicals

## Slide 83
Petrochemicals
Ethane CH3-CH3

## Slide 84
Ethylene Production via Cracking of Ethane
Petrochemicals

## Slide 85
Petrochemicals
Ethane and other oil distillates such as propane, butane and naphtha are
converted into important compounds, aromatic compounds and olefins.
And among the olefins (ethylene - polypropylene - butadiene - isobutylene) which are considered the basic building blocks for the production of plastics - rubber - petrochemical products.
The transformation of the steam cracking process takes place and this method depends on the temperature - pressure - contact time so that the feed material is mixed from petroleum gases or oil distillates with water vapor and then the mixture is passed in ovens whose temperature rises to approximately 870oC where cracking obtaining olefins.
Ethane CH3-CH3

## Slide 86
Petrochemicals
Feeding Stream | Products |  |  |  | Total % of Ethane, Propane, butane, Gasoline & Syngas.
 | Ethylene % | Propylene % | Butadiene % | Olefins % | 
Ethane gas | 80 | 1.4 | ------ | 81.4 | 18.6
Propane gas | 45 | 14.5 | 2.7 | 62.2 | 37.8
Light Naphtha | 36.2 | 16.7 | 4.3 | 57.2 | 42.8
Heavy Naphtha | 29.8 | 14 | 4.5 | 48.3 | 51.7
Gas oil diesel | 25.7 | 13.3 | 4.2 | 43.2 | 56.8
The table: shows the percentage of olefins and other materials produced
from the steam cracking operations of the steam oil distillates.
Petrochemicals from Ethane

## Slide 87
Ethylene
CH2=CH2
Petrochemicals
Petrochemicals from Ethane

## Slide 88
Petrochemicals
When you turn ethylene gas into polyethylene (plastic). Polyethylene will have either a low or high density depending on its exposure to heat and pressure.
  Exposing the polyethylene to higher temperatures, causing and it’s molecules branch out and they become less dense. in the other hand, High density polyethylene is formed when linear polymer is formed at lower temperature and pressure.
Polyethylene is the most common plastic material in the world, and is known for its simple structure and low cost.
Polyethylene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 89
Petrochemicals
Petrochemicals
from Ethylene
Low Density Polyethylene
Its carbon chains have many long side branches
It is produced by pure ethylene polymerization under high pressure 1500-3000 atm and temperature 150-300oC in the presence of a catalyst (free radical) such as peroxides.
The molecular weight of the product is 10,000-40,000 and its average density is 0.92 at 20oC
LDPE side branches consist of the ethyl group and the butyl group in ratio 2:1.

## Slide 90
Petrochemicals
Petrochemicals
from Ethylene
High Density Polyethylene
It contains linear chains with few side branches.
These chains have the freedom to agglutinate, which increases their degree of crystallization to 90%, as well as the degree of melting.
  Molecular weight of the product is 500,000
  Produced using Philips method under low pressure and low temperature in the presence of
an effective catalyst of Chromium trioxide based on silicon dioxide.

## Slide 91
Abbreviation | HDPE | LDPE | LLDPE
Schematic Molecular Structure |  |  | 
Type of polymerization | homopolymer | homopolymer | homopolymer blended with on of α-olefins (1-butene, 1-hexene, 4- methyl-1-pentene and 1-octene)
Degree of branching | Linear Structure | Has significant numbers of short branches | Has significant numbers of long branches
Density | It has a density of 0.941-0.965g/cm3 | density of 0.91-0.925g/cm3 | 
The degree of crystallinity | High crystallinity degree of crystallinity typically in the range of 70% to 80% | Low crystallinity The degree of crystallinity is usually in the range of 40% to 55% | have a similar crystallinity as LDPE 49.9%
Melting point | 130 C | 110 C | 120 C
Flexibility | It has been the distinction of being the strongest, toughest, and least flexible of other polyethylene | It is very flexible | is the most flexible of the plastic sheeting films
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 92
Application on (LDPE/LLDPE).
Gas and water pipes
Carrier bags
Heavy duty sacks
Application on (HDPE).
Chemical drums & jerricans
Toys
HDPE
Cable
Petrochemicals
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 93
Polyvinyl Chloride PVC
Petrochemicals
It is produced from ethylene gas in several stages
(1) Treatment of ethylene with chlorine gas in the presence of FeCl3 as a catalyst at 60oC (transformed into a colourless liquid that is ethylene dichloride)
(2) The formation of vinyl chloride
Extracting the hydrogen chloride molecule in the thermal cracking unit by using coal as a catalyst
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 94
Petrochemicals
(3) Suspension polymerization
Uses of PVC:
Water Pipes:
PVC helps conserve energy and water by creating virtually leak-free pipes
Packaging
Because it is durable, dependable and light weight, flexible PVC helps packaging do its job to maintain the integrity of the products inside, including medicines.
Household Products
PVC’s affordability, durability and water resistance make it ideal for rain coats, boots and shower curtains.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 95
Petrochemicals
Polyvinylidene dichloride (PVDC)
Polyvinylidene chloride (PVDC) fibers are synthetic fibers in which the fiber-forming substance is any long chain synthetic polymer consisting of at least 80% by weight of vinylidene chloride.
They are called Saran fibers which are very resilient and has excellent chemical resistance to
many chemicals including acids, alkalis, bleaches, oils, and most organic solvents.
Is an addition polymer of vinylidene chloride.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 96
Petrochemicals
Styrene
Polystyrene
Styrene & Polystyrene Synthesis
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
“Badger Process”
Dehydrogenation at high temperature

## Slide 97
Petrochemicals
Applications and uses of Polystyrene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 98
Petrochemicals
Solid - prepared in two stages by ethylene
Poly vinylacetate
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Used in paints (latex) - as adhesives

## Slide 99
Petrochemicals
Used in paints (latex) - as adhesives
Production of Poly(vinyl alcohol) (PVA)
Poly vinylacetate
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 100
Petrochemicals
Ethanol CH3CH2OH
Liquid substance - its boiling point of 87oC
water
Ethanol synthesis:
1. By the addition of sulfuric acid to ethylene and then treat the product with
2. Then; treating ethylene with water vapor at 325oC at a pressure of 60-90 atm, then the mixture is pumped in a gaseous state to the reactor containing a catalyst of H3PO4 / Silica
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 101
Petrochemicals
Used as a solvent
It is used in many industries such as cosmetic powders – makeup industry
It is used in the manufacture of paints - cleaning materials
Preparing prescription drugs.
Preparation of a number of chemical compounds such as acetaldehyde-acetone ....
Ethanol CH3CH2OH
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Applications and uses of Ethanol

## Slide 102
Petrochemicals
Acetaldehyde
It is produced by ethylene oxidation in the presence of a catalyst
It is used in the production of many petrochemicals such as pentaerythritol - acetic acid
Pentaerythritol
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Acetic acid

## Slide 103
Petrochemicals
Ethylene oxide
Partial direct oxidation of ethylene by passing a mixture of ethylene and oxygen onto a
catalyst of silver (loaded with ammonia)
Method for Synthesis
It is used in the production of ethylene glycol - ethanol amine - acrylonitrile - glycol ethers .........
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021
Treating ethylene with chlorine and water produces chlorohydrin, which is heated with lime
water

## Slide 104
Petrochemicals
Ethylene Glycol
Ethylene glycol (EG) is an important organic compound and chemical intermediate used in a large number of industrial processes.
  Colourless liquid substance with a boiling point of 197.5oC
Physical Properties
Synthesis Methods
It is prepared by treating ethylene oxide with water in a ratio of (1: 1) in the presence of a catalyst.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 105
Ethylene glycol uses
Petrochemicals
Ethylene Glycol
It is used as Anti freeze to reduce the freezing point of water inside car coolers (melting point -15.6oC) and also reduces the evaporation losses in hot climates (high boiling point).
  It is used to thaw snow from aircraft runways
  Used in the preparation of dioxane - terephthalic acid (for the production of synthetic fibers)
  It interacts with ammonia to produce ethanol amine.
  It is used in the manufacture of crackers
  It is used in the manufacture of cosmetic products
  It is used in the manufacture of antiseptic solutions
  It is used in the manufacture of pesticides
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 106
Petrochemicals
Ethanol amine
The ratio of the products can be controlled by the stoichiometry of the reactants
Ethanol amine is a bifunctional molecule , containing both a primary amine and
is a colourless, viscous liquid with an
a primary alcohol. Ethanolamine odour reminiscent of ammonia.
Synthesis Methods
Mono-ethanolamine (MEA) is produced by treating ethylene oxide with aqueous ammonia ; the reaction also produces diethanolamine (DEA) and triethanolamine (TEA).

## Slide 107
Petrochemicals
Ethanol amine
Ethanol amine uses
TEA is used in the manufacture of soap and detergents.
Removing the acidity of natural gas.
20% of the DEA solution is added to absorb H2S of LPG at 30-40oC and H2S is separated at 120oC for re-use of the DEA.
  It is used in the production of dyes - cosmetics - ornamental materials.

## Slide 108
Petrochemicals
Acrylonitrle
Liquid substance - its boiling point 77oC
It is prepared by reacting hydrogen cyanide with ethylene oxide.
Used in the production of acrylic fibers that are used in knitting woolen clothes - blankets - carpets
It is used in the manufacture of synthetic rubber by interacting with butadiene and styrene.

## Slide 109
Petrochemicals
Acrylonitrle
It is used in the production of acrylic acid.
It is used in the production of methyl acrylate.

## Slide 110
Petrochemicals
Acrylic acid is an important polymer as raw material for many industrial and consumer products. It can numerous to apply for surface coatings, textiles, adhesives, paper treatment, baby diapers, feminine hygiene products detergents and super absorbent polymers as known (Danner et al., 1998).
Acrylic acid
Currently, most acrylic acid is obtained from the catalytic partial oxidation of ethylene.

## Slide 111
Petrochemicals
Petroleum from other Fractions (cut)
From Propylene
From Butane
From Naphtha Aromatic compounds
Poly(methylmethacrylate)
Polypropylene
Isopropyl alcohol
Acrylonitrile
Acetone
Phenol
1-Butene
2-Butene
Butadiene
Butadiene Rubber
Benzene
styrene
Phenol
Toluene
Toluene diisocyanate
Xylene
P-xylene
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 112
Petrochemicals
Polypropylene
Polypropylene is one of those rather versatile polymers out there. It serves double duty, both as a plastic and as a fiber. As a plastic it's used to make things like dishwasher-safe food containers. As a fiber, polypropylene is used to make indoor-outdoor carpeting, the kind that you always find around swimming pools and miniature golf courses.
Polypropylene can be made from the monomer propylene by Ziegler- Natta polymerization and by metallocene catalysis polymerization*.
*

## Slide 113
Petrochemicals
Poly(methyl methacrylate)
Produced from propylene in several steps
It is used in the production of plastics with optical properties and is sold under the name “Lucite” or “Plex Glass” or “Perspex” )used in making airplane windows( in addition to manufacturing lenses - artificial teeth.

## Slide 114
Petrochemicals
Acrylonitrile
Isopropyl alcohol
It is produced by adding water to propylene with the presence of sulfuric acid or a catalyst such as tungsten oxide.
It is produced by treating propylene with ammonia in the presence of oxygen and in the presence of bismuth, molybdenum or uranium as a catalyst.
It is used as a solvent and raw material in preparing acetone

## Slide 115: Synthesis
Petrochemicals
Acetone
Phenol
Uses:
It is used as a solvent
It is used in the preparation of chloroform - iodoform
It is used in nail polish remover
Synthesis

## Slide 116
1-Butene
2-Butene
Petrochemicals
Butane is used to prepare a number of petrochemical products by removing hydrogen and using suitable catalysts. These products include the following: 1-Butene, 2-Butene and Butadiene
From Butane
Ethyl methyl ketone
H2
H3C C C CH3
O
O
Maleic anhydride
O C
O
HC C
HC
O2/CuCl2/PdCl2 120oC/20 atm
MoO/VO 400oC/4.3 atm
It is used as an organic
solvent for paints and
varnishes

## Slide 117
Petrochemicals
Butadiene
Butadiene is a colourless gas with a boiling point of -4.5oC
Production of butadiene can be done by either in one of two ways:
1- Extraction
A by-product of the Naphtha steam cracker process used in the production of olefins such as ethylene and propylene.
2- Dehydrogenation from butane
Dehydrogenation of butane with two-step catalysts

## Slide 118
Petrochemicals
Butadiene
Rubber
Butadiene
Synthesis
Uses
It is used in making tires after mixing with specific proportions of styrene butadiene
rubber.
The gas is dissolved in hydrocarbon solvents and polymerized to
polybutadiene by the action of anionic or Ziegler-Natta catalysts.

## Slide 119
Petrochemicals
Naphtha is the main source for the production of aromatic compounds such as gasoline - toluene – xylene.
It is obtained by treating the naphtha with the reformate catalyst to remove sulfur by hydrogenation.
The cyclic saturated compounds and paraffinic compounds (straight-chain) are converted to the required aromatic compounds using platinum chloride and rhenium chloride as catalysts at temperatures of 430-530 ° C and pressure 8-50 atm.
Petrochemicals from Naphtha Aromatic compounds

## Slide 120: Petrochemicals from Naphtha Aromatic compounds
Petrochemicals
1- Benzene
styrene
The conversion of cyclic compounds into aromatic compound.
The conversion of paraffinic compounds (straight-chain) compounds into aromatic compound.
Chem 342, By Dr. Seham ALTERARY. 1st Semester 1443-2021

## Slide 121
Petrochemicals
I-Benzene
I-Benzene
styrene
Phenol
From
Styrene is produced by direct dehydrogenation of ethylbenzene in the presence of the dehydrogenation catalyst and steam (heat) as shown in the following reaction:
From
Oxidation of benzene to phenol with 30% H2O2 in liquid-phase was carried out

## Slide 122
Petrochemicals
II-Toluene
Toluene diisocyanate
TDI is a clear, colourless to pale
yellow liquid. MDI
yellow crystalline
solid.
is a light
There
are several forms of
TDI and
MDI, which are called isomers. The two most common TDI isomers are 2,4-TDI and 2,6-TDI. The most common isomer of MDI is 4,4'-MDI.

## Slide 123: Petrochemicals from Naphtha Aromatic compounds
Petrochemicals
III-Xylene
P-xylene
P-Xylene is oxidized to Terphthalic acid by air oxidation in the presence of cobalt as a catalyst and acetic acid medium.

## Slide 124
Bis(2-ethyl) hexyl Phthalate (Dioctyl phthalate)
2
Petrochemicals
II-Xylene
o-Xylene
O-Xylene is oxidized to Phthalic acid, the oxidation product can be converted into esters named Bis(2-ethyl) hexyl ester, which is used as a plasticizer for plastics when reacted with 2-ethyl hexanol.

## Slide 125
Petrochemicals