High Performance Liquid Chromatography

---
What is HPLC ?
It is a separation technique that involves:
Injection of small volume of liquid sample
Into a tube packed with a tiny particles (stationary phase).
Where the individual components of the sample are moved down the packed tube (column) with a liquid (mobile phase)forced through the column by high pressure delivered by the pump.
These component are separated from one another by column packing.
The separated component are detected at the exit of the column by flow through detector that measure their amount.

---
Theory :
Depending on the HPLC mode , there are different types of the adsorption forces :
Hydrophobic (non-specific) interaction in reversed phase.
Dipole-dipole (polar) interaction in normal phase.
Ionic interaction in the ion exchange chromatography.
separation of mixture by the molecular size of component in Size exclusion chromatography.

---
Types of HPLC:
Classification based on the nature of the stationary phase and separation process:
a-Adsoption chromatography:
The stationary phase is an adsorbent (like silca gel).
Separation based on repeated adsorption- adsorption steps.

---
b- ion exchange chromatography:
The stationary bed has an ionically charged surface of opposite charged to the sample ions.
The stronger the charge on the sample the stronger it will be attracted to the ionic surface the longer it will take to elute.

---
C-Size exclusion chromatography:
The column filled with material having controlled pore sizes.
Larger molecules are rapidly washed through the column.
smaller molecules penetrate inside the porous of packing particles and elute later.

---
Normal and reversed phase chromatography:
Normal phase :
The stationary bed is strongly polar in nature (e.g : silica gel).
The mobile phase is non polar.
Polar samples are retained on the polar surface of the column packing for longer , than less polar material.

---
Reversed phase chromatography:
The stationary phase is (non polar )in nature .
The mobile phase is a polar liquid.
The more non polar the material is , the longer it will be retained.(water & methanol or acetonitrile).

---
Instrumental HPLC system:
1-mobile phase reservoir.
2-pumping.
3-injector.
4-column.
5-detector.
6-Data system.
reservoir

---
  APPLICATION:
Qualitative/quantitative analysis of nucleic acid , amino acid and protein in physiological sample.
Measuring level of active drug and degradation product in pharmaceutics.
Measuring level of hazardous compound.
Monitoring environmental sample.
Purifying compounds from mixture.

---
HPLC chromatogram:

---
HPLC parameters:
Dead volume
Retention volume( VR )
Retention time ( tR )
Void time ( t0 )
Capacity factor(k)
Selectivity ()
Efficiency
Resolution (R)
Peak symmetry factor (s)

---
Dead volume
is the total volume of the liquid phase in the chromatographic column.
V₀ = Vcolumn – Vpartical + Vpores
V₀ = 0.65 ( π D 2 L / 4 )
where dead volume equal 65% of empty column volume

---
Retention Volume:
Total volume of eluent (in ml) require to elute certain substance.
The eluent is the "carrier" portion of the mobile phase.
VR = tR x F

---
Retention time:
Time from injection point to maximum detector response for corresponding compound.
Qualitative analysis.
Affected by temperature, flow rate , column and mobile phase.

---
Void Time:
Time require for non retarine substance to pass through the column.

---
Peak symmetry:

---
Capacity factor
Use to describe the migration rat of solutes on columns
K = (tR – t0) / t0
.(Recommended to be (2 - 10