## Slide 1: سبر 1213 Network Defense 4 Part 3#Lecture Securing Your Network
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1

## Slide 2
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Remote Access
VPNs and VPN concentrators

## Slide 3
Tunneling Protocols
text
-
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
IPsec as a tunneling protocol
  Authentication
    AH provides authentication &integrity (protocol ID 51)
  Encryption
    ESP adds confidentiality (protocol ID 50)
      Uses tunnel mode for VPNs with IKE over port 500
TLS as a tunneling Protocol
  Useful when VPN go through NAT
  SSTP uses TLS over port 443

## Slide 4
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Site-to-Site VPNs
Gateways as VPN servers

## Slide 5
Always-On VPNs
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Site-to-site VPNs
Regular VPNs for users
Mobile devices

## Slide 6
Tunneling Protocols
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
L2TP
  not used by itself for VPN traffic
HTML5 VPN Portal
  allows users to connect to the VPN using their web browser

## Slide 7
Network Access Control
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Health agents
  Inspects clients for predefined conditions
  Restricts access of unhealthy clients to a remediation network
  Used for VPN clients and internal clients

## Slide 8: NAC Agents
-
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Permanent (Agent)
  Installed on client and remains on
  client
  Persistent NAC agent
Dissolvable (Agentless)
  Does not stay on client
  Downloaded to client when session
  starts
  Removed during or after session
  Commonly used for mobile devices

## Slide 9
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Identity and Access Services
PAP – Sends passwords in cleartext
CHAP – uses shared secret
TACACS+
  Cisco alternative to RADIUS
  Uses TCP port 49
  Encrypts entire authentication process
  Uses multiple challenges and responses

## Slide 10
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Identity and Access Services
RADIUS

## Slide 11
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
AAA Protocols
Provide authentication, authorization, and accounting
  Authentication verifies a user’s identification
  Authorization provides access
  Accounting tracks user access with logs

## Slide 12
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
From Appendix C – Table 1

## Slide 13
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
From Appendix C – Table 2

## Slide 14
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1
Chapter 4 Summary
Exploring Advanced Security Devices
Securing Wireless Networks
Understanding Wireless Attacks
Using VPNs for Remote Access
Check out the free online labs

## Slide 15: End of Part Three
King Saud University – Applied Studies and Community Service –سبر 1213 - اسم المقررLecture 1