## Slide 1: Experiment 5 Thermal conductivity measurement
Shereef Sadek
ME 322

## Slide 2: Experiment 5 Thermal conductivity measurement
What is Heat?
  Heat is the form of energy that is transferred across the boundary of a system at a given temperature to another system at a lower temperature by virtue of the temperature difference between the two systems.
  Heat is only defined at the boundary of a system. It is defined as energy being transferred across the system boundary. The term Heat Transfer is meant to describe this process.
Units of Heat
  It is measured in British Thermal Unit (BTU): Quantity of heat required to raise the temperature of 1 lbm of water by 1 F at a reference temperature.
  Or the amount of heat required to raise the temperature of 1 g of water by 1 C at a reference temperature

## Slide 3: Experiment 5 Thermal conductivity measurement
The symbol denotes the amount of heat transfer
The rate of heat transfer is denoted by
Usually we are interested in the heat transfer per unit area, heat flux ,
There are three modes of heat transfer: conduction, convection and radiation.
In real life all three modes are present at the same time. However, we are interested in conduction only.

## Slide 4: Experiment 5 Thermal conductivity measurement
Conduction heat transfer occurs due to molecular motion within the material
Since heat transfer is related to temperature difference, hence it depends on the temperature distribution within the material
We can relate the heat transfer to the temperature gradient using Fourier Law,
,
  Where is the rate of heat transfer through the area A in the x-direction measured in
  is the heat flux in the x-direction measured in
  is the Thermal Conductivity of the material measured in (
  is the temperature gradient across the material in the x-direction measured in

## Slide 5: Experiment 5 Thermal conductivity measurement
Across any section the heat transfer depends on the section area, however the heat flux only depends on the temperature gradient.
The thermal conductivity is a material property, the determination of its value for copper is the objective of this experiment.

## Slide 6: Experiment 5 Thermal conductivity measurement
Consider a constant cross-section bar
We can write,
Where, are the bar density, specific heat capacity and internal heat source, respectively.

## Slide 7: Experiment 5 Thermal conductivity measurement
Consider a constant cross-section bar
At steady state, , and in the case there are no internal heat sources we get
Hence the heat flow is constant along x, .

## Slide 8: Experiment 5 Thermal conductivity measurement
Consider a constant cross-section bar
Integrating from
Then
If , then
The value of the constant c is calculated from the boundary conditions and is equal to Q.

## Slide 9: Experiment 5 Thermal conductivity measurement
Consider a constant cross-section bar
  What if the area is variable?
  For a tapered cylinder the diameter is given by
  Then the area is given by