## Slide 1: Chapter 27
Examples

## Slide 2
Ex. 1. A copper wire in a typical residential building has a cross-sectional area of 3.31x 106 m2. If it carries a current of 10.0 A, what is the drift speed of the electrons? Assume that each copper atom contributes one free electron to the current. The density of copper is 8.95 g/cm3. (Atomic mass of cupper is 63.5 g/mol.
# Recall that 1 mol of any substance contains Avogadro’s number of atoms (6.02x 1023). Knowing the density of copper 8.95 g/cm3, we can calculate the volume occupied by 63.5 g (≡ 1mol) of copper:

## Slide 3
Vd = I / n q A
10 / (8.49 x 10 28 m-3 )(1.6 x 10 -19 C)(3.31 x 10 -6 m-2)
= 2.22 x 10 -4 m/s

## Slide 4
Ex. 2 Calculate the resistance of an aluminum cylinder that is 10.0 cm long and has a cross-sectional area of 2.0x 10-4 m2. Repeat the calculation for a cylinder of the same dimensions and made of glass having a resistivity of 3x1010 Ω

## Slide 6
(Ex 3.a) Calculate the resistance per unit length of a 22-gauge Nickle Chrome wire, which has a radius of 0.321 mm.
(Ex 3.b) If a potential difference of 10 V is maintained across a 1.0-m length of the Nickle Chrome wire, what is the current in the wire?

## Slide 7
I = DV/ R = 10 V / 4.6  = 2.2 A

## Slide 8
Ex. 6. A resistance thermometer, which measures temperature by measuring the change in resistance of a conductor, is made from platinum and has a resistance of 50.0 Ω at 20.0°C. When immersed in a vessel containing melting indium, its resistance increases to 76.8 . Calculate the melting point of the indium.
R = Ro[1 + α(T - To)]
a = 3.92 x 10-3 C-1

## Slide 9
Ex. 7 An electric heater is constructed by applying a potential difference of 120 V to a Ni-chrome wire that has a total resistance of 8.0 Ω . Find the current carried by the wire and the power rating of the heater.

## Slide 10
If we doubled the applied potential difference, the current would double but the power would quadruple because

## Slide 11
Ex. 8 Estimate the cost of cooking a turkey for 4 h in an oven that operates continuously at 20.0 A and 240 V.