## Slide 1
Digital Signal
Continuous time
Continuous amplitude
Discrete time
Continuous amplitude
Discrete time
Discrete amplitude
Analog Signal
Discrete-time Signal
Digital Signal

## Slide 2
Analog Signal
Discrete-time Signal
Digital Signal
Digital Signal – contd.

## Slide 3
A digital signal processing scheme
DSP (Digital Signal Processing)
To avoid aliasing for sampling
Analog to Digital Converter
Digital to Analog Converter
To avoid aliasing for sampling
Computer / microprocessor / micro controller/ etc.

## Slide 4
Some Applications of DSP
Noise removal from speech.
Noisy Speech
Clean Speech

## Slide 5
Some Applications of DSP
Signal spectral analysis.
Time domain
Frequency domain
Single tone: 1000 Hz
Double tone: 1000 Hz and 3000 Hz

## Slide 6
Some Applications of DSP
Noise removal from image.

## Slide 7
Some Applications of DSP
Image enhancement.

## Slide 8
Summary Applications of DSP
Digital speech and audio:
Speech recognition
Speaker recognition
Speech synthesis
Speech enhancement
Speech coding
Digital Image Processing:
Image enhancement
Image recognition
Medical imaging
Image forensics
Image coding
Multimedia:
Internet audio, video, phones
Image / video compression
Text-to-voice & voice-to-text
Movie indexing
……..

## Slide 9
For a given sampling interval T, which is defined as the time span between two sample points, the sampling rate is given by
samples per second (Hz).
For example, if a sampling period is T = 125 microseconds, the sampling rate is
determined as fs =1/125 s or 8,000 samples per second (Hz).
Sampling
Sample and Hold

## Slide 10
Sampling - Theorem
Freq. = 2 / 23
Freq. = 7 / 23
Freq. = 22/ 23

## Slide 11
Sampling - Theorem
The sampling theorem guarantees that an analog signal can be in theory perfectly recovered as long as the sampling rate is at least twice as large as the highest-frequency component of the analog signal to be sampled.
The condition is:
For example, to sample a speech signal containing frequencies up to 4 kHz, the minimum sampling rate is chosen to be at least 8 kHz, or 8,000 samples per second.

## Slide 12
Sampling - Theorem
Sampling interval T= 0.01 s
Sampling rate fs= 100 Hz
Sinusoid freq. = 4 cycles / 0.1 = 40 Hz
Sampling condition is satisfied, so reconstruction from digital to analog is possible.
Do this by yourself!

## Slide 13
Sampling Process
x(t): Input analog signal
p(t): Pulse train

## Slide 14
Sampling Process
In frequency domain:
Xs(f): Sampled spectrum
X(f): Original spectrum
X(fnfs): Replica spectrum

## Slide 15
Sampling Process
Original spectrum
Original spectrum plus its replicas
Original spectrum plus its replicas
Original spectrum plus its replicas
Reconstruction not possible
Minimum requirement for Reconstruction

## Slide 16
Shannon Sampling Theorem
For a uniformly sampled DSP system, an analog signal can be perfectly recovered as long as the sampling rate is at least twice as large as the highest-frequency component of the analog signal to be sampled.
Half of the sampling frequency fs/2 is usually called the Nyquist frequency
(Nyquist limit), or folding frequency.

## Slide 17
Problem:
Example 1
Solution:
Using Euler’s identity,
Hence, the Fourier series coefficients are:

## Slide 18
Example 1 – contd.
a.
b.
After the analog signal is sampled at the rate of 8,000 Hz, the sampled signal spectrum and its replicas centered at the frequencies nfs, each with the scaled amplitude being 2.5/T
Replicas, no additional information.

## Slide 19
Signal Reconstruction
First, the digitally processed data y(n) are converted to the ideal impulse train ys(t), in which each impulse has its amplitude proportional to digital output y(n), and two consecutive impulses are separated by a sampling period of T;
second, the analog reconstruction filter is applied to the ideally recovered sampled signal ys(t) to obtain the recovered analog signal.

## Slide 20
Signal Reconstruction

## Slide 21
Signal Reconstruction
Perfect reconstruction is not possible, even if we use ideal low pass filter.
Aliasing

## Slide 22
Example 2
Problem:
Solution:
Using the Euler’s identity:

## Slide 23
Example 2 – contd.
a.
b.
The Shannon sampling theory condition is satisfied.

## Slide 24
Example 3
Problem:
Solution:
a.
b.

## Slide 25
Quantization
L: No. of quantization level
m: Number of bits in ADC
: Step size of quantizer
i: Index corresponding to binary code
xq: Quantization level
xmax: Max value of analog signal
xmin: Min value of analog signal
Example:
Unipolar

## Slide 26
Quantization – contd.
Bipolar

## Slide 27
Example 4
Problem:
Solution:
a.
b.
c.
101
d.
Quantization error: