| Question # 1 The resultant of the cable forces and has a magnitude of 900 N and its line of action has an angle of 30° with x-axis as shown in the figure. Determine the magnitude of and forces. |  |
| --- | --- |
| Question # 2 A rectangular plate of 1 m × 2 m is subjected to six forces as shown in the figure. If the moment of these forces about point A is 50 N.m (Clockwise), then calculate the magnitude of the force P. |  |
| Question #3 For the force system shown in the figure, replace the given system of forces by a single resultant force R. and find its intersections with x and y axes measured from point O and sketch it. |  |
| Question # 4 For the given force of 2 kN, determine in a vector form (i) Moment about the point O (MO) (ii) Moment about the point A (MA) (iii) Moment about the line OD (MOD) (iv) Moment about the x-axis (Mx) |  |
| Question # 5 Determine the resultant of the system of forces and couple shown in the figure. Assume that the resultant will be applied at O. |  |

# Text boxes

King Saud University							GE 201 Statics

College of Engineering							Summer Semester 1436-37 H

Department of Civil Engineering

30°

30°

45°

45°

45°

30°

45°

10 N

10 N

10 N

P

P

45°

A

B

C

D

E

F

1 m

1 m

1 m

10 N

B

z

O

D

C

0.4 m

0.5 m

0.2 m

0.2 m

2 kN

0.25 m

0.2 m

y

x

A