King Saud University

College of Computer and Information Sciences

Department of Computer Engineering

CEN 521 – Advanced Computer Architecture

Semester II, Academic Year 2018-2019

Dr. Musaed A. Alhussein

Homework 2

Problem 1:  Bits in  a Cache

- How many total bits are required for a direct-mapped cache with 64KB of data and 16-word blocks, assuming a 32-bit address?

- Show the portions of an address in this mapping, by showing Tag, Index …etc fields, with the width of each field (i.e. number of bits of each field).

Problem 2:  Missed and Associativity in Caches

Consider a small cache consisting of a total size of 16 words, configured as direct mapped with two-word blocks. Show the hits and misses and final cache contents given the following sequence of word addresses:    6,  214,  175,  214,  6,  84,  65,  174,  64,  105,  85,  215

Problem 3:  Missed and Associativity in Caches

Assume there are two small caches, each consisting of a total size of 16 words:

Cache 1: Direct-mapped with one-word blocks

Cache 2: Direct-mapped with four-word blocks

Show the hits and misses and final cache contents for each cache organization given the following sequence of word addresses:    2, 3, 11, 16, 21, 13, 64, 48, 19, 11, 3, 22, 4, 27, 6 , 11