## Slide 1: Routing and routing tables
2nd semester 1437-1438

## Slide 2: From Lab2 Slides
Our lecture today

## Slide 3: Objectives
Explain how routers use information in data packets to make forwarding decisions
Explain the encapsulation and de-encapsulation process used by routers when switching packets between interfaces
Compare ways in which a router builds a routing table when operating in a small to medium-sized business network.
Explain routing table entries for directly connected networks.
Explain how a router builds a routing table of directly connected networks.
Explain how a router builds a routing table using static routes.
Explain how a router builds a routing table using a dynamic routing protocol.

## Slide 4: Sending a Packet
A host could send a packet to: itself, local host, or remote host
router
Notes: Itself - This is a special IP address of 127.0.0.1 which is referred to as the loopback interface. This loopback address is automatically assigned to a host when TCP/IP is running. The ability for a host to send a packet to itself using network functionality is useful for testing purposes. Any IP within the network 127.0.0.0/8 refers to the local host.
The main role of the network layer is to move packets from a sending host to a receiving host.

## Slide 5: Router
Routers connect multiple networks.
It have multiple interfaces, each on a different IP network.
It is responsible for the routing of traffic between networks.
Notes: 5
Function of a Router
4.1.1.2 Why Routing?

## Slide 6: Functions of a Router
To do so, router does two important functions:
Create routing tables which supply a wealth of information about paths to other networks (Routing)
  It helps to determine the best path to send packets
Forward packets toward their destination (Forwarding)
Forwards packet to interface indicated in routing table.
Encapsulates the packet and forwards out toward destination.
Notes: Forwarding: When a packet arrives at a router’s input link, the router must move the packet to the appropriate output link .
Routing: The network layer must determine the best route or path taken by packets as they flow from a sender to a receiver.

## Slide 7: Packet Forwarding Decision
Every router has a routing table. To forward a packet, a router:
Notes: Depending on the network-layer protocol, the header value could be the destination address of the packet or an indication of the connection to which the packet belongs.
  Examining the value of a field in the arriving packet’s header
  Then using this header value to index into the router’s routing table.
  The value stored in the routing table entry for that header indicates the router’s outgoing link interface to which that packet is to be forwarded.

## Slide 8: Router Packet Forwarding Decision
Router either forwards packets to directly connected or remote networks

## Slide 9: Forwarding

## Slide 10: Router Switching Function
A switching function is a process used by a router to accept a packet on one interface and forward it out of another interface.
Notes: As we know, the primary function of a router is to forward packets toward their destination.
This is accomplished by using a switching function, which is the process used by a router to accept a packet on one interface and forward it out of another interface.

## Slide 11: Switching Packets between Networks Router Switching Functions
A key responsibility of the switching function is to encapsulate packets in the appropriate data link frame type for the outgoing data link.
Notes: 11
4.2.1 Switching Packets between Networks
4.2.1.1 Router Switching Functions
Note: In this context, the term “switching” literally means moving packets from source to destination and should not be confused with the function of a Layer 2 switch.

## Slide 12: Switching Packets between Networks Send a Packet
Notes: 12
4.2.1 Switching Packets between Networks
4.2.1.2 Send a Packet

## Slide 13: Switching Packets between Networks Forward to the Next Hop
?
?
MAC
MAC
type
Notes: 13
4.2.1 Switching Packets between Networks
4.2.1.3 Forward to the Next Hop

## Slide 14: Switching Packets between Networks Packet Routing
Notes: 14
4.2.1 Switching Packets between Networks
4.2.1.4 Packet Routing

## Slide 15: Switching Packets between Networks Reach the Destination
Notes: 15
4.2.1 Switching Packets between Networks
4.2.1.5 Reach the Destination
4.2.1.6 Activity – Match Layer 2 and Layer 3 Addressing

## Slide 16: Activity
Pc1 want send a packet to Pc2, fill the required addresses that Pc1 will use to send the packet

## Slide 17: Forwarding Decisions
Notes: 17
4.2.2 Path Determination
4.2.2.1 Routing Decisions

## Slide 18: Routing

## Slide 19: The Routing Table
routing table !
Notes: 19
Functions of a Router
4.1.1.5 Routers Choose Best Paths

## Slide 20: The Routing Table
Routing Table is a file stored in RAM that contains information about
  Directly connected networks
  Remote networks
  Network or next hop associations
What if there are many paths
to a remote network
Notes: 20
4.3 Router Operation
4.3.1 Analyze the Routing Table
4.3.1.1 The Routing Table

## Slide 21: Routers Choose Best Paths
Routing table store the best path
  Determine the best path to send packets to remote networks
Routers use static routes and dynamic routing protocols to learn about remote networks and build their routing tables.
How a router learns about remote networks and finds the best path
Notes: 21
Functions of a Router
4.1.1.5 Routers Choose Best Paths

## Slide 22: Best Path
Best path is selected by a routing protocol based on the values or metrics of paths.
A metric is the value used to measure the distance to a given network.
Best path to a network is the path with the lowest metric.
Notes: 22
4.2.2 Path Determination
4.2.2.2 Best Path

## Slide 23: Best Path
Dynamic routing protocols use their own rules to assign metrics:
  Routing Information Protocol (RIP) - Hop count
  Open Shortest Path First (OSPF) - Cost based on cumulative bandwidth from source to destination
  Enhanced Interior Gateway Routing Protocol (EIGRP) - Bandwidth, delay, load, reliability

## Slide 24: Load Balancing
When a router has two or more paths to a destination with equal cost metrics, then the router forwards the packets using both paths equally.
Notes: 24
4.2.2 Path Determination
4.2.2.3 Load Balancing

## Slide 25: Administrative Distance
If multiple paths to a destination are configured on a router, the path installed in the routing table is the one with the best Administrative Distance (AD).
Administrative Distance is the “trustworthiness”
The Lower the AD the more trustworthy the route.
Notes: 25
4.2.2 Path Determination
4.2.2.4 Administrative Distance

## Slide 26: The Routing Table Routing Table Sources
show ip route command is used to display the contents of the routing table
  Local rote Interfaces –Added to the routing table when an interface is configured. (displayed in IOS 15 or newer)
  Directly connected interfaces -Added to the routing table when an interface is configured and active.
  Static routes - Added when a route is manually configured and the exit interface is active.
  Dynamic routing protocol - Added when EIGRP,OSPF, … are implemented and networks are identified.
Notes: 26
4.3 Router Operation
4.3.1 Analyze the Routing Table
4.3.1.2 Routing Table Sources

## Slide 27: The Routing Table Routing Table Sources
Notes: 27
4.3 Router Operation
4.3.1 Analyze the Routing Table
4.3.1.2 Routing Table Sources

## Slide 28: IPv4 Router Routing Table
R1#show ip route
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
D 10.1.1.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
D 10.1.2.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
192.168.10.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
L 192.168.10.1/32 is directly connected, GigabitEthernet0/0
192.168.11.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
L 192.168.11.1/32 is directly connected, GigabitEthernet0/1
209.165.200.0/24 is variably subnetted, 2 subnets, 3 masks
C 209.165.200.224/30 is directly connected, Serial0/0/0
L 209.165.200.225/32 is directly connected, Serial0/0/0
R1#
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: 6.2.2.2 IPv4 Router Routing Table

## Slide 29: Router Routing Tables Directly Connected Routing Table Entries
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
L 192.168.10.1/32 is directly connected, GigabitEthernet0/0
A
B
C
A | Identifies how the network was learned by the router.
B | Identifies the destination network and how it is connected.
C | Identifies the interface on the router connected to the destination network.
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
64.100.0.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: 6.2.2.3 Directly Connected Routing Table Entries

## Slide 30: Router Routing Tables Remote Network Routing Table Entries
D 10.1.1.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
A | Identifies how the network was learned by the router.
B | Identifies the destination network.
C | Identifies the administrative distance (trustworthiness) of the route source.
D | Identifies the metric to reach the remote network.
E | Identifies the next hop IP address to reach the remote network.
F | Identifies the amount of elapsed time since the network was discovered.
G | Identifies the outgoing interface on the router to reach the destination network.
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
64.100.0.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: 6.2.2.4 Remote Network Routing Table Entries

## Slide 31: Directly Connected Routes Directly Connected Interfaces
A newly deployed router, without any configured interfaces, has an empty routing table.
RTA#show ip route
Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, * - candidate default
U - per-user static route, o - ODR
Gateway of last resort is not set
RTA#
Currently, no routes in the routing table.

## Slide 32: Directly Connected Routes Directly Connected Interfaces
An active, configured directly connected interface creates two routing table entries Link Local (L) and Directly Connected (C)
4.3.2.2
Notes: 32
4.3 Router Operation
4.3.2 Directly Connected Routes
4.3.2.2 Directly Connected Route Table Entries

## Slide 33
Configuring an interface
Adding an ip address/mask to an interface tells the router that it is a member, “Directly Connected” to that network
Notice the route is shown with the subnet mask and the “exit-interface.”
Don’t forget the “no shutdown”
Don’t forget the interface must be in “up” and “up”
Directly Connected Networks and the IP Routing Table
RTA(config)#inter e 0
RTA(config-if)#ip add 192.168.2.1 255.255.255.0
RTA(config-if)#no shutdown
RTA#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
C 192.168.2.0/24 is directly connected, Ethernet0
RTA#

## Slide 34
Viewing the Routing Table Process
Use the “debug ip routing” command to view the Cisco IOS routing table process of adding a directly connected network to the routing table.
When finished, be sure to use “undebug all”
Debug commands are used to view detailed information about Cisco IOS processes – more later.
Directly Connected Networks and the IP Routing Table
RTA# debug ip routing
RTA(config)#inter e 0
RTA(config-if)#ip add 192.168.2.1 255.255.255.0
RTA(config-if)#no shutdown
00:28:56: RT: add 192.168.2.0/24 via 0.0.0.0, connected metric [0/0]
00:28:56: RT: interface Ethernet0 added to routing table
RTA#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
C 192.168.2.0/24 is directly connected, Ethernet0
RTA# undebug all

## Slide 35
Viewing the Routing Table Process
Directly connected routes will also be removed if the link goes down.
Directly connected routes will only be in the routing table if, it is not administratively down, the line is “up” and protocol is “up”
For serial interfaces, don’t forget the “clock rate” command on the router with the DCE cable – neither interface will be “up” and “up” until both ends are configured correctly.
Directly Connected Networks and the IP Routing Table
RTA# debug ip routing
RTA(config)#inter e 0
RTA(config-if)#shutdown
00:34:38: RT: interface Ethernet0 removed from routing table
00:34:38: RT: del 192.168.2.0 via 0.0.0.0, connected metric [0/0]
00:34:38: RT: delete network route to 192.168.2.0
RTA#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
RTA# undebug all

## Slide 36
Directly Connected Networks and the IP Routing Table
RTA#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
C 172.16.0.0/16 is directly connected, Serial0
C 192.168.2.0/24 is directly connected, Ethernet0
RTB#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
C 172.16.0.0/16 is directly connected, Serial0
C 192.168.1.0/24 is directly connected, Serial1
RTC#show ip route
Codes: C - connected,.. <Other codes and gateway information omitted>
C 10.0.0.0/8 is directly connected, Ethernet0
C 192.168.1.0/24 is directly connected, Serial1
The Routing Tables
Notice that the routers only know about their own directly connected networks.
They are not sharing routing information because we have not configured any static routes or dynamic routing protocols.

## Slide 37
Routing – Only directly connected hosts (routers)
Routers can only reach networks known about in its own routing table.
Directly Connected Networks and the IP Routing Table
RTA#show ip route
C 172.16.0.0/16 is directly connected, Serial0
C 192.168.2.0/24 is directly connected, Ethernet0
RTA#ping 172.16.0.1
Sending 5, 100-byte ICMP Echos to 172.16.0.1, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 56/57/60 ms
RTA#ping 172.16.0.2
!!!!!
RTA#ping 192.168.1.1
.....
RTA#ping 192.168.1.2
.....
RTA#ping 10.1.0.1
.....

## Slide 38: Routing and Forwarding Outline