## Slide 1: Laboratory Acquired Infections
CLS 416

## Slide 2: Routes of Lab. Acquired infections
Route
Accidental inoculation:
Pricking & cutting skin
Lab. Animal injury
Accidental ingestion:
mouth pipetting
eating, drinking, smoking
Splashing into face & eye
Organisms
HB. virus, TB, syphilis, S.aureus
Brucella spp,
Typhus, equine encephalitis, cat scratch fever, tetanus, Rabies
S. typhi, Shigella spp., scarlet fever, HAV,
Brucella spp., vibrio cholerae, Polio
Toxoplasma, Brucella, relapsing fever,
adenoviruses

## Slide 3: Routes of Lab. Acquired infections
Route
Spilage & diretct contact,
cuts & abrasion--------blood
hand--------mouth or eye
Aerosoles, droplet inhalation
Open containers & lyophilized cultures, cap removal, test tube mixing, (surface contamination, size>0.1mm)
High speed blenders, pipette mix,
pipette spills & transfr, decanting
bunsen burner.(droplet inhalation
size <0.1mm)
Organisms
As 1------3
Influenza virus, brucellosis, TB
Q- fever, Anthrax, Tularemia,
Pulmonary mycosis.

## Slide 5: Agents in each Risk Group
Risk Group I
Risk Group II
Risk Group III
Risk Group IV
Food spoilage bacteria,
common molds & yeasts.
Staphylococci, streptococci, Enterobacteria
except S.typhi, clostridia, vibrios, polio virus,
adenoviruses, coxackievirus, hepatitis virus,
blastomyces, toxoplasma, leishmania
brucella, S.typhi, TB, francisella, Y. pestis,
rickettsiae, chlamydia, coccidiodes, HIV,
histoplasma, arboviruses.
Small pox, arboviruses, haemorrhagic viruses
as lassa, marburg & ebola viruses. equine &
other encephalitis viruses.

## Slide 6: Types of safety cabinets

## Slide 7: Types of safety cabinets

## Slide 9: Classification of Laboratories
Basic Laboratories
(Risk groups I & II organisms)
Containment Laboratories
(Risk group III organisms)
Maximum Containment Laboratories
(Risk group IV organisms)