## Slide 1
Lecture 3
Computer Networks Management
Standards, Models and Language
Dr. Mostafa H. Dahshan
Department of Computer Engineering
College of Computer and Information Sciences
King Saud University
mdahshan@ksu.edu.sa
Edited By Maysoon AlDuwais

## Slide 2
Overview
• SMI Data Definition Language
• ASN.1 language
• Basic encoding rule
• Management application functions

## Slide 3: SMI Structure Of Management Information
  SMI is a data definition language for MIB objects
Purpose: well-defined, unambiguous syntax and semantics of mgmt data
Base data types:
  straightforward, boring
OBJECT-TYPE
  standard type of managed info defines data structure, semantics of managed object, including status
MODULE-IDENTITY
  groups related objects into a MIB module
Basic Data Types
INTEGER
Integer32
Unsigned32
OCTET STRING
OBJECT IDENTIFIED
IpAddress
Counter32
Counter64
Gauge32
TimeTicks
Opaque

## Slide 4
SNMP MIB
OBJECT TYPE:
OBJECT TYPE:
OBJECT TYPE:
objects specified via SMI
OBJECT-TYPE construct
MIB module specified via SMI
MODULE-IDENTITY
(100 standardized modules, more vendor-specific)
MODULE

## Slide 5: SNMP MIB Object
    object ID unique ID
    and descriptor and name for the object
    syntax used to model the object
    access access privilege to a managed object
    status implementation requirements
    definition textual description of the semantics of object type

## Slide 6: SMI: Object, module examples
OBJECT-TYPE: ipInDelivers
MODULE-IDENTITY: ipMIB
ipInDelivers OBJECT TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION
“The total number of input
datagrams successfully
delivered to IP user-
protocols (including ICMP)”
::= { ip 9}
ipMIB MODULE-IDENTITY
LAST-UPDATED “941101000Z”
ORGANZATION “IETF SNMPv2
Working Group”
CONTACT-INFO
“ Keith McCloghrie
……”
DESCRIPTION
“The MIB module for managing IP
and ICMP implementations, but
excluding their management of
IP routes.”
REVISION “019331000Z”
………
::= {mib-2 48}

## Slide 7: MIB example: UDP module
Object ID Name Type Comments
1.3.6.1.2.1.7.1 UDPInDatagrams Counter32 total # datagrams delivered
at this node
1.3.6.1.2.1.7.2 UDPNoPorts Counter32 # underliverable datagrams
due to no app at port
1.3.6.1.2.1.7.3 UDInErrors Counter32 # undeliverable datagrams
all other reasons
1.3.6.1.2.1.7.4 UDPOutDatagrams Counter32 # datagrams sent
1.3.6.1.2.1.7.5 udpTable SEQUENCE one entry for each port
in use by app, gives port #
and IP address

## Slide 8: Why do we need ASN.1? What is the presentation problem?
The Presintation Problem:
Q: does perfect memory-to-memory copy solve “the communication problem”?
A: not always!
problem: different data format, storage conventions
struct {
char code;
int x;
} test;
test.x = 259;
test.code=‘a’
a
00000001
00000011
a
00000011
00000001
test.code
test.x
test.code
test.x
host 1 format
host 2 format

## Slide 9: Solving the presentation problem (The solution: ASN.1)
1. Translate local-host format to host-independent format
2. Transmit data in host-independent format
3. Translate host-independent format to remote-host format
aging 60’s
hippie
2007 teenager
grandma

## Slide 10
Abstract Syntax Notation One (ASN.1)
ASN.1 is a language that defines the syntax of messages to be exchanged between peer applications independently of local representation.
• Addresses both syntax and semantics
• Two types of syntax
• Transfer syntax: set of rules for communicating information between systems
• Makes application layer protocols independent of lower layer protocols
• Can generate machine-readable code
• Basic Encoding Rules (BER) is used in management modules
34
  Abstract syntax: set of rules that specify data type and structure for information storage

## Slide 11: ASN.1 & BER in the OSI model

## Slide 12
Backus-Naur Form (BNF)
• Definition:
• <name> ::= <definition>
• Rules:
• <digit> ::= 0|1|2|3|4|5|6|7|8|9
• <number> ::= <digit> | <number> <digit>
• <op> ::= +|-|x|/
• <SAE> ::= <number>|<SAE>|<SAE><op><SAE>
• Example:
• 9 is primitive 9
• 19 is construct of 1 and 9
• 619 is construct of 6 and 19

## Slide 13
Backus-Nauer Form (BNF)
• BNF is used for ASN.1 constructs
• Constructs developed from primitives
• The above example illustrates how numbers are constructed from the
primitive <digit>
• Simple Arithmetic Expression entity (<SAE>) is constructed from the
primitives <digit> and <op>

## Slide 14
Simple Arithmetic Expression
• <SAE> ::= <number> | <SAE><op><number>
• Example: 26 = 13 x 2
• Constructs and primitives

## Slide 15
Type and Value
• Assignments
• <BooleanType> ::= BOOLEAN
• <BooleanValue> ::= TRUE | FALSE
• ASN.1 module is a group of assignments
person-name Person-Name::=
{
first "John",
middle “ T",
last "Smith“
}

## Slide 16
Data Type: Example 1
PersonnelRecord ::= SET {
name,
title GraphicString,
division CHOICE {
marketing SEQUENCE {Sector, Country},
research CHOICE {
product-based NULL,
basic NULL
}
}
}
Figure 3.13 ASN.1 Data Type Definition: Example 1

## Slide 17
Data Type: Example 1
• Module name starts with capital letters
• Data types:
• Primitives: NULL, GraphicString
• Constructs
• Alternatives : CHOICE
• List maker: SET, SEQUENCE
• Repetition: SET OF, SEQUENCE OF:
• Difference between SET and SEQUENCE
SET
  – No order required
  – Order not important
  – Data types should all be distinct
SEQUENCE
  – The order in the list is maintained
SEQUENCE OF SEQUENCE makes tables of rows

## Slide 18
Data Type: Example 2
Trade-message ::= SEQUENCE {
invoice-no INTEGER
name
details
GraphicStrig,
SEQUENCE OF
SEQUENCE {
part-no INTEGER
quantity INTEGER
},
charge REAL,
authenticator Security-Type
}
Security-Type ::= SET {
…
--SEQUENCE OF SEQUENCE makes table
Figure 3.14 ASN.1 Data Type Definition: Example 2
}

## Slide 19
ASN.1 Symbols
Symbol Meaning
::=
|
-
Defined as
or, alternative, options of a list
Signed number
--
{}
[]
()
..
Following the symbol are comments
Start and end of a list
Start and end of a tag
Start and end of subtype
Range

## Slide 20
Keyword Examples
• CHOICE
• SET
• SEQUENCE
• OF
• NULL
• Keywords are in all UPPERCASE letters

## Slide 21
ASN.1 Data Type Conventions
Example

## Slide 22
Structure
• Simple
• PageNumber ::= INTEGER
• ChapterNumber ::= INTEGER
• Structure / Construct
• BookPageNumber ::= SEQUENCE {ChapterNumber, Separator, PageNumber}
• Tagged
• Derived from another type; given a new ID
• Other types:
• CHOICE, ANY

## Slide 23
Structure
• BookPages ::= SEQUENCE OF {BookPageNumber}
or
• BookPages ::=
SEQUENCE OF {
SEQUENCE {ChapterNumber, Separator, PageNumber}
}
• Example: {1-1, 2-3, 3-39}

## Slide 24
Enumerated Integer
RainbowColors ::= ENUMERATED {
violet (0)
indigo (1)
blue
(2)
green (3)
yellow (4)
orange (5)
red (6)
}
• ENUMERATED is a special case of INTEGER
• Example: RainbowColors(5) is orange

## Slide 25
ASN.1 Module Example
IpNetMediaEntry ::=SEQUENCE{
ipNetToMediaIfIndex
INTEGER
ipNetToMediaPhysAddress PhysAddress
ipNetToMediaNetAddress IpAddress
ipNetToMediaType
INTEGER
}

## Slide 26
Object Name
itu
0
iso
1
iso-itu
2
org
3
dod
6
internet
1
private
4
enterprise
1
internet OBJECT IDENTIFIER ::=
{iso(1) org(3) dod(6) internet(1)}
IBM
2

## Slide 27
Basic Encoding Rules (BER)
50
ASN.1 syntax containing management info is encoded
using the BER (Basic Encoding Rules) → defined for the transfer syntax.
ASCII text data is converted to bit-oriented data.
TLV: Type, Length, and Value are components of the structure.
Length: of the Value field in number of octets.
Value: is encoded based on the data type.

## Slide 28
P/C bit:
0: primitive
1: construct
Type Length Value(TLV) Encoding

## Slide 29
Basic Encoding Rules (BER)
Tag Value Type
1
2
3
4
5
6
9
BOOLEAN
INTEGER
BIT STRING
OCTET STRING
NULL
OBJECT IDENTIFIER
REAL
51

## Slide 30
{weight, 259}
{lastname, “smith”}
lastname ::= OCTET STRING
weight ::= INTEGER
TLV Encoding Example
module of data type
declarations written
in ASN.1
instances of data type
specified in module
Basic Encoding Rules
(BER)
03
01
02
02
‘h’
‘t’
Value, 259
Length, 2 bytes
Type=2, integer
transmitted
byte
stream
Value, 5 octets (chars)
‘i’
‘m’
‘s’
05
04
Length, 5 bytes
Type=4, octet string
52