## Slide 1: Lec8: Tools and methods for controlling and managing Networks

## Slide 2: Tools and methods for controlling and managing Networks
There are different assistant software tools and methods that help in managing the network in different things such as:
Special management programs such as antivirus, network performance monitors.
Programs for controlling the network and producing reports, e.g. applications for receiving reports from routers and switches.
Programs for controlling connection units and preparing reports.
Programs for analyzing protocol and calculating average data traffic.
Statistical analysis programs.

## Slide 3: Remote Monitoring (Rmon)
Provides standard information that a network administrator can use on the management of a group of LANs from a central site to:
  Monitor
  Analyze
  troubleshoot
RMON specifically defines the information that any network monitoring system will be able to provide
Rmon One of the most famous MIB (Management information Base) database.

## Slide 4: Rmon
RMON collects nine kinds of information, including:
  packets sent
  bytes sent
  packets dropped
  statistics by host by conversations between two sets of addresses

## Slide 5: Rmon Functions:
Creating current and historical reports on average data traffic in different network devices that are connected to the main network management station.
Producing different event and alarm mechanisms that are used to inform the network administrator about any urgent changes in the network.
Filtering and capturing exchanged data packets by different protocols in the network for further analysis.

## Slide 6: Examples of Network Management Systems
manageWise
(SMS)
LANDesk

## Slide 7: manageWise
Features:
Creates network maps automatically allowing administrators to locate problems fast.
Prevents downtime by identifying potential problems early.
Produce reports in different format (*.html-*.txt) for analysis of network status.

## Slide 8: SMS (System Management Server)
Functions:
Creating Main database that contains all the details about hardware and software in the network.
Software distribution from a single computer to all the computers in the network (No more need to install software by CD on each PC separately).
The ability to troubleshoot problems.

## Slide 9: LANDesk
Functions:
Uses on-demand technology to load resources only when called.
Centralized log management for convenient planning and analysis.
Configure performance thresholds and send alerts and generate log file.

## Slide 10: Protocols Analyzer Software Tools
Tools that are used for reading exchanged data packets produced by a protocol.
There are different protocols analyzers suitable for different kind of communications.
Example:
  Wireshark

## Slide 11: Functions of Protocols Analyzer Software Tools
Capture transferred data packets from the network.
Uses special software to decode the captured data.
Filtering and sorting the received data to facilitate processing them.
Offers readable identifiers for the used protocols.
Viewing the collected packets directly after capturing them or later.
Generating data traffic on the network.

## Slide 12: Functions of Statistical Reports Generator Software Tool
Collects statistical data using report programs and use them as a daily evaluation for network operation.
Collect and format LAN network information before and after any failure or for any changes in the network.
Plan for future network requirements and costs.

## Slide 13: LAN Measurements Software
Measurements programs that is used specially for LAN is considered as a subsection programs from the general inventory programs.
It gives an important information about the network and suggest important applications on it .

## Slide 14: Functions of LAN Measurements Software
Determining the number of copies of software that should be bought to improve the performance of network management.
Improving security system in the network.
Collecting statistical data.
Gives an overview about the users, resources and times of using the resources.
Offers a huge support for load balancing and operational reports.

## Slide 15: Problem Solving Life Cycle
User
Help Desk
Problem
Solution
Network Technician
Network Engineer
If problem solved by help desk
If problem isn’t solved.
If problem solved by technician
If >30 minutes passed and problem isn’t solved
Problem
Problem
Solution
Solution
Problem is solved

## Slide 16: Help Desk
Help desk is considered as the first connection point for users when a problem occur
Help desk determines the problem and its relation to the network, or programs, or workstations.
A specialist person from the helpdesk starts asking questions to the user to determine the section responsible for solving the problem.

## Slide 17: Example of Questions asked by the Help Desk
Q1: When did the problem happen?
Q2: Did the problem occurred before or happened frequently?
Q3: Did the problem happened due to an action or a specific event?
Q4: Can you determine the problem exactly?
Q5: What is the extent of the problem?
Q 6. Is there any other problem?

## Slide 18: The Work Order
The work order contains all events related to the problem from the beginning to the end, such as follows:
  The specialists who have dealt with the problem.
  Problem definition.
  Location of the problem.
  Previous problems that happened at the same Location.
  The date where system stopped.
  The date of the last backup operation.
  Solution steps and the time required for the solution.

## Slide 19: Network Technician
  The specialist from the help desk direct the problem that he couldn’t solve to the network technician.
  The network technician job is determining the problem and restarting the user during 20-30 minutes.
  If more than 30 minutes passed and the problem is still not solved, the technician transfer the problem to the engineer.

## Slide 20: Network Engineer
The network engineer cooperates with network technician and the manufacturer and every one related to the problem to determine the problem precisely and solve it as soon as possible.

## Slide 21: Network Statistics
It is a detailed report that shows the status of the network system at a certain time. It contains:
  Location of all the failures.
  All the hanged failures.
  All the failures that is not solved yet.
  All kind of failures and their solutions.
  The optimal usage for the network
  Weakness points in the network and their locations.
  Future projects for network and its desired performance.

## Slide 22: Network Trouble Log
Network Trouble log covers failures that happens in the network system such as hardware, software, and configuration failures that could happen and last for days or weeks or sometimes months until they are solved.
Network trouble log could be viewed by the help desk staff to help them in solving the frequent problems quickly.