## Slide 1
AME 4950
Renewable Energy
Lecture 1
SOLAR RADIATION

## Slide 2
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 3
What is the Sun?
The sun is a gaseous body composed mostly of hydrogen and some helium.
The huge gravitational force causes intense pressure and temperature at the core.
These conditions initiate nuclear fusion reactions.
The sun fuses hydrogen into helium at its core and the resulting energy radiates outward.
Energy is convected to the photosphere

## Slide 4
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 5
Radiation from the Sun
The surface of the photosphere is at about 5777 K.
Once the energy reaches the surface of the photosphere, it escapes to space by radiation.
The sun is considered a blackbody.
It radiates diffusely (uniformly) in all directions.
All the energy leaving the sun’s surface will reach a sphere containing earth.

## Slide 6
Radiation from the Sun
The net radiation heat transfer between the sun’s surface (1) and the surface of the sphere containing earth (2) is given by:
F1→2 = 1
A1 = 4 p r12, where r1 is the radius of the sun (6.955x108 m)
T2 is negligible
The total rate of heat transfer leaving the sun’s surface and reaching Surface 2 is: 3.84 x 1026 W.
SUN
EARTH
1
2

## Slide 7
Solar Constant
The average distance between the sun and earth is 1.496 x 1011 m.
This distance is called an astronomical unit (AU).
The irradiance (Gsc) incident on Surface 2 (including earth) will be:
SUN
EARTH
1
2
1.496 x 1011 m
Gsc
The value of Gsc is 1367 W/m2.
This value is called the Solar Constant.

## Slide 8
Solar Radiation Spectrum
The solar radiation spectrum closely matches the spectrum of a blackbody (but only at the top of the atmosphere).
Once solar radiation penetrates the atmosphere, the spectrum is affected by the presence of gases.
For example, ozone (O3) greatly reduces ultraviolet radiation.

## Slide 9
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 10
Atmospheric Effects
The solar irradiance reaching the earth’s surface is affected by:
  Suspended particles (e.g. dust)
  Gases in the atmosphere
  Clouds
These substances can:
  Absorb solar radiation
  Reflect solar radiation
  Scatter solar radiation

## Slide 11
Atmospheric Effects
Solar radiation not affected by these substances reaches the earth’s surface as direct radiation.
Remaining radiation reaching the surface is diffuse radiation.
Total of direct and diffuse radiation is called global radiation.

## Slide 12
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 13
Solar Radiation Intensity
Solar irradiance (G) incident on the earth’s surface in the normal direction is focused on a small area.
If the same (G) is incident at a different angle, it will be spread over a larger area.
This means that the solar intensity in the normal direction is highest.
Solar intensity at high latitudes is lower.

## Slide 14
Solar Radiation Intensity
This also means that solar intensity is higher in the middle of the day (e.g. at noon) than in the early morning or late afternoon.

## Slide 15
Solar Radiation Intensity

## Slide 16
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 17
Air Mass
The amount of solar radiation interacting with the atmosphere depends on how much atmosphere it passes through.
When the sun is directly overhead (at zenith), the amount of atmosphere that the sun’s rays pass through is at a minimum.
As the sun approaches the horizon, the sun’s rays must pass through a greater amount of atmosphere.
This phenomenon is characterized by the air mass.

## Slide 18
Air Mass
The larger the air mass, the more solar radiation will be absorbed (or reflected) by the atmosphere
This reduces the quantity of solar irradiance reaching the earth’s surface.
The larger air mass also changes its wavelength composition
This is the reason for the change in the sun’s color in early morning and late afternoon.

## Slide 19
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 20
Seasonal Variation of Solar Radiation
The earth rotates around the sun in an elliptical orbit.
The plane formed by the earth’s rotation around the sun is called the ecliptic plane.
The earth’s axis is tilted by 23.5° to the ecliptic plane.
Because of this tilt, the lengths of day and night vary throughout the year.

## Slide 21
Seasonal Variation of Solar Radiation
The point at which the day is shortest in the northern hemisphere is called winter solstice.
The point at which the day is longest in the northern hemisphere is called summer solstice.
The two points at which day and night have equal lengths are called the spring equinox and fall equinox.

## Slide 22
Sun’s Declination
The equatorial plane is the surface cutting through the earth’s equator.
Solar declination is the angle between the equatorial plane and the rays of the sun.
The angle of solar declination changes continuously as Earth orbits the sun, ranging from –23.5° to +23.5° (positive when the northern hemisphere is tilted toward the sun).

## Slide 23
Summer Solstice
At summer solstice, the sun’s rays are perpendicular to the tropic of cancer.
Daytime is longest in the northern hemisphere.
Daytime is shortest in the southern hemisphere.

## Slide 24
Winter Solstice
At winter solstice, the sun’s rays are perpendicular to the tropic of capricorn.
Daytime is shortest in the northern hemisphere.
Daytime is longest in the southern hemisphere.

## Slide 25
Spring and Fall Equinoxes
At spring and fall equinoxes, the sun’s rays are perpendicular to the equator.
Day and night have equal lengths.

## Slide 26
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 27
Lines of Longitude
Lines of longitude start at the north pole and end at the south pole.
Lines of longitude are also called meridians.
There are 360 meridians, one for each degree.
The meridian passing through Greenwich is called the prime meridian, and it is given the value of 0°.
Riyadh is approximately 46° east of the prime meridian.

## Slide 28
Lines of Longitude
As the earth turns once around its axis, it passes through 360 meridians.
Moving from one meridian to the next takes 4 minutes.
15 degrees of longitude correspond to 1 hour.
Example: If the time in Greenwich is 10:00, the time in a city 30° east will be 12:00, and the time in a city 45° west will be 7:00.
What about the time in locations between?

## Slide 29
Standard Time
To simplify calculation of time and avoid an infinite number of times throughout the world, Standard Time was introduced
Clocks are usually set for the same reading throughout a zone covering approximately 15° of longitude

## Slide 30
Standard Time
The time at the center of the zone is called standard time
Zones are 15° apart

## Slide 31
Solar Time
Solar time is the time used in calculating the sun’s position.
Solar time does not coincide with standard time.
In solar time, 12:00 always represents the time when the sun is exactly halfway through the sky.
This time is called solar noon.
The time of Dhuhr Athan is solar noon.

## Slide 32
Solar Time
It is necessary to convert standard time to solar time by applying two corrections
  Constant correction for the difference in longitude between the observer’s meridian (longitude) and the meridian on which the local standard time is based
  Equation of time, which takes into account the changes in the earth’s rate of rotation

## Slide 33
Conversion from Standard Time to Solar Time
Local solar time at a given location is denoted by LST
Correction for
Longitude
Correction for
Rate of Earth Rotation
Where:
LL is the longitude at the given location
LS is the longitude at the standard meridian for the time zone
deg W means moving in the western hemisphere
  If a location is in the eastern hemisphere, (4) becomes (-4)
EOT is called the Equation of Time

## Slide 34
Equation of Time
Earth moves in an elliptical (not circular) orbit around the sun, moving faster near Perihilion than at Aphelion.
This affects solar time.
The correction used to account for this phenomenon is called Equation of Time (EOT)

## Slide 35
Equation of Time
EOT can be found from:
Where:
n is the day of the year

## Slide 36
Equation of Time
EOT for the 21st of each month:

## Slide 37
Time Calculation Examples
If the local standard time in Makkah is 9:45am on February 21st, calculate the solar time:
SOLUTION
LS is 45° east
LL for Makkah is 39.8° east
Correction for longitude: (39.8 – 45) x (-4) = 20.8 min
EOT = -13.9 min (from table or equation)
→ LST = 9:45 – (20.8 min) – 13.9 min ≈ 9:10
Correction for
Longitude
Correction for
Rate of Earth Rotation

## Slide 38
Time Calculation Examples
What is the time of Dhuhr Athan in Riyadh on February 21st?
SOLUTION
LS is 45° east, and LL for Riyadh is 46.7° east
Correction for longitude: (46.7 – 45) x (-4) = -6.8 min
EOT = -13.9 min (from table or equation)
LST at Dhuhr Athan is solar noon, which is always 12:00
→ 12:00 = Local Standard Time – (-6.8 min) – 13.9 min
→ Local Standard Time = 12:00 + 13.9 – 6.8 ≈ 12:07
Correction for
Longitude
Correction for
Rate of Earth Rotation

## Slide 39
Time Calculation Examples
If the local standard time in Atlanta, Georgia is 3:00pm on November 21st, calculate the solar time:
SOLUTION
LS is 75° west
LL for Atlanta is 84.4° west
Correction for longitude: (84.4 – 75) x (4) = 37.6 min
EOT = 13.8 min (from table or equation)
→ LST = 15:00 – (37.6 min) + 13.8 min ≈ 14:36
Correction for
Longitude
Correction for
Rate of Earth Rotation

## Slide 40
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 41
Solar Angles
The location of the sun is determined by:
  Location on earth
  Day of the year
  Time of the day
It is convenient to describe these three quantities by angles:
Location on earth is determined by latitude (l)
Day of the year is determined by declination angle (d)
Time of the day is determined through solar time by the hour angle (h)

## Slide 42
Declination Angle
The declination angle can be determined as follows:
Where:
n is the day of the year

## Slide 43
Hour Angle
The hour angle h is the angle between the projection of P on the equatorial plane and the projection on that plane of a line from the center of the sun to the center of earth.
15° of hour angle corresponds to one hour of time.

## Slide 44
Hour Angle
The hour angle is set to zero at local solar noon
The hour angle is considered negative in the morning and positive in the afternoon.
The maximum value of hour angle is at sunset
The minimum value of hour angle is at sunrise
The magnitude of hour angle at sunrise and sunset on a given day are identical.
The hour angle is calculated by:
h = (LST – 12:00) x 15°/hour

## Slide 45
Determining Sun’s Location in the Sky
The sun’s location in the sky can be determined from the following information:
  Latitute (l)
  Declination angle (d)
  Hour angle (h)
The most convenient way to describe the sun’s location in the sky is by using two angles:
Solar elevation (or altitude) angle (b )
Solar azimuth angle (f )

## Slide 46
Solar Elevation Angle
The solar elevation angle is the angle between the sun’s ray and the projection of that ray on a horizontal surface
At sunrise and sunset, the solar elevation angle is 0°.
It can be found from:
The daily maximum elevation angle occurs at noon (bnoon).
It is given by:

## Slide 47
Sun’s Zenith Angle
The sun’s zenith angle (b Z) is the angle between the sun’s rays and a perpendicular to the horizontal plane at point P.

## Slide 48
Solar Azimuth Angle
The solar azimuth angle (f ) is the angle in the horizontal plane measured, in the clockwise direction, between north and the projection of the sun’s rays on the horizontal plane.
The solar azimuth angle can be found from:

## Slide 49
Example
For Riyadh on February 21st, calculate sunset time (in standard time).
SOLUTION
At sunset, the elevation angle b = 0°
Latitude of Riyadh: l = 24.6°
Declination angle on February 21st: d = -10.8°
sin (0) = cos (24.6) x cos (h) x cos (-10.8) + sin (24.6) x sin (-10.8)
→ h = 85°
h = (LST – 12:00) x 15°/hour
→ LST = 17:40
Local Standard Time = 17:40 + (46.7 – 45)x(-4) + 13.9
→ Local Standard Time ≈ 17:47

## Slide 50
Example
For Riyadh on February 21st, calculate the azimuth angle at sunset
SOLUTION
The solar azimuth angle is given by:
At sunset, the elevation angle b = 0°
Latitude of Riyadh: l = 24.6°
Declination angle on February 21st: d = -10.8°
Hour angel (found from previous example): h = 85°
cos (f ) = sin (-10.8) x cos (24.6) – cos (-10.8) x sin (24.6) x cos (85)
→ cos (f ) = -0.206 (second quadrant)
→ f = 101.9° OR 258.1°
The first solution represents sunrise, and the second represents sunset.
→ f = 258.1°

## Slide 51
Angles for Non-Horizontal Surfaces
The angle of incidence (q ) is the angle between the sun’s rays and the normal to the surface.
The tilt angle (a ) is the angle between the normal to the surface and the normal to the horizontal surface
a
y
f
b

## Slide 52
Angles for Non-Horizontal Surfaces
The surface solar azimuth angle (g ) is the angle measured in the horizontal plane between the projection of the sun’s rays on that plane and the projection of a normal to the surface
a
y
f
b

## Slide 53
Angles for Non-Horizontal Surfaces
The surface azimuth angle (y ) is the angle in the horizontal plane measured, in the clockwise direction, between north and the projection of the normal to the surface.
a
y
f
b

## Slide 54
Non-Horizontal Surface Angles Relations
a
y
f
b

## Slide 55
Special Case: Horizontal Surface
If the surface is horizontal, a = 0
  q = qZ (zenith angle)
  The angles: y and g are undefined.
a
y
f
b

## Slide 56
Summary of Solar Angle Relations
a
y
f
b
h = (LST – 12:00) x 15°/hour

## Slide 57
Summary of Surface Angle Relations
a
y
f
b

## Slide 58
Example
A flat plate solar collector is placed on a roof in the city of Dubai. The collector is tilted by 30° to the south. For May 21st at 14:00 (local standard time), calculate the angle of incidence (q ).

## Slide 59
Example
A flat plate solar collector is placed on a roof in the city of Dubai. The collector is tilted by 30° to the south. For May 21st at 14:00 (local standard time), calculate the angle of incidence (q ).
GIVEN
For Dubai:
  Latitude (l) = 25.2° North
  Longitude (LL) = 55.3° East
  Standard Meridian (LS) = 60°
For May 21st:
  EOT = 3.3 min
  d = 20°
Tilt Angle: a = 30°
The collector is facing south: surface azimuth angle y = 180°

## Slide 60
Sun Chart
The Sun Chart shows the changes in of the solar elevation and azimuth angles for representatives days of the year.
http://solardat.uoregon.edu/SunChartProgram.html

## Slide 61
Sun Path
A sun chart can be viewed in three-dimensions.
The result is usually referred to as the Sun Path.

## Slide 62
Experiment
The solar elevation and azimuth angles will be measured on March 2nd at 9:45am on the roof of the ME Department.
The elevation angle can be measured by measuring the length of the shade of an object.
L
Lshadow
b

## Slide 63
Experiment
The solar azimuth angle (f ) can be measured by a protractor
N
f

## Slide 64
Experiment
At 9:45am on March 2nd , the following can be shown:
LST = 9:45 – (46.7 – 45) x (-4) – 12.19
→ LST = 9:39.6 am (or 9.66)
h = (LST – 12:00) x 15°/hour
→ h = -35.1°
Latitude of Riyadh: l = 24.7°
Declination angle on February 21st: d = -7.21°
→ b = 43.2°
→ f = 128.5°

## Slide 65
Experiment
We will use a ruler that has a length L = 1.05 m long.
The length of the shadow should be Lshadow = 1.12 m.
L
Lshadow
b

## Slide 66
Experiment
The solar azimuth angle (f ) can be measured by a protractor
The protractor will measure the angle between north and the shadow. We’ll call this angle (K)
f = 180° - K
Since f is 128.5°, the protractor should measure an angle of 51.5° (or ~ 52°).
N
f

## Slide 67
Unit Outline
What is the sun?
Radiation from the sun
Factors affecting solar radiation
  Atmospheric effects
  Solar radiation intensity
  Air mass
  Seasonal variations
Calculating time
Solar angles
Solar irradiation on surfaces

## Slide 68
A surface can be irradiated by the following three sources:
  Direct irradiation (GD).
  Diffuse irradiation (Gdq).
  Irradiation reflected from the ground (GR).
The total irradiation on a surface is, therefore:
Gt = GD + Gdq + GR
To model the performance of a solar collector, it is necessary to have accurate information about each of the three components.
Solar Irradiation on Surfaces

## Slide 69
Direct irradiation on a surface of any orientation can be deduced from the direct irradiation on a surface normal to the sun’s rays.
The direct irradiation on a surface normal to the sun’s rays is usually called direct normal irradiance (DNI).
Direct normal irradiance is denoted by (GND).
Determination of Direct Irradiation (GD)
GND
GD
q

## Slide 70
The general relationship between GND and GD is:
GD = GND cos q
If the angle of incidence (q ) is larger than 90°, the surface is not receiving direct sunlight.
In this case, GD = 0.
Determination of Direct Irradiation (GD)
GND
GD
q
GND
GD=0
q

## Slide 71
Direct normal irradiance (GND) can either be measured or estimated
Measurements provide accurate, real-time data for a specific location.
  Requires a well-maintained measurement station.
Estimation of GND is more convenient, but it is not as accurate as actual measurements.
The most common method for measuring GND is by using a pyrheliometer.
The most common method to estimate GND is the ASHRAE Clear Sky Model.
Determination of Direct Normal Irradiance (GND)

## Slide 72
A pyrheliometer measures direct normal irradiance.
Sunlight enters the instrument through a window and is directed onto a sensor.
The sensor converts heat to an electrical signal.
The signal voltage is converted via a formula to measure watts per square meter.
To keep the sunlight normal to the window at all times, a solar tracking system is used.
Pyrheliometer

## Slide 73
This model estimates the direct normal irradiance (GND) on a clear day, i.e. no clouds, dust, or pollution.
ASHRAE Clear Sky Model
where,
A: apparent solar irradiation at air mass equal to zero (in W/m2)
B: atmospheric extinction coefficient
b : solar elevation (altitude) angle

## Slide 74
ASHRAE Clear Sky Model
A and B can be found from the table below on the 21st day of every month.

## Slide 75
ASHRAE Clear Sky Model
Actual direct normal irradiance (GND) may differ from the ASHRAE Clear Sky Model due to local atmospheric conditions.
For this reason, actual measurements are more reliable.
Al-Sanea, S. A., Zedan, M. F., & Al-Ajlan, S. A. (2004). Adjustment factors for the ASHRAE clear-sky model based on solar-radiation measurements in Riyadh. Applied energy, 79(2), 215-237.

## Slide 76
Diffuse irradiation (Gdq) on a surface of any orientation can be deduced from the diffuse irradiation on a horizontal surface (Gd).
Determination of Diffuse Irradiation (Gdq)
Gdq = Gd Fsur-sky
where, Fsur-sky is the view factor of the surface with respect to the sky.
Fsur-sky is given by:
where a is the tilt angle.

## Slide 77
Diffuse irradiation on a horizontal surface (Gd) can be either measured or estimated.
The most common method for measuring Gd is by using a pyranometer.
The most common method to estimate Gd is by applying a factor to GND from the ASHRAE Clear Sky Model.
Diffuse Irradiation on Horizontal Surface (Gd)

## Slide 78
A pyranometer measures total irradiance on a plane.
Its method of operation is similar to a pyrheliometer, but it does not track the sun.
Usually, a pyranometer is mounted horizontally.
It is also usually mounted high above the ground to avoid reflected irradiation.
Pyranometer

## Slide 79
For a pyranometer mounted horizontally and high above the ground:
Gt = GD + Gd + GR Gt = GND cos q + Gd
Pyranometer
0
Since the pyranometer is mounted horizontally, q is the same as the zenith angle (q Z).
Substituting and rearranging:
Gd = Gt – GND cos q Z
By using a pyrheliometer to obtain GND and a pyranometer to obtain Gt, Gd can be found.

## Slide 80
Diffuse irradiation on a horizontal surface (Gd) can be estimated using the ASHRAE Clear Sky Model.
Gd = C GND
where C can be found from the table below.
Gd from ASHRAE Clear Sky Model

## Slide 81
The amount of irradiation a surface receives due to reflection from the ground (GR) is given by:
GR = GtH rg Fsur-g
where,
  GtH : total irradiation the ground receives from the sun.
  rg : reflectance of the ground.
  Fsur-g : view factor of the surface with respect to the ground.
Fsur-g can be found from:
Determination of Reflected Irradiation (GR)

## Slide 82
Example
A flat plate solar collector is placed on a roof in the city of Dubai. The collector is tilted by 30° to the south. For May 21st at 14:00 (local standard time), calculate the total irradiation on this collector. Assume the ground reflectivity to be 0.6.

## Slide 83
Example
A flat plate solar collector is placed on a roof in the city of Dubai. The collector is tilted by 30° to the south. For May 21st at 14:00 (local standard time), calculate the total irradiation on this collector. Assume the ground reflectivity to be 0.6.
GIVEN
For Dubai:
  Latitude (l) = 25.2° North
  Longitude (LL) = 55.3° East
  Standard Meridian (LS) = 60°
For May 21st:
  EOT = 3.3 min
  d = 20°
Tilt Angle: a = 30°
The collector is facing south: surface azimuth angle y = 180°
Ground reflectivity: r = 0.6

## Slide 84
Gt = GD + Gdq + GR
GD = GND cos q
ASHRAE Clear Sky Model:
Gdq = Gd Fsur-sky
GR = GtH rg Fsur-g
Gd = C GND

## Slide 85
The station is located on the roof of the ME Department.
It has been collecting data every minutes for more than a year.
Solar Radiation Measurement Station at KSU

## Slide 86
Solar Radiation Measurement Stations in KSA
https://rratlas.kacare.gov.sa/RRMMPublicPortal/
OLD DATA
NEW DATA
http://rredc.nrel.gov/solar/new_data/Saudi_Arabia/