## Slide 2
MATH 1111

## Slide 3: Reference:

## Slide 4
Office Number and Location: Building 26 , A (9)

## Slide 5
Mid 1
Mid 2

## Slide 6: Test dates
First Midterm 7th week
Second Midterm 14th week

## Slide 7: Methods of Assessment:
Mark | Course Assessment
30 | Midterm exams
5 | Class activates
5 | Presentations
10 | Homework
10 | Quizzes ( Lms* )
40 | Final Examination
100 | Total
* http://lms.ksu.edu.sa.

## Slide 9: Introduction To Number Systems
Second Section:
Octal Number System
First Section:
Binary System
Third Section:
Hexadecimal System

## Slide 10: Binary System

## Slide 11
The main purpose for this lesson is to introduce the following:
Understand the concept of binary system.
Conversion any number decimal to the binary number and converse.
define how can conversion Binary Fractions.
Use Arithmetic in the Binary System.

## Slide 12: Binary System
The binary system is a different number system.
The coefficients of the binary numbers system have only two possible values: 0 or 1.
Each coefficient d is multiplied by 2n.
For example, the decimal equivalent of the binary number 11010.11 is 26.75, as shown from the multiplication of the coefficients by powers of 2:
1x24 + 1x23 + 0x22 + 1x21 + 0x20 + 1x2-1 + 1x2-2 = 26.75
the digits in a binary number are called bits.

## Slide 13: Binary to Decimal Conversion
A binary number can be converted to decimal by forming the sum of powers of 2 of those coefficients whose value is 1.
Example 2
Convert the binary number (1101001)2 to decimal.
Solution:
(1101001)2 =1x26 + 1x25 + 0x24 + 1x23 + 0x22 + 0x21 + 1x20
= 64 + 32+ 0 + 8 + 0 + 0 + 1
=105

## Slide 14: Binary Fractions
decimal number system, each digit of a number represents an increasing power of ten. This is true for all digits to the left of the decimal point ... for numbers to the right; each digit represents a decreasing power of ten.
In binary, the concept is the same, except that digits to the right of the "binary point" represent a decreasing power of two.

## Slide 15
Example3:
Convert the (110.001)2 to decimal.
Solution:
(110.001)2 = 1x22 + 1x21 + 0x20 + 0x2-1 +0x2-2 +1x2-3
= 4+2+0+0+0+0.125
= 6.125
Example 4
Convert (0.11101)2 to decimal.
Solution:
(0.11101)2 = 1x2-1 + 1x2-2 + 1x2-3 + 0x2-4 + 1x2-5
= 0.5 + 0.25 + 0.125 + 0 + 0.03125
= 0.90625

## Slide 16: Decimal to Binary Conversion
Algorithm 1
To convert from a base-10 integer numeral to its base-2 (binary) equivalent,
the number is divided by two, and the remainder is the least-significant bit.
The (integer) result is again divided by two, its remainder is the next least significant bit.
This process repeats until the quotient becomes zero.

## Slide 17: Decimal to Binary Conversion
Example 5
Convert 2310 to binary number.
Solution:
The answer is found by reading "up" from the bottom. Therefore, 2310 = 1 01112
 |  | Quotient |  | Remainder
1. | 23 ÷ 2 = | 11 |  | 1
2. | 11 ÷ 2 = | 5 |  | 1
3. | 5 ÷ 2 = | 2 |  | 1
4. | 2 ÷ 2 = | 1 |  | 0
5. | 1 ÷ 2 = | 0 |  | 1
 | sign bit |  |  | 

## Slide 18: Decimal to Binary Conversion
Example 6:
Convert 46 10 to base 2.
Solution:
Therefore, 4610 = 10 11102
 |  | Quotient |  | Remainder
1. | 46 ÷ 2 = | 23 |  | 0
2. | 23 ÷ 2 = | 11 |  | 1
3. | 11 ÷ 2 = | 5 |  | 1
4. | 5 ÷ 2 = | 2 |  | 1
5. | 2 ÷ 2 = | 1 |  | 0
6. | 1 ÷ 2 = | 0 |  | 1
 | sign bit |  |  | 

## Slide 19: Decimal Fractions to Binary Fractions Conversions
To convert the fractional part successive multiplications are done instead of divisions. In each case the remaining fractional part is used in the succeeding multiplication

## Slide 20: Decimal Fractions to Binary Fractions Conversions
Example 7
Convert the decimal fraction 0.5937510 to binary fraction.
Solution:
To convert the fractional part (0.59375)10, successive multiplications are done instead of divisions. In each case the remaining fractional part is used in the succeeding multiplication
Therefore 0.5937510 = 0.100112
 |  | Integer |  | Fraction
1. | 0.59375 x 2 = | 1 |  | 0.1875
2. | 0.1875 x 2 = | 0 |  | 0.375
3. | 0.375 x 2 = | 0 |  | 0.75
4. | 0.75 x 2 = | 1 |  | 0.5
5. | 0.5 x 2 = | 1 |  | .0

## Slide 21: Decimal to Binary Conversion
Example 8
Convert 46.5937510 to base 2.
Solution:
First, convert the whole number (46) using the previous method.
4610 = 10 11102
Next, convert the fractional part (0.59375), also use the previous method.
0.5937510 = 0.100112
Therefore, 46.5937510 = 10 1110.10011 2

## Slide 22: Arithmetic in the Binary System

## Slide 23: Binary Addition
The process for adding binary numbers is the same in any number system, except that you must be aware of when (and what) to “carry”.
In the decimal system, a carry occurs when the sum of 2 digits is 10 or more. For example,
In binary, a carry occurs when the sum of 2 binary digits is 2 or more. This leaves only four possibilities:
0 + 0 = 02 0 + 1 = 12 1 + 1 = 102 (therefore, 0 with a carry) 1 + 1 + 1 = 112 (therefore, 1 with a carry)

## Slide 24: Binary Addition
+ | 0 | 1
0 | 0 | 1
1 | 1 | 10
Addition table
Example9:
Add the binary numbers
0011 00102 + 0011 01112:
Solution:

## Slide 25: Binary Addition
Example10:
Add the binary numbers
1011.012+11.0112
Solution:
+ | 0 | 1
0 | 0 | 1
1 | 1 | 10
Addition table

## Slide 26: Binary Subtraction
For binary subtraction, there are four facts instead of one hundred:

## Slide 27: Binary Subtraction
Example 11:
Subtract: 10101.101_1011.11
Solution:
  Step 1: 1 – 0 = 1.
  Step2: Borrow to make 10 – 1 = 1.
  Step3: Borrow to make 10 – 1 = 1.
Step 4: Cascaded borrow to make 10 – 1 = 1.
  Step 5: 1 – 1 = 0.
  Step 6: 0 – 0 = 0.
  Step7: Borrow to make 10 – 1 = 1.

## Slide 28
Checking the Answer
You can check the answer in a few ways. One way is to add the result (1001.111) to the subtrahend (1011.11), and check that that answer matches the minuend (10101.101):

## Slide 29: Binary Multiplication Binary multiplication uses the same algorithm as in decimal, but uses just three order-independent facts:
0 x 0 = 0,
1 x 0 = 0,
1 x 1 = 1
Example 12:
Multiply 1011.01 x 110.1

## Slide 31: Homework
All Exercises Page 10